COMPUTER PROGRAMS FOR LOCATING THE MOON 

                    EIMAC DIVISION OF VARIAN 
                       301 INDUSTRIAL WAY 
                     SAN CARLOS, CALIFORNIA 

     In  two  previous  issues  of the Eimac EME notes, methods
were described for determining antenna aiming data to "hit" the
moon.  In bulletin AS-49, there was a reprint of an article  by
Don Lund, WA0IQN, an article by Victor Michael, W3SDZ, and some
letters  to  the  technical  editor  of QST from Alan Goodacre,
VE3BZS, all  discussing  antenna  aiming.   Also,  in  bulletin
AS-49-1   more   information  on  aiming  data  was  presented.
Bulletin AS-49-1 stressed the use of the Nautical  Almanac  and
the  Hydrographic Office publication HO-214.  It is possible to
determine  the  moon's  position  by   means   of   those   two
publications  without  extensive  mathematics.  However, as one
becomes more involved in the EME project,  the  habits  of  the
moon  become  interesting.  Also, more sophisticated methods of
tracking the moon become attractive.

     For those persons having  access  to  handheld  scientific
calculators,   new  techniques  become  available.   For  those
Amateurs having access to a computer, either punch-card  or  an
active  terminal,  another  interesting  hobby  of  writing and
modifying programs develops.

     In  this  issue  of  the  EME  notes,  four  programs  are
presented  which  may be of interest.  One is in BASIC, two are
in TYMSHARE SUPERBASIC and one in TYMSHARE SUPERFORTRAN.  As is
usually the case, these  programs  will  probably  need  to  be
modified  to  run  on  the  machine available to the individual
amateur.

                    PROGRAM 1 [MOONLOC1.BAS] 
                        LANGUAGE: BASIC 

     This program will run on  almost  all  machines  accepting
BASIC.  The operator must put in data from the Nautical Almanac
for  the  year,  month,  day  and  hours that the elevation and
azimuth is desired.  Also, the latitude and  longitude  of  the
geographic  location in question must be entered.  Statement 20
allows the operator to put in the time  interval,  in  minutes,
between each calculation.

     The origin of this program is not known.

                    PROGRAM 2 [MOONLOC2.BAS] 
                 LANGUAGE: TYMSHARE SUPERBASIC 

     The  program  is  a  modified  version  of program 1.  The
output format is slightly different.  Also, limits can  be  put
on   the   azimuth  and  elevation  angles  at  the  operator's
discretion.  The program requires latitude  and  longitude  and
time  interval  inputs.   Also,  Nautical  Almanac data for the
year,  month,  day  and  hours  must  be  put  into  the   data
statements.   Statement 610 allows the operator to put the data
in  for  identification.   The  computer  does  not  use   this
statement in the calculations.  The computer will pause and let
you  type  in  the  date.   When inserting the date, do not use
commas for seperating the month, day, and year.  If you do, the
computer will become confused.  When  the  carriage  return  is
depressed the computer will carry on.

                    PROGRAM 3 [MOONLOC3.BAS] 
                 LANGUAGE: TYMSHARE SUPERBASIC 

     This  program  was  originally  written  in BASIC by Lance
Collister, WA3GPL.  However, the  BASIC  used  on  the  General
Electric  terminal was sufficiently different from the TYMSHARE
SUPERBASIC that the program would not run.  A few modifications
were made to allow  the  TYMSHARE  machine  to  run.   What  is
presented  here will not run on the GE computer.  Perhaps those
who attempt to use this  program  will  have  to  make  further
changes for their individual cases.

     The  program  is  very  useful  because no almanac data is
required.  The program  allows  the  calculation  of  the  moon
position  by  comparing back to the position of the moon at the
start of the Julian calendar.  The operator need  put  in  only
the  latitude,  longitude,  time interval, month, day, year and
hours between which aiming data is  required.   If  rising,  or
setting,   moon   calculations   are   required,  the  computer
determines the time and will execute the printout requested.

                    PROGRAM 4 [MOONLOC4.FOR] 
                LANGUAGE: TYMSHARE SUPERFORTRAN 

     This program was supplied by Louis  Anciaux,  WB6NMT.   As
received,  the  program  was on tape and written in FORTRAN IV.
Again,  the  program  was  modified  to   run   with   TYMSHARE
SUPERFORTRAN.   This  program  requires  nautical almanac data.
However the GHA and declination for 0000, 0600, 1200, 1800, and
2400 hours GMT is all  that  is  required.   The  program  will
interpolate  for  all  othe  times.   Of  course, the latitude,
longitude, and time interval for the calculation must be  typed
in.

                    PROGRAM 5 [MOONLOC5.BAS] 
                  LANGUAGE: MITS ALTAIR BASIC 

     This  program  is  a version of Lance Collister's (WB7CCI)
original moon tracking  program  written  in  GE  BASIC.   This
particular  version  was modified by Jay Liebmann, K5JL, to run
on a MITS Altair 8800B.  The program requires about 6700  Bytes
of memory.