AUTOLOAD.DOC   by  Willis E. Howard, III

The program AUTOLOAD.COM implements the CP/M function
which allows a program to be automatically loaded
and run, following the cold boot.  The mechanics of
this are described by Kelly Smith in Microsystems,
Vol. 3 (1982), #1, page 88.

At first, the program will prompt for the disk to
be modified.  Type in the disk designation (e.g. A
or B in caps) corresponding to a valid disk on your
system.  Follow the single letter with a carriage
return.

The program then prompts for the command line.  At
this point, type in a single command line followed
by a carriage return, as you would for CP/M.  This
command line ( e.g. STAT *.* ) will be stored on
the system tracks of your designated disk and
executed every time you have a cold boot.

This is especially useful if you want to load a
software driver or other special program each time
the system is cold booted.  Note that the command
line can also consist of a submit command which will
allow a wide range of actions to be performed on
cold boot.

In general, your CBIOS should contain the commands

	XRA	A
	STA	CCP+7

in the warm boot section.  CCP is the starting address
of the CCP in your system.  This command will prevent
the autoload command line from being executed on warm 
boot.

This program defaults to the start of the CCP on 
track 0 and sector 2.  This default may be changed at
run time by responding to the request for which disk
'DISK A OR B ?' with an asterisk '*' following the
disk letter , e.g. with A* to select disk A and to
change the default track and sector numbers.  You will
be prompted for input.  This is a dangerous command
since it writes on your disk exactly where you tell
it to, so be sure to get the track and sector numbers
right!  No provision has been made for the begin of
the CCP at any position other than the beginning
of the designated sector.

There is only one error message 'ERROR' with an immediate
return to CP/M.  This can come from incorrect numerical
input or a bad disk select, read or write.

WEH,III   April,1982