COMPLEX MATH SUBROUTINES FOR CBASIC

		    by

	       E.R. LE CLEAR

	       10/12/1980

This file describes a method for  storing  and  using  CBASIC  "public
library"  subroutines  as  well  as  providing  listings  for specific
complex math routines. In order to illustrate the general use of these
subroutines, program LPFILTAN.BAS is provided which  can  be  used  to
predict  the  input  impedance and voltage transfer characteristics of
multiple low pass filters.  

       *****  THE PUBLIC LIBRARY  *****

Since CBASIC does not normally use line numbers,  the  numeric  lables
required  to  identify  program  transfer  statement  entry  can occur
anywhere in the program and in any order. This allows programs  to  be
written  and  reference  predefined  "line  numbers"   which    define
subprograms  that  can  be  appended  to  the  main  program  prior to
compilation. These subprograms are maintained on the disk as a library
of files that can be  concantenated to the main program. For instance,
suppose that main program file NETWORK.TMP has been written which uses
subroutines  REC/POL  and  POL/REC.  A  CBASIC  source  file  is  then
generated as follows:


PIP NETWORK.BAS=NETWORK.TMP,REC/POL.SRT,POL/REC.SRT


The program file NETWORK.BAS now includes all three files concatenated
to form a single program file which is ready to compile and run. Note:
all  of  the  library  subroutine  file  headings  are  of  the format
XXXXXX.SRT .  

       *****  COMPLEX MATH SUBROUTINES  *****

Basic cannot handle complex math expressions directly.  It is  usually
necessary  to  carry  the real and imaginary parts through the program
separately. For instance, in  order  to  add  two  complex  quantities
(A=B+C), the following program segments might be used:  

       BR=WWWW         REAL PART OF B
       BI=XXXX         IMAGINARY PART OF B
       CR=YYYY         REAL PART OF C
       CI=ZZZZ         IMAGINARY PART OF C
       AR=BR+CR        REAL PART OF A


                                   1








       AI=BI+CI        IMAGINARY PART OF A

       IE. (AR+JAI)=(BR+JBI)+(CR+JCI)

ADDITION and subtraction are straightforward and are  usually  simpler
TO  do in line as they are required.  Complex multiplication, division
and other functions become quite  tedious  to  handle  and  are  prime
candidates for subroutine implementation.


File DISK.DOC is  the  documentation  file  for  the  author's  CBASIC
complex  math  disk. This File is used to provide documentation of the
disk programs. Removing documentation from individual subroutine files
and accumulating them in a separate documentation file  minimizes  the
length  of  the  final  source  file while a printout provides a handy
reference while writing new programs.  A  brief  description  of  each
subroutine  is  provided including the "line number" of the subroutine
and a definition of the input and output variable formats.


When a subroutine is used, the appropriate variables must  be  renamed
to  that of the input variable required by the subroutine. In the same
manner, output variables must be renamed if the data is  to  be  saved
for  future use.  Many times, the current output variable can be used 
immediately by the next subroutine without renaming the variables.


The most commonly used subroutines will be 100.00 through 104.100.  It
is  almost  impossible  to  do  even  the simplest ac circuit analysis
without using one of these.


Subroutines 105.100 and 106.100 will be useful  in  certain  microwave
engineering calculations while subroutines 107.100 through 111.100 are
used in advanced circuit analysis using matrix algebra.


Routines 107.100 through 110.100 provide  means  to  change  from  one
matrix type to another. These types are:  

       S       SCATTERING MATRIX
       X       TRANSMISSION MATRIX
       Z       IMPEDANCE MATRIX
       Y       ADMITTANCE MATRIX

A brief discussion on the relationships between the different matrices
is provided in appendix A.




				   2








Subroutine   111.100  provides  the  means  for  multiplying  matrices
(primarily x matrices). Matrices must be  multiplied  in  the  correct
direction or errors will result.

       *****  APPLICATION PROGRAM  *****

File LPFILTAN.BAS is a program for predicting the  characteristics  of
low pass filters with up to 10 sections of the following type:  

       ---<LA >---<RLA>---
       1		 1
  O--------<CA >---<RCA>--------O
       1
      <RB >
       1
      <LB >
       1
      <CB >
       1
   O-----------------------------O

The number of sections is limited by  the  first  DIM  statement.  The
value  can  be changed but 10 sections is more than adaquate to handle
any practical filter.


The program will first ask for the number of sections  (N),  generator
source  resistance  (RG)  and  load  (RL).   After entering these, the
program will request  values  for  each  component  in  each  section.
Entering a "-" response results in the following:  

    COMPONENT		   VALUE AUTOMATICALLY ENTERED
    ---------		   ---------------------------
    LA,CB		       1E+15
    ALL OTHERS		       1E-15

Any value other than "-" will be entered directly.

After entering all component data, the program will ask whether a hard
copy is desired. Any response other than "Y" will cause  the  printout
to be directed to the console.


The program will next ask for the minimum and maximum frequencies  and
the  number of frequency points to be calculated. These points will be
distributed in a  logrithmic manner so that data can be plotted  on  a
LIN-LOG graph with physically equal spacing.




				   3








After calculating and printing the  results  at  all  of  the  desired
frequencies,  the  program will ask if you want to run a new frequency
plot with the same part values (F), rerun the whole program  with  new
values and frequency parameters (P) or quit (Q).


The following dialog shows the evaluation of  a  six  section  eliptic
filter.  This  particular  filter  is  a low pass prototype. Prototype
filters are  normalized  to  RG=RL=1  and  a  cutoff  frequency  of  1
RADIAN/SEC (.1592 HERTZ).  


       Program run to evaluate pass band
A>CRUN2 B:LPFILTAN

CRUN VER 2.05
                       LOW PASS FILTERS
NUMBER OF SECTIONS ? 6
RG,RL ?  1,1
TYPE IN SECTION PARAMETERS. TYPE - IF ELEMENT NOT USED
FOR SHORTED SERIES ARM, SET RB=1E+15
FOR OPEN SHUNT ARM, SET RB=1E+15
LA,RLA FOR SECTION  1 ? 1.323,-
CA,RCA FOR SECTION  1 ? .0833,-
RB,LB,CB FOR SECTION  1 ? -,-,1.284
LA,RLA FOR SECTION  2 ? 1.011,-
CA,RCA FOR SECTION  2 ? .5563,-
RB,LB,CB FOR SECTION  2 ? -,-,1.807
LA,RLA FOR SECTION 3  ? .7551,-
CA,RCA FOR SECTION  3 ? 1.004,-
RB,LB,CB FOR SECTION  3 ?-,-,1.337
LA,RLA FOR SECTION  4 ? .8300,-
CA,RCA FOR SECTION  4 ? .8402,-
RB,LB,CB FOR SECTION  4 ? -,-,1.204
LA,RLA FOR SECTION  5 ? 1.088,-
CA,RCA FOR SECTION  5 ? .3188,-
RB,LB,CB FOR SECTION  5 ? -,-,1.516
LA,RLA FOR SECTION  6 ? 0,0
CA,RCA FOR SECTION  6 ?-,-
RB,LB,CB FOR SECTION  6 ? -,-,1.087
HARD COPY ? (Y OR N) Y

 LOW PASS FILTER ANALYSIS

FILTER CONSTANTS

RG= 1
RL= 1



				   4








LA 1  = 1.323  RLA 1  = 1E-15
CA 1  = 0.0833 RCA 1  = 1E-15  
RB 1  = 1E-15  LB 1  = 1E-15   CB 1  = 1.284

LA 2  = 1.011  RLA 2  = 1E-15
CA 2  = 0.5563 RCA 2  = 1E-15
RB 2  = 1E-15  LB 2  = 1E-15   CB 2  =1.807

LA 3  = 0.7751 RLA 3  = 1E-15
CA 3  = 1.004  RCA 3  = 1E-15
RB 3  = 1E-15  LB 3  = 1E-15   CB 3  = 1.337

LA 4  = 0.83   RLA 4  = 1E-15
CA 4  = 0.8402 RCA 4  = 1E-15
RB 4  =1E-15   LB 4  = 1E-15   CB 4  =1.204

LA 5  = 1.088  RLA 5  = 1E-15
CA 5  = 0.3188 RCA 5  = 1E-15
RB 5  = 1E-15  LB 5  =1E-15    CB 5  =1.516

LA 6  = 0      RLA 6  = 0
CA 6  = 1E-15  RCA 6  = 1E-15
RB 6  = 1E-15  LB 6  = 1E-15   CB 6  = 1.087

FMIN,FMAX ? .01592,.1592
NUMBER OF DATA POINTS ? 20
FREQ	      ALPHA(DB)     ANG(ALPHA)	      ZIN	    ANG(ZIN)
---------------------------------------------------------------------
1.592E-02      -0.09	       -37.70	   8.401E-01	   -13.09
1.797E-02      -0.11	       -42.50	   8.101E-01	   -13.39
2.029E-02      -0.13	       -47.91	   7.779E-01	   -13.26
2.290E-02      -0.15	       -54.00	   7.451E-01	   -12.53
2.585E-02      -0.16	       -60.86	   7.142E-01	   -11.03
2.918E-02      -0.18	       -68.63	   6.890E-01	   -8.58
3.294E-02      -0.18	       -77.44	   6.751E-01	   -5.16
3.718E-02      -0.16	       -87.51	   6.798E-01	   -1.00
4.198E-02      -0.13		80.92	   7.123E-01	   3.16
4.738E-02      -0.08		67.49	   7.809E-01	   5.93
5.349E-02      -0.03		51.78	   8.861E-01	   5.46
6.038E-02      -0.00		33.37	   9.996E-01	   0.03
6.816E-02      -0.03		11.87	   1.037E 00	   -9.91
7.694E-02      -0.12		-13.08	   9.289E-01	   -18.59
8.685E-02      -0.18	       -42.34	   7.677E-01	   -17.12
9.804E-02      -0.08	       -78.54	   7.693E-01	   -3.15
1.107E-01      -0.02		53.78	   1.101E 00	   -4.15
1.249E-01      -0.18		-9.02	   9.403E-01	   -22.22
1.410E-01      -0.08		73.88	   1.294E 00	   -4.34
1.592E-01      -0.22		26.99	   8.275E-01	   22.50



                                   5









       PROGRAM RUN TO EVALUATE STOP BAND

NEW FREQ PLOT(F), NEW PARAMETERS(P) OR QUIT(Q) F
FMIN,FMAX ? .1592,..3184
NUMBER OF DATA POINTS ? 20
FREQ	      ALPHA(DB)     ANG(ALPHA)	       ZIN	    ANG(ZIN)
----------------------------------------------------------------------
1.592E-01      -0.22		26.99	   8.275E-01	   22.50
1.651E-01      -20.72		83.71	   1.815E 01	   -87.78
1.712E-01      -41.30		51.20	   2.840E 00	   -90.00
1.776E-01      -63.29		33.29	   1.853E 00	   -90.00
1.842E-01      -91.06		20.83	   1.450E 00	   -90.00
1.911E-01      -108.44		11.27	   1.219E 00	   -90.00
1.982E-01      -89.51		3.52	   1.063E 00	   -90.00
2.055E-01      -93.28	       -2.99	   9.488E-01	   -90.00
2.132E-01      -110.71	       -8.60	   8.599E-01	   -90.00
2.211E-01      -92.85	       -13.52	   7.878E-01	   -90.00
2.293E-01      -89.74	       -17.90	   7.277E-01	   -90.00
2.378E-01      -89.63	       -21.84	   6.764E-01	   -90.00
2.466E-01      -91.43	       -25.41	   6.319E-01	   -90.00
2.558E-01      -95.44	       -28.68	   5.927E-01	   -90.00
2.653E-01      -104.97	       -31.69	   5.578E-01	   -90.00
2.752E-01      -105.49	       -34.47	   5.264E-01	   -90.00
2.854E-01      -96.52	       -37.05	   4.979E-01	   -90.00
2.960E-01      -92.90	       -39.45	   4.720E-01	   -90.00
3.070E-01      -90.97	       -41.71	   4.482E-01	   -90.00
3.184E-01      -89.93	       -43.82	   4.262E-01	   -90.00


NEW FREQ PLOT(F), NEW PARAMETERS(P) OR QUIT(Q) Q

A>




It should be pointed out that the program  utilizes  the  X  parameter
matrix  to calculate the overall filter characteristics rather than an
elaborate ladder network representation. This results in a simpler and
shorter program. In addition,the program can be  easily  modified  for
other  types  of filter sections without a major rewrite (ie. hi-pass,
bandpass and bandstop). In  order  to  simplify  programming,  a  unit
matrix  is  defined  prior to entering the matrix multiplication loop.
This allows a valid matrix product when passing through the  loop  the
first time.





				   6







Although this file is not intended as a tutorial on ac circuit theory,
it was  felt  that  some  exposure  was  required.  File  APPENDIX.DOC
presents the circuit interpretations of the Z,Y,S and X matrices.

















































				   7