Documentation of PCONE, program for the design of printed circuits.
  Extract from the program comments in PCONE -not a translation of the
  Dutch documentation file.

   ****  (c) G.J. te Meerman 1984  ****  VERSION 1-10-1984
   ****  Klooslaan 12 9712 XN Groningen, the Netherlands ****


  ACKNOWLEDGEMENTS

  The CP/M adaptation has been designed by J. Schouten. It concerns
  the files CPMFMT.FOR and SUPPORT.MAC The list device is directly
  addressed in these subroutines, through a BIOS call.

  The program to use the space above the limit of the program is
  designed by William R. Pearson. The source is included in
  SUPPORT.MAC

  ******************************************************************
   Public domain software. This software may be used in any form,
  but not published, sold or incorporated into commercial software
  and/or commercially distributed software without the written
  permission of the author.
  This software is made available to promote CAD programming by the
  amateur community.
  The author welcomes suggestions and improvements, and would like
  to receive floppy disks with examples of input for PC boards,
  preferably inclusive a schematic!
  The most recent version is available from the author at costprice.
  (20$ US or the exchange equivalent in travelers cheques)
  Formats: 8" SSSD, 5" Heath (hard sectored), Osborne SSDD,
  ******************************************************************

  This program is an aid for the design of printed circuit boards.
  A lay-out of IC's is drawn. Separate points can be defined as well.
  The primary scale is on a grid where the distance between two IC
  connections is two grid distances (2x .05")
  The line thickness is assumed to be such that one connection may run
  between two IC pens.
  The program has a standard auto-routing facility to find non-crossing
  connections between two points. There is of course no guarantee that
  such a solution can be found in one plane.
  To minimize the effort of the designer, all connections that cannot
  be found, are drawn as far as possible, ending in a square soldering
  pad. The remaining line can then be tried on the second plane. The
  drawing of an unfound line is carried out from two positions: from
  the point of departure and from the target point. The reason for this
  procedure is, that in this way all IC's are soldered on the backplane
  and that plating through can be achieved by soldering a wire to both
  sides of the PC board.
  The sequence of the input is very important in the use
  of the program. As a general rule short connections should be found
  first, and longer connections later.
  It is recommended to make two files of connections: the first file
  contains the connections proper ordered according to two principles
  short connections first and connections in the X direction first.
  The second file should contain the power supply connections and the
  decoupling lines. The program makes then a file with unfound
  connections that can be tried on the second plane.

  Program description.

  The basic data for the IC board lay-out are present in two
  datafiles. The first datafile consists of the basic positions
  of the IC's on the board their orientations and names and
  all the desired connections, using names and pinnumbers.
  All coordinates are gridcoordinates. A gridcoordinate is 1/20 inch.
  The grid is maximally 80*126 points large, giving a maximal size for
  the board of 10X16 square centimeters. (EUROCARD)

  The program is split up in a series of subroutines.
  The first set consists of several utility routines, to interface the
  subroutines with specific input and output media.
  The second set of subroutines defines and draws the IC pen positions.
  The third set of subroutines computes the actual routings, and gives
  information on the connections that are not found.

  Basic information on the algorithm used

 The basis of this program is a recursive algorithm. The problem of
 finding a connection between two points on a grid, is equivalent to
 the problem of finding a path through a maze. At each gridpoint
 there is the problem of returning, continuing or one of two turns
 of 90 degrees.
 The program minimizes first in the X or the Y direction, or it continues
 in the chosen direction, depending on the option chosen.
 All points passed are marked, making it.
 impossible to reach an already investigated point again from another path.
 If no more movement is possible, the path is followed back. At each point
 on the way back the algorithm checks if another continuation was possible.
 This limits any search to the inspection of maximally all grid points.
 This investigation involves about 10.000 points, which is in the reach of
 a microcomputer. To prevent too long searches the length of each path is
 restricted to 600 steps. If the path becomes longer, it is assumed that
 the connection cannot be found. Not more than 750 grid points are
 investigated.
 As a first try, a connection is searched that is optimal. As a second try
 the connection is searched, where non-optimality is allowed.
 By a bisection principle the optimality criterion is relaxed, such that
 the shortest connection is found. (generally, the principle does not
 always lead to the shortest route, due to some interference caused by
 previous steps)
 If this search does not lead to succes, the route to the nearest point
 in the direction of the second point is drawn. From the second point
 a route nearest to that intermediate point is drawn.

  Description of the options.

  1. Entering description data for pens and rows of pens. A filename is
  requested for the file containing the basic data of IC's and single
  rows of pens. End of file is detected automatically.
  The description of the IC's is threefold.
  first and second : coordinates of first pen, in grid coordinates.
  If the second coordinate is negative, the IC is turned -90 degrees.
  third: the number of pins. If the number of pins is negative, only
  one row is drawn.
  The data for each IC are entered on one line. The order of entry
  indicates the order for drawing.
  2. Entering connection data. All connection data resides on files. The
  filename is requested, the  program reads the connections in and
  searches the connections in the present plane. A filename to store the
  residuals of non found connections is requested also.
  Dataformat for connections:
  Connections are defined by: ICnumber1,pennumber1,ICnumber2,pennumber2
  If Icnumber? is negative, absolute gridcoordinates are assumed.

  FURTHER OPTIONS:

  3. Store the present plotfield and the datagrid
  4. Read the plotfield and the datagrid
  5. Plot the present plane
  6. Interchange the grid (IC connections and plane interconnections
     are stored there)
  7. Clear the grid and the plotfield
  8. Copy the grid in the alternate area
  9. Separate connections according to found and not found.
     (with the aim of changing the order where unfound connections
     are read in before found connections)
  10. Optimize connection order. Unfound connections are placed earlier
      in the order, until no improvement takes place or more than
      50 different orders have been tried.
  11. Change parameters. The maximum detour and the priority direction
      may be changed
  A typical session for users will run as indicated below:

  1. the basic positions of the pens are read in and plotted
  2. the plotfield is saved on a file
  3. the connections of the second plane are found (power lines)
  4. we change to the first plane by reading the saved file and
     interchanging the grid thereafter.
  5. the connections of the first plane are searched. If a connection
     cannot be found, the connection is drawn from two sides towards the
     nearest points that can be reached and where no corresponding grid
     point on the second plane is already occupied
  6. we change to the second plane: save the present plane on disk
     read in the other plane and interchange the grid
  7. the residual connections are tried on the second plane
  8. the plotfield is saved and we change to the first plane
  9. repeat steps 6-8 until all connections are found
  10. plot both plotfields


  USE OF THE OPTIMIZATION OPTION
  The optimization option assigns to each connection a number, indicating
  the order of this connection. If the connection cannot be found,
  it is put earlier in the order. The alternate grid is now used for
  storage of the IC pen information. No provisions are made for inter-
  connections between layers. A typical optimization sessions runs as
  as follows:
   1. Read in information about IC positions
   2. Choose the optimization option
   3. Write out the connections in the new order

  Use of the splitting option.
  The splitting option is used after reading in IC positions
  Two datasets are generated for found and unfound connections


             IMPORTANT NOTE !!!!!

        This program stores the plotfield only, and no grid. The
        plotfield output is therefore NOT compatible with version 1.3.1


   ***** Interface information for plotters *****

  The plotting routine assumed is a standard CALCOMP routine.
  call: CALL PLOT(X,Y,N) meaning: draw a straight line to x,y from the
  present position, if N=2 actual drawing, if N=3 movement only.
  Plotting routines assume an Epson MX-80 or FX-80 printer. Because the
  interface is handled with a standard plotroutine, it is easy to use this
  program with another plotter or a graphics unit.
  Some users will have to make a systemspecific PLOT routine. This applies
  also to the RESET routine used to initialize the plotter.

   HOW TO CONTRUCT PCONE FROM REL FILES?
   L80 PCONE,PCSUB,ZOEK,PLOMAT,SUPPORT,CPMFMT,SORT,PCONE/N/E


















mber of pins
     DGRID: dataarray for grid and for s