******* The Lucas-Lehmer test ****************

Author: Albert van der Horst
        Hobby Computer Club (Holland)

The original intention of the program was to put the 
Osborne  in  the race for finding the world  largest 
prime.  It  was initiated in a time that  the  world 
record  was a number of about 40000 bits (ca.  12000 
decimal  digits or 5Kbyte) The program  will  handle 
such  numbers, although not easily.  I had the  idea 
that  where  an  Osborne clearly could  not  beat  a 
monstruous Cray computer,  maybe a thousand Osbornes 
would.  Helas,  the  world  record is now  at  about 
120000 bits,  well beyond reach of any machine  that 
cannot address more than 64Kbyte. 

The algorithm used

The  easiest numbers to check for primeness are  the 
Mersenne numbers. They are of the form 2^n-1 . So in 
hexadecimal  notation  the 31st Mersenne number  is 
7FFF FFFF .
The way to check whether such a number is prime,  is 
as follows:
 1 Start with 4
 2 Square the number
 3 Take the remainder after division by the Mersenne 
     number
 4 Repeat with step 4 for a number of n-2 times.

If  the final result is zero the Mersenne number  is 
prime. A proof of this is to be found in 
Knuth  The art of programming part 2

The multiplication method

For the purpose of using a processor (Z80) without a 
build in multiplication a special algorithm is  used 
that  will multiply numbers of 100 decimal digits in 
a splitsecond (!) 
The idea is as follows:
Look at the following example
                                     
                                     
                     1111            
                    31421X           
                    ------           
                     1111            
                  1111...            
                    2222.            
                 3333....            
                   4444..            
                 ---------                    
                 34908731


What is done here is that first 1*1111 is calculated 
and added at all the places where it is needed. Then 
we need 2*1111, 3*1111 etc. but these can be 
obtained without multiplication from the previous 
auxiliary number etc. Of course in the program bytes 
take the place of the decimal digits. Advantage is 
taken from the fast byte search and the double 
register set of the Z80.

Time needed

A  calculation  of  the world record  of  1961  will 
merely  take  an overnight  calculation.  For  still 
longer  numbers  a save option is build in.  If  you 
type  'S' (capital!) the program is interrupted  and 
stores itself with a unique filename on drive A: You 
may  continue  the  program  at  a  later  time   by 
restarting the resulting PR00????.COM program.  This 
option  works on the Osborne.  It is not clear to me 
how generally applicable the technique used  is.  If 
it doesnot work you may save by typing
A>SAVE  40  PR000123.COM     (or whatever  name  you 
think of)

How to start
Start the program by typing LUCLEM
Then  you are asked for a number.  The program  will 
tell  you whether the corresponding Mersenne  number 
is prime.  It may take very long but if possible the 
program will take a shortcut and return immediately.
While  the  program is running you may interrupt  it 
with one of three upper case letters: Q,R or S

R will restart (ask you for an other number)
Q will return to CP/M
S will save the program as described earlier

During the calculation, the number of squaring steps 
still  to be done is presented on the  screen.  Also 
this  number  is used to make unique file  names  in 
case of saving.


Restrictions
The  program in its present form (version 1.0)  will 
need  at least 34Kbyte besides the CCP that  remains 
loaded.  (  the CCP takes 5.5Kbyte) If there is  not 
enough memory you could reassemble after diminishing 
LENMAX.  That  implies that the largest  number  the 
program can handle will become less than 8Kbyte.
Reassembling  can be done with a Z80 macro assembler 
or after some editing with a normal Z80 assembler.

For  a  calculation taking months  (as  this  might) 
cosmic  rays cannot be ignored.  They will result in 
random  memory  failures ( this is  the  reason  why 
important  computers  always  have parity  check  in 
their memories).  However these errors are  detected 
by an excess 255 check, and you will get the message
FATAL  ERROR.  In that case restart the program from 
your previous stop.  If the error persists,  it is a 
program error. Then please inform me.