1802 Cross-assembler  Rev. 2.1                          Page 1















                              1802 Cross-assembler


                                    Rev. 2.1


                    Copyright (c) 1980 William C. Colley, III



                           The Manual Such As It Is.



































        1802 Cross-assembler  Rev. 2.1                          Page 2


        Index


        1.1            Format of Cross-assembler Commands............. 3

             1.1.1     Command Strings................................ 3
             1.1.2     Options........................................ 3
             1.1.3     Examples....................................... 3

        1.2            Format of 1802 Cross-assembler Source Files.... 5

             1.2.1     Statements..................................... 5
             1.2.2     Symbols........................................ 6
             1.2.3     Numeric Constants.............................. 6
             1.2.4     Strings........................................ 7

        1.3            Expression Evaluation.......................... 8

        1.4            1802 Instructions.............................. 9

             1.4.1     No Argument Group.............................. 9
             1.4.2     Register Group................................. 9
             1.4.3     Immediate Group................................ 9
             1.4.4     Short Branch Group.............................10
             1.4.5     Long Branch Group..............................10
             1.4.6     Input/Output Group.............................10

        1.5            Pseudo-operations..............................11

             1.5.1     END............................................11
             1.5.2     EQU............................................11
             1.5.3     BYTE...........................................11
             1.5.4     TEXT...........................................11
             1.5.5     BLK............................................12
             1.5.6     WORD...........................................12
             1.5.7     Conditional Assembly...........................12
             1.5.8     ORG............................................13
             1.5.8     SET............................................13
             1.5.10    PAGE...........................................13
             1.5.11    LOAD...........................................14

        1.6            Error Messages.................................15

        1.7            Assembler Abort Conditions.....................17

        1.8            Compiling the Assembler........................19

        1.9            Final Comments.................................21











        1802 Cross-assembler  Rev. 2.1                          Page 3


        1.1       Format of Cross-assembler Commands

        1.1.1     Command Strings

                  To  run  the 1802 cross-assembler,  type the  following 
                  command line:

                  A>a18 filename options

                  filename: The   name  of  the  source  input  file   is 
                            filename.rca,    the    list   can   go    to 
                            filename.prn,  and  the  hex file can  go  to 
                            filename.hex.

                  options:   See next section.

                 
        1.1.2     Options

                  The  source file comes from the currently  logged  disk 
                  drive  unless  it is redirected by putting  the  string 
                  "sd" in the options field.  s specifies the source file 
                  and d is a device code from the following list:

                  a, b, c, d     Disk drives.
                  -              The currently logged in disk drive.

                  Lines  of input containing errors will always be output 
                  to the console device.  If the full listing is desired, 
                  it must be called for by putting the string "ld" in the 
                  options field.  l specifies list file and d is a device 
                  code as per the source file, or one of the following:

                  x              Console device.
                  y              List device.

                  The  hex file will not be output unless called  for  as 
                  per the list file.

                  Options  must be run together into a single string with 
                  no embedded blanks.


        1.1.3     Examples

                  A>a18 barf          source -- a:barf.rca
                                      list   -- none.
                                      hex    -- none.

                  A>a18 barf sblxha   source -- b:barf.rca
                                      list   -- con:
                                      hex    -- a:barf.hex







        1802 Cross-assembler  Rev. 2.1                          Page 4


                  A>a18 barf ly       source -- a:barf.rca
                                      list   -- lst:
                                      hex    -- none.

                  A>b:a18 barf sbh-   source -- b:barf.rca
                                      list   -- none.
                                      hex    -- a:barf.hex




















































        1802 Cross-assembler  Rev. 2.1                          Page 5


        1.2       Format of 1802 Cross-assembler Source Files

                  Lines of source input are terminated with CR/LF  pairs.  
                  Internally,  the  character before the LF is discarded, 
                  so if the CR is missing, the last character of the line 
                  will be eaten up.  The internal line buffer will hold a 
                  120  character line.   This may be changed by  altering 
                  the  "#define  LINLEN  120" statement  in  a18.gbl  and 
                  recompiling the cross-assembler.   Excess characters in 
                  the line are thrown out.

                  Lower  case  letters are converted to upper case in  as 
                  few places as possible.  They are:

                       1)  In opcodes,

                       2)  In checking for keywords such as NOT, and

                       3)  In command strings.

                  This  means that "not",  "NOT",  "Not",  etc.  are  all 
                  possible  spellings of the logical inversion  operator.  
                  This  also  means that "foo" and  "FOO"  are  different 
                  symbols.  Watch this if you start encountering U errors 
                  of symbols that you "know" you defined.


        1.2.1     Statements

                  Source files input to the 1802 Cross-assembler  consist 
                  of statements of the form:

                  [label] [opcode] [arguments] [;comments.]

                  Labels  are recognized by their beginning in column  1.  
                  If  it  doesn't  begin there,  it is assumed to  be  an 
                  opcode.    Labels  are  assigned  the  current  program 
                  counter  value  unless  the line's opcode is  "EQU"  or 
                  "SET".

                  Opcodes  may  be either 1802 instruction  mnemonics  or 
                  pseudo-ops.

                  The  arguments following the opcode will vary with  the 
                  opcode.  In the case of opcodes such as "NOP", they may 
                  be absent entirely.

                  Lines terminate with either a CR/LF pair or a semicolon 
                  that  is  not embedded in a  quoted  string.   Anything 
                  after a semicolon is ignored by the assembler, but will 
                  appear in the listing.  Note that a semicolon in column 
                  1 will make the entire line a comment.







        1802 Cross-assembler  Rev. 2.1                          Page 6


        1.2.2     Symbols

                  Symbols  may  be of any length,  but only the  first  8 
                  characters  are  significant.   This may be changed  by 
                  changing  the "#define SYMLEN 8" statement  in  a18.gbl 
                  and   recompiling  the  assembler.    Note  that   this 
                  increases  the storage required by the symbol table  as 
                  each  entry  in the symbol table is SYMLEN+2  bytes  in 
                  length.   The  following  characters  are  legal  in  a 
                  symbol:

                       A-Z  a-z  !  #  $  %  &  .  :  ?  @  [  \  ]
                                 ^  _  `  {  |  }  ~  0-9

                  Note  that symbols may not begin with 0-9 as this would 
                  make it impossible to tell numbers from symbols.

                  A  special  symbol $ is always equal to the address  of 
                  the first byte of code generated by a given line.


        1.2.3     Numeric Constants

                  The  default  base for numeric  constants  is  decimal.  
                  Putting a trailing H,  D,  Q,  O,  or B onto the number 
                  will  override the default base.   The base designators 
                  may  be  in  either  lower or upper  case  and  are  as 
                  follows:

                       H    Hexadecimal    (Note that for A-F, lower case 
                                            is converted to upper case.)
                       D    Decimal

                       O,Q  Octal          (Either O or Q will do.)

                       B    Binary

                  Numbers are 16-bit unsigned quantities.  Overflows from 
                  the upper byte are ignored with no error flagged.   For 
                  example:

                       0fedcbh        evaluates to edcb hex.
                       000111000b     evaluates to 39 hex.
                       035q           evaluates to 1d hex.
                       128            evaluates to 80 hex.
                       1feh           evaluates to 1fe hex.

                  Numbers are recognized by their first character of 0-9, 
                  so  make sure that hex numbers have a zero padded  onto 
                  the front if needed.

                  A character constant is a string composed of zero, one, 
                  or two ASCII characters,  delimited by either single or 
                  double  quotes (' or ").   Note that single quotes only 
                  balance single quotes,  and double quotes only  balance 




        1802 Cross-assembler  Rev. 2.1                          Page 7


                  double quotes.  Thus a character constant of 22 hex can 
                  be specified by '"'.  For example:

                       "ab"           evaluates to 6162 hex.
                       ""             evaluates to 0000 hex.
                       "'"            evaluates to 0027 hex.
                       'A'            evaluates to 0041 hex.

                  Note that in the two-character character constant,  the 
                  left-hand character will appear in the upper-order byte 
                  and  the right-hand character will appear in the lower-
                  order byte.


        1.2.4     Strings

                  Strings  are  formed  in  the  same  way  as  character 
                  constants  except that they may be of any length up  to 
                  and including 255 characters.  The first character will 
                  be placed in the lowest-order memory byte.  A line-feed 
                  character  may  not  be  embedded in  a  string  as  it 
                  terminates  the line and will yield a  quote  imbalance 
                  error.   Note  that  strings  are  only  valid  in  the 
                  arguement field of an "TEXT" pseudo-op.



































        1802 Cross-assembler  Rev. 2.1                          Page 8


        1.3       Expression Evaluation

                  The  following  operators are allowed  in  expressions.  
                  The operators are listed in order of precedence.

                       Unary Plus, Unary Minus

                       *, /, MOD, SHL, SHR

                       +, -

                       >, >=, <, <=, <>, =
                                 (These can also be written as
                                      GT, GE, LT, LE, NE, EQ.)

                       NOT       (1's complement)

                       AND       (Bitwise logical AND)

                       OR, XOR   (Bitwise logical OR and Exclusive OR)

                       HIGH, LOW

                  Parentheses are used to change the order of precedence.  
                  During  evaluation of an expression,  as soon as a  new 
                  operator  is encountered that has precedence less  than 
                  or   equal  to  the  last  operator  encountered,   all 
                  operations up to the new operator are performed.   That 
                  is,   subexpressions  involving  operators  of   higher 
                  precedence are computed first.

                  All operators except +,  -,  *,  /, =, <>, >=, <=, >, < 
                  must  be separated from their operands by at least  one 
                  space or tab.

                  The  "HIGH mumble" is equivalent to "mumble SHR 8"  and 
                  "LOW mumble" is equivalent to "mumble AND 0ffh".

                  The  relational  operators (=,  >,  etc.)  evaluate  to 
                  0ffffh if the relationship is true, 0 if it is false.

                  Expressions  are terminated by commas,  semicolons,  or 
                  CR/LF pairs.
















        1802 Cross-assembler  Rev. 2.1                          Page 9


        1.4       1802 Instructions

                  The  instructions of the 1802 microprocessor fall  into 
                  several catagories.   Most require an argument,  though 
                  some permit none.  Blanks may be used freely throughout 
                  the argument field (except within symbols or  operators 
                  such  as NOT) to enhance the readability of the  source 
                  code.  The basic syntax is as follows:

                  [label]   SEX       expression     ;comments.


        1.4.1     No Argument Group

                  This group contains the following opcodes:
                   
                       ADC       ADD       AND       DIS       IDL
                       IRX       LDX       LSDF      LSIE      LSKP
                       LSNF      LSNQ      LSNZ      LSQ       LSZ
                       MARK      NOP       OR        REQ       RET
                       RSHL      RSHR      SAV       SD        SDB
                       SEQ       SHL       SHLC      SHR       SHRC
                       SKP       SM        SMB       STXD      XOR

                  These opcodes permit no arguments.


        1.4.2     Register Group

                  This group contains the following opcodes:

                       DEC       GHI       GLO       INC       LDA
                       LDN       PHI       PLO       SEP       SEX
                       STR

                  This  group  requires one argument in the  range  0-15.  
                  The labels R0,  R1,  ...,  R9,  RA,  RB,  ...,  RF  are 
                  predefined by the assembler for specifying registers in 
                  these  instructions.   If the argument is out of range, 
                  a register (R) error is flagged.

                  Note that a LDN R0 instruction will draw a register (R) 
                  error as its opcode is used for the IDL instruction.


        1.4.3     Immediate Group

                  This group contains the following opcodes:

                       ADCI      ADDI      ANI       LDI       ORI
                       SDBI      SDI       SMBI      SMI       XRI

                  This group requires one argument between -128 and  255.  
                  If  the argument is out of range,  a value (V) error is 
                  flagged.




        1802 Cross-assembler  Rev. 2.1                          Page 10




        1.4.4     Short Branch Group

                  This group contains the following opcodes:

                       B1        B2        B3        B4        BDF
                       BGE       BL        BM        BN1       BN2
                       BN3       BN4       BNF       BNQ       BNZ
                       BPZ       BQ        BR        BZ        NBR

                  This  group requires one argument whose high-order byte 
                  is  the  same as the high-order byte of  $+1.   If  the 
                  high-order  bytes do not match,  a branch (B) error  is 
                  flagged.


        1.4.5     Long Branch Group

                  This group contains the following opcodes:

                       LBDF      LBNF      LBNQ      LBNZ      LBQ
                       LBR       LBZ       NLBR

                  This group requires one argument having any value.


        1.4.6     Input/Output Group

                  This group contains the following opcodes:

                       INP       OUT

                  This group requires one argument in the range 1-7.   If 
                  the  argument  is out of range,  a value (V)  error  is 
                  flagged.























        1802 Cross-assembler  Rev. 2.1                          Page 11


        1.5       Pseudo-operations

        1.5.1     END

                  When  this  statement  is  encountered,  the  assembler 
                  decides  that  the  end of the  source  file  has  been 
                  reached.    If  this  statement  is  missing  or  in  a 
                  conditional assembly block that is not being assembled, 
                  the  assembler will encounter end-of-file on the source 
                  file.   In this case,  the assembler will attach an END 
                  statement  and will flag a * error.   The syntax is  as 
                  follows:

                  [label]   END

                  If  any IF statement is not closed with an ENDI at this 
                  point, an if (I) error will be flagged.

                  This statement permits no arguments.


        1.5.2     EQU

                  This statement is used to assign a permenant value to a 
                  symbol.   This value may not be subsequently changed by 
                  a SET,  another EQU, or by writing the symbol in column 
                  1 as a label.  The syntax is as follows:

                  label     EQU       expression

                  A  phasing  (P)  error  will  result  if  any   forward 
                  references  are  encountered in the evaluation  of  the 
                  expression.


        1.5.3     BYTE

                  This statement is used to place bytes in memory.   Each 
                  byte  is defined by an expression.   Multiple bytes can 
                  be defined by expressions separated by commas.   If  an 
                  expression  evaluates to a quantity outside the range -
                  128 to 255,  a value (V) error is flagged.   The syntax 
                  is as follows:

                  [label]   BYTE      [expr1][,epxr2].....


        1.5.4     TEXT

                  This statement is used to place strings in memory.  Its 
                  arguments may only be strings.  Multiple strings may be 
                  placed  in  memory  if  the strings  are  separated  by 
                  commas.  The syntax is as follows:

                  [label]   TEXT      [string][,string].....




        1802 Cross-assembler  Rev. 2.1                          Page 12




        1.5.5     BLK

                  This statement is used to reserve a block of memory for 
                  working  storage,  etc.   It requires one argument that 
                  gives the number of bytes of storage to  reserve.   The 
                  syntax is as follows:

                  [label]   BLK       expression


        1.5.6     WORD

                  This statement is used to place words in memory.   Each 
                  word  is defined by an expression.   Multiple words may 
                  be defined by expressions separated by  commas.   Words 
                  are  placed in memory with their high-order byte in the 
                  low-order memory location and the low-order byte in the 
                  high-order memory location.  The syntax is as follows:

                  [label]   WORD      [expr1][,expr2].....


        1.5.7     Conditional Assembly

                  Blocks of code can be assembled or not assembled  based 
                  on  the value of some expression.   The basic syntax is 
                  as follows:

                            IF        expression

                       (lines of code)

                            ENDI

                  If the expression evaluates to 0,  the code will not be 
                  assembled.   The source lines will be transfered to the 
                  listing,  but no hex output will be generated.   It  is 
                  recommended  that a value of 0ffffh be used for a  true 
                  value  since it turns into a false value under  bitwise 
                  inversion.

                  In  addition,   the  ELSE  directive  is  supported  as 
                  follows:

                            IF        expression

                       (lines of code)

                            ELSE

                       (more lines of code)

                            ENDI




        1802 Cross-assembler  Rev. 2.1                          Page 13



                  This is equivalent to:

                            IF        expression

                       (lines of code)

                            ENDI
                            IF        NOT expression

                       (more lines of code)

                            ENDI

                  Note  that  labels  are not  permitted  on  conditional 
                  assembly directives.   Also note that an END  statement 
                  can  fail  to be recognized if it is in  a  conditional 
                  assembly block with a false expression.

                  A  phasing  (P) error will be flagged if there are  any 
                  forward references in the expression.


        1.5.8     ORG

                  This  statement  is  used  to load  a  value  into  the 
                  assembly program counter.   The value is obtained  from 
                  the  expression.   If  the expression contains  forward 
                  references, a phasing (P) error will result. If a label 
                  is present, it will be EQUed to the new program counter 
                  value.  The syntax is:

                  [label]   ORG       expression


        1.5.9     SET

                  This statement is used to assign a temporary value to a 
                  symbol.   The  symbol may not be redefined by an EQU or 
                  by  writing it in column 1 as a label,  but it  may  be 
                  redefined by another SET statement.   The value for the 
                  symbol is obtained from the expression.  If it contains 
                  forward  references,  a phasing (P) error will  result.  
                  The syntax is:

                  label     SET       expression


        1.5.10    PAGE

                  This  statement  is used to set  the  assembly  program 
                  counter to the beginning of the next 256-byte page.  If 
                  the  program  counter is already at the beginning of  a 
                  page,  the  statement  has no effect.   It  permits  no 
                  arguments, and it handles a label in the same way as an 




        1802 Cross-assembler  Rev. 2.1                          Page 14


                  ORG statement does.  The syntax is as follows:

                  [label]   PAGE


        1.5.11    LOAD

                  This statement is used to load a 16-bit immediate value 
                  into a register.   It is,  in effect, a built-in macro.  
                  The syntax is as follows:

                  [label]   LOAD      reg, data

                  The  following sequence of instructions is placed  into 
                  the code:

                  [label]   LDI       HIGH data
                            PHI       reg
                            LDI       LOW data
                            PLO       reg

                  Note  that  execution  of  this macro blows  up  the  D 
                  register.




































        1802 Cross-assembler  Rev. 2.1                          Page 15


        1.6       Error Messages

                  Error  messages  are flagged with a  single  letter  in 
                  column  1  of the offending line in the  listing.   The 
                  meaning of each letter follows.

                       B    Short  branch  was not to a location  on  the 
                            current page.   Note that the branch must  go 
                            to  the same page as $+1 is on.   Thus  short 
                            branch  instrucions  at location  0xxffh  act 
                            strangely.  Don't ask me, I didn't invent the 
                            instruction set!

                       D    Digit too large for the base was encountered.  
                            In particular,  watch for 8 or 9 in an  octal 
                            number and a-f in a decimal number.

                       E    Expression ill-formed.

                       I    If  stack imbalance.   Look for ELSE or  ENDI 
                            without  an IF or an IF still open at the end 
                            of the file.

                       L    Invalid  label.   Label may  contain  invalid 
                            characters  or  be equal to a  reserved  word 
                            like  A  or NOT.   Label may be present on  a 
                            conditional assembly directive.

                       M    Label multiply defined.   Label defined  more 
                            than  once  and all definitions are  not  SET 
                            statements.

                       O    Invalid   opcode.    Look  for  misspellings, 
                            missing semicolons, or opcodes in column 1.

                       P    Phasing error.   Look for expressions in ORG, 
                            EQU,  SET,  or  IF  directives  that  contain 
                            forward references.  If none exist, something 
                            wierd is going on as a label that was defined 
                            in pass 1 mysteriously vanished in pass 2.

                       R    Register  instruction  argument out of  range 
                            (0-15) or LDN R0 instruction.

                       S    Syntax error.   Check your syntax against  my 
                            samples.

                       T    Too  many  arguments  on  this  line.    WORD 
                            directives may only define 127  words,  while 
                            TEXT  and BYTE directives may only define 255 
                            bytes.    On   other  statements,   you   put 
                            superfluous arguments on the line.

                       U    Undefined    symbol    encountered     during 
                            expression evaluation.




        1802 Cross-assembler  Rev. 2.1                          Page 16



                       V    Value  out of bounds.   In  particular,  BYTE  
                            expressions  and 8-bit immediate values  must 
                            evaluate  to  -128  to 255,  while  I/O  port 
                            numbers must evaluate to 1 to 7.

                       *    This  statement generated by  the  assembler.  
                            Right  now,  this only happens if you drop an 
                            END   statement   or   remove   it    through 
                            conditional assembly.

                       "    Quote  imbalance error.   Bear in mind that ' 
                            will  not terminate a string started  with  " 
                            and vice-versa.

                       (    Parenthesis imbalance error.  Count them!











































        1802 Cross-assembler  Rev. 2.1                          Page 17


        1.7       Assembler Abort Conditions

                  Under  certain circumstances,  this assembler will just 
                  give up and quit in the middle of an assembly.   If you 
                  don't  get the error count diagnostic on  the  console, 
                  read  your  screen for sure!   The  following  messages 
                  occur:

                       1)   Can't open source.

                            The   source  file  does  not  exist  on  the 
                            specified disk drive.

                       2)   Can't open list.
                            Can't open hex.

                            No  directory entries left on the disk  drive 
                            in question.

                       3)   Illegal command line.

                            Bone up on command lines.

                       4)   No file info supplied.

                            Bone up on command lines.

                       5)   If stack overflow.

                            IF  directives  may only be nested  16  deep.  
                            Rebuild  your  source  code  to  reduce  your 
                            nesting depth, or change the "#define IFDEPTH 
                            16"  statement in a18.gbl and  recompile  the 
                            assembler.

                       6)   Disk read error.

                            Source  file  has  a bad CRC  or  some  other 
                            difficulty.

                       7)   Disk write error.

                            Out of disk or directory space on the list or 
                            hex file.

                       8)   Error closing file.

                            Problem  closing  list  or  hex  file.    You 
                            shouldn't get this one.

                       9)   Symbol Table Overflow.

                            Your source program defines too many symbols.  
                            The  current limit is 500.   If you have more 
                            memory than I do, you can change the "#define 




        1802 Cross-assembler  Rev. 2.1                          Page 18


                            SYMBOLS  500" line in a18.gbl  and  recompile 
                            the assembler.   Otherwise,  you must work on 
                            your source code.
























































        1802 Cross-assembler  Rev. 2.1                          Page 19


        1.8       Compiling the Assembler

                  To  compile the assembler as it stands,  you will  need 
                  the following items:

                       1)   40K of RAM.

                       2)   The BDS C Compiler (good box, Leor!!).

                       3)   Microsoft's     MACRO-80     Macro-assembler.          
                            (Note:  Only needed if you want to play  with          
                            the  functions  in a18tbls.mac as they  exist          
                            in  a  form digestible by CLINK in  the  file          
                            a18tbls.crl.)

                  To  get  a18tbls.crl  up  from  scratch,   you  do  the 
                  following.   I  assume  MACRO-80 lives on drive  B  and 
                  everything else on drive A.

                       A>b:m80 a:,=a18tbls/r

                  This should yield a file a18tbls.rel on drive A.

                       A>b:l80 /d:0/p:0,a18tbls,a18tbls.crl/n/e

                  At  this  point,  LINK-80 will ask if you want to  move 
                  anyway.  TELL IT NOT TO!!!!!

                  You  should  now have a18tbls.crl on  drive  A.   Erase 
                  a18tbls.rel.

                  Now you are ready to compile the rest of the beast.

                       A>cc1 a18.c
                       A>cc1 a18asmln.c
                       A>cc1 a18eval.c
                       A>cc1 a18get.c
                       A>cc1 a18put.c
                       A>cc1 a18symb.c

                  Now you can link it all together.

                       A>clink a18 -s

                       *a18asmln
                       *a18eval
                       *a18get
                       *a18put
                       *a18symb
                       *a18tbls

                  And, as if by magic, you've got a18.com!

                  Note that the linkage can all be done on one line,  but 
                  my paper isn't wide enough here to do it that way.




        1802 Cross-assembler  Rev. 2.1                          Page 20



                  Note  that if you have more than 40K of  RAM,  you  may 
                  want  to increase your symbol table size.   Symbols are 
                  10 bytes each, so plan accordingly.























































        1802 Cross-assembler  Rev. 2.1                          Page 21


        1.9       Final Comments
                  Happy  assembling!   If you have questions or note  any 
                  bugs,   I'd   appreciate  a  shout  at   (617)258-1204, 
                  (617)266-3179,  or on the Boston CBBS at (617)963-8310.  
                  The  questions will point up weaknesses in the  manual, 
                  and the bugs need to be stamped upon unmercifully.