EDIT - Super CP/M text editor

Introduction
EDIT  is an enhanced version of the standard CP/M text  editor,  ED.COM, 
with many additional features.  It is a character orientated editor, and 
unlike a screen editor, can be used with any normal I/O device, authough 
a  fast VDU will speed operation.  EDIT requires CP/M 2.0  or  later,and 
will  operate  in any sized system,  however,  a large system will  make 
editing long files easier and faster.

Invoking EDIT
EDIT is invoked via the CP/M console processor command:

          EDIT N:filename.ext (X)

where filename.ext is the name of the file to be edited and the optional 
disk drive specifier 'N:' is the disk to use and is in the range 'A:' to 
'P:'  (assuming  you  have  that many drives!).  If there  is  no  drive 
specifier, the current disk will be used.

If the filename.ext does not exist, a new file is created and 'New file' 
is printed.

If  the file exists,  then 'Loading...' is printed and the file is  read 
into memory (unless an 'X' was typed after the filename in CP/M). If all 
the file is read into memory, End of Input File is printed. When filling 
memory,  a  few  hundred  bytes  of  memory are  always  left  free  for 
insertions  (and for a command line buffer).  After the file is  loaded, 
the first 10 lines are echoed to the screen.

Command Mode
When EDIT is ready to accept a command,  it prints an asterisk.  So that 
Carraige  Return can be treated like a text character for  searches  and 
inserts,  the  'ESC'  key  is used to terminate all  commands.  The  ESC 
character is echoed as a dollar sign ($). A command consists of a single 
letter (in either upper or lower case) which may be preceded by a number 
which  is  an  integer in the range -65535 to  +65535.  To  specify  the 
largest  possible  valid  number,  a hash sign (#)  may  be  used.  Edit 
commands will default to 0 if no number is entered.

String commands require the string to be terminated with a ESC,  however 
non   string  commands  do  not require an  ESC  following  the  letter, 
authough a trailing ESC will be ignored by EDIT.  Any number of commands 
may be input on a single command line (which may be several lines on the 
terminal)  but they will only be executed when two consecutive ESC's are 
input. The command line length is only limited by the space remaining in 
the  system  after  the main file has been loaded.  If  the  input  line 
approaches  the limit of memory the bell will ring every time a  key  is 
pressed,  authough  the  character  will still  be  accepted.  About  20 
characters  later,  when  there  is no more room,  only  the  DELETE  or 
BACKSPACE key will be accepted.

The editor uses the concept of a cursor,  which, at any time, is between 
two  characters  of  text.  The cursor can be moved around the  text  in 
memory,  both  as direct commands and as the result of  other  commands. 
Most  operations  are  relative  to the  current  cursor  position.  For 
instance,  the T command prints out the line that the cursor is on, with 
a 'squiggle' (depending how your terminal interprets code 7E Hex) placed 
at the cursor position.

Editor Control Keys
At any time during EDIT operation (except during disk reads and  writes) 
execution  may  interrupted and control returned to the command mode  by 
pressing Control-C (Hex 3,  Ascii ETX).  Characters may be deleted using 
either the BACKSPACE OR DELETE keys,  Control-X will delete the  current 
line being entered and Control-R will re-type the current line.

The  text output from EDIT to the screen may be paused at any time  with 
Control-S.  After  it  has been paused,  the output may be restarted  by 
hitting any key.

Control-Z  is  used  with the C,S & N commands.  In a  search  string  a 
Control-Z is interpreted as matching any single character.

Carraige  Return  has  no particular significance to EDIT  except  as  a 
normal text character. Line-Feeds are supplied automatically following a 
Carraige Return, therefore the line feed key is disabled.
 
All  other control keys will be treated as text keys and will be  echoed 
as  an upper case letter preceded by a caret,  e.g.  Control-T  will  be 
echoed as '^T'.

Edit Commands
In the descriptions that follow:

+n       = Only positive numbers allowed (or sensible)
n        = Either positive or negative numbers alllowed
string   = Search string. Maximun of 32 characters
text     = Any characters except EDIT control characters
$        = An ESC must be used to terminate this string
(  )     = Optional parameter

+nA - Append text
The A command reads in 'n' lines of text from the disk.  If no number is 
specified, as much text as possible is read in, else the number of lines 
of  text  are read in.  The text is appended to the end of the  text  in 
memory.   If the end of the input file is reached,  End of Input File is 
printed.

+B - Beginning
The B command on its own (or with a positive number) moves the cursor to 
the beginning of file. The -B command moves the cursor to the end of the 
file. The number, if present, is ignored.

Cstring1$string2$ - Change text
The  C  command searches from the current cursor position for  a  string 
matching 'string1', and if found, replaces it with 'string2', and leaves 
the  cursor at the end of 'string2'.  If a match is not found,  an error 
message  is printed,  and EDIT returns to command mode.  A Control-Z  in 
'string1'  will match any single character in the main text.  If a  null 
string is input for 'string2' (e.g.  'Cstring1$$') ,  the effect will be 
to delete the next occurance of 'string1' in the text.

nD - Delete characters
The  delete command deletes 'n' characters either from (if positive)  or 
before (if negative) the current cursor position.  A zero number has  no 
effect.

E - End edit
Editing  is  terminated with the E command.  This causes  the  following 
sequence of events:

     Any scratch file created with the O command is deleted.
     Any backup file ('filename.BAK') present on disk is deleted.
     The original file is renamed to 'filename.BAK'.
     All text in memory is written to the work file 'filename.$$$'
     Any remaining text in the input file is written to disk.
     The work file is renamed to 'filename.ext'
     The  message Finished Editing 'filename.ext' is then  printed,  and 
     control returns to CP/M.

H - Halt
The halt command is mainly used in macro and iterative commands to pause 
operation  until any key is pressed.  If a Control-C is pressed while in 
Halt, command mode will be entered.

Itext$ - Insert text
The I command allows text to be inserted at the current cursor position. 
The text string may be any length (subject to the amount of memory left) 
and  may  include  Carraige Returns.  It may not  include  edit  control 
characters,  e.g. ^C,^R,^S,^X or ESC, as these characters are acted upon 
directly. 

nJ - Jump to line
The  J command moves the cursor to the start of line 'n',  counted  from 
the start of the file in memory.

+nK - Kill lines
The  K  command kills (deletes) 'n' lines of text from (if positive)  or 
before (if negative) the current cursor position.  '1K' will delete  all 
the characters up to, and including the next Carraige Return, and 'K' or 
'0K'  will  delete  all  characters from the start of the  line  to  the 
current cursor position.

+nL - move Lines
The L command moves the cursor 'n' lines from (if positive),  or  before 
(if negative) the current cursor position,  and leaves the cursor at the 
start  of  that line.  A special case is 0L (or just L) which moves  the 
cursor to the start of the line that it is on.

+nM - Move characters
The  M  command moves the cursor 'n' characters from  (if  positive)  or 
before (if negative) the current cursor position.

Nstring$ - Search memory and input file
The N command is the same as the S command, except that if the string is 
not  found  in memory,  then any of the input file remaining on disk  is 
searched as well.  If there is insufficient room for all the text to  be 
read in, the overflow is written out to the work file.

nO$ - Output to scratch file
The O command outputs 'n' lines of text from the current cursor position 
to a scratch file on disk.  This file is always deleted at the end of an 
EDIT  session,  but may be read in elsewhere using the R  command.  Note 
that  an ESC is required immediately after the O even though there is no 
filename given.
nO(N:)filename.ext$ - Output to disk file

This version of the O command creates a file filename.ext,  on  optional 
disk N: and writes 'n' lines of text from the current cursor position to 
the file. This file is not deleted at the end of an EDIT session and may 
be read back using the R command.

nP - Print page of text
The  P command is equivalent to 10L10T,  i.e.  the cursor moves down  10 
lines and then types out 10 lines. 

Q - Quit editing
The Q command will terminate EDIT, and leave the disk files as they were 
before  invoking  EDIT.  Thus all work done in the current edit  session 
will  be lost.  Because of this,  QUIT asks for confirmation.  If  N  is 
typed,  command  mode  will be re-entered without changes,  and if Y  is 
typed, control will return to CP/M.

R$ - Read scratch file
The  R command reads in text that has been saved using the O command  at 
the current cursor postion.  Note that the ESC is required after R, even 
though there is no filename given.  Note also that the cursor is left at 
the end of the text read in.

R(N:)filename.ext$ - Read disk file
The R command reads text in from filename.ext on optional disk N: at the 
current  cursor position.  If the file cannot be found File not found is 
printed, and command mode is entered. Note that the cursor is positioned 
at the end of the text read in.

Sstring$ - Search for string
The  S  command  searches  the text,  starting  at  the  current  cursor 
position,  for a match with 'string'. If a match is found, the cursor is 
moved to the end of 'string', otherwise an error is printed, and command 
mode  entered,  with the cursor position unchanged.  A Control-Z in  the 
string will match any single character.

+nT - Type lines of text
The  T command types 'n' lines of text from (if positive) or before  (if 
negative)  the  current cursor position.  A special case of  type  is  T 
without  any number or sign.  This prints out the current line with  the 
cursor  shown as a 'sqiggle'.  This is automatically executed at the end 
of  each command string unless an P,T,V or Z has been executed  in  that 
string. 

V - Verify file parameters
This command prints out the size of file, the amount of free memory, the 
line  of the file that the cursor is on,  and the name of the file being 
edited.

nW - Write lines to output file
The  W command writes 'n' lines from the start of the text in memory  to 
the output file.  If no number is entered, the entire file is written to 
disk.  All the text that is output to disk is then deleted, thus freeing 
the memory work space. 

-Xcommandstring$$ - Define macro
A macro command,  consisting of any editor commands (except X),  may  be 
defined using the -X command.   As escapes can be included in the macro, 
the define macro command must be terminated with 2 escapes.  Macro's are 
limited to 80 characters.

-2X - Print macro
This form of the macro command prints the currently stored macro.

nX - Use macro
The  X command executes the currently defined macro 'n' times as part of 
the  normal  command line.  If the macro is  undefined,  or  empty,  the 
command will be ignored. The macro facility is very useful for storing a 
command  string  that is used frequently during an  edit  session.  Note 
however,  that  a  macro must be re-defined as the start  of  each  edit 
session.

Y - Type 5 lines each side of the cursor
This  command is equivalent to the command -5TT5T and is useful to  look 
at the file around the cursor position.

Z - move cursor to end of text
The  Z command is identical to the -B form of the B command,  and  moves 
the cursor to the end of the text in memory.

n<commandstring> - Iterate
The iterate command is be used to repeat a command string 'n' times. The 
Iterate  command  can be nested up to 8 levels deep,  and  may  be  used 
within  macros,  and  macro's  may be used  within  an  iteration.  This 
facility, combined with macro's make repetitive changes very simple. The 
H command is also very useful in iterations as confirmation can be given 
after each operation.

Example EDIT session
In  this  short example of EDIT use,  user input is shown  with  various 
comments on the right hand side.


A>EDIT MYFILE                           (CP/M command)
Super CP/M Editor V3.19
New File
*IThis is a test file to check EDIT     (<RET> inserted at end of line)
This is a second line
This is a third line
$$                                      (Press ESC to get the $)
*2J$$                                   (Jump to line 2)
-This is a second line                  (Note cursor postion)
*Cthird$3rd$$                           (Change 'third' to '3rd')
This is a 3rd  line
*B10T$$                                 (Type out the first 10 lines)
This is a test file to check EDIT
This is a second line
This is a 3rd line
*E$$                                    (End edit session)
Finished editing MYFILE.
A>                                      (Return to CP/M)




                         Command Summary


     nA                      Append text from input fill
     +B                      Move cursor to start (or end) of text
      Cstring1$string2$      Change string1 to string2
    +nD                      Delete characters
      E                      End edit, write file to disk
      H                      Halt until a key is pressed
      Itext$                 Insert text at cursor
     nJ                      Jump to line number
    +nK                      Kill lines from cursor
      L                      Move cursor to start of current line
    +nL                      Move lines from cursor
    +nM                      Move characters from cursor
      N                      as S,but searches disk as well
     nO$                     Output lines to default save file
     nOfilename.ext$         Output lines to filename.ext
     nP                      Print page of text
      Q                      Quit with no file changes
      R$                     Read default save file at cursor
      Rfilename.ext$         Read filename.ext in at cursor
      Sstring$               Search for string
      T                      Type current line and cursor position
    +nT                      Type lines from pointer
      V                      Verify file parameters
     nW                      Write lines to disk
     -X                      Define macro (80 characters max)
    -2X                      Print macro
     nX                      Use macro
      Y                      Type 5 lines each side of the cursor
      Z                      Move cursor to end of buffer
     n<commandstring>        Execute commandstring n times

    2 consecutive ESC's terminate and execute the command line
    A hash, where 'n' is allowed is equal to 65000
    Strings and filenames must be terminated with ESC