XREFASM

This is a modified version of one of the XREF utilities from the
US Library.  Those utilities produced a cross-referenced list
from Assembler Source Files (without doing the assembly) using
Line Numbers for the cross-referencing - not really very helpful!

This version works on the .PRN file produced by ASM and MAC
from Digital Research, and Z80ASM from the UK Volume 5.
It produces an alphabetially sorted, full cross-reference list
of Labels by address.  Labels are truncated to 7 characters for
economy of storage while the cross-reference list is being built.

The output is directed to a separate file, with Filetype (.REF),
and appears on the console, or may optionally be directed to
the printer instead.

The command syntax is as follows:

	XREFASM n:FILENAME.PRN q:

where     n: is an optional drive name for the source of the .PRN
File, and q: is an optional drive name to receive the .REF File.

If these drive names are omitted, then the default drive is assumed
for the .PRN file and the destination of the .REF file.

The Reference Output lists the label, then the address at which
the label was specified (or its Value, if an EQUATE) followed by
a colon.  Then come the addresses of all the places where that
label was referenced.  (See file XREFASM.REF as example)

In order for a label to be correctly recognised from the source,
all labels should either be terminated by a colon (:), or should
be identified as an EQUATE.  Failure to ensure this will result
in the address which identifies the label (in the first column of
the reference output), being shown as zero;  however all other
references will be correct and the label's own address will be
included in the list.

In order to reference only legal files, XREFASM expects the first
column in every line of the .PRN file to contain either a blank
(Ascii 20H) or a Form Feed (Ascii 0CH).  Any other character will
cause the referencing process to abort.  Normally in an assembly
file with no errors, this requirement is true until the end of
the assembly is reached, when the error count or next address
is written to column 1 of that line.   Any error flags which
result from an incorrect file are placed in column 1 on the line
in which they occur.  Thus XREFASM terminates neatly at the end
of the .PRN file or as soon as it encounters any error.


Ray Halls.
August 1982