MZ80B DISC FORMAT
			-----------------
	5.25in Disc, 35 Track, Double sided, Double density,
	with 512 byte sectors.

	Side I.D.s on disc are the reverse of normal.

	The first sector on track 0, ID side 0 is 256 bytes
	and the first gap 3 is increased by 256 * 4EH to
	keep the format buffer the same for all tracks.

	ID side 0 sectors go from 1 to 10 with skew as below.
	ID side 1 sectors go from 11 to 20 with skew as below.

	Physical Skew
	-------------
	ID side 0   1,6,2,7,3,8,4,9,5,10
	ID side 1   11,16,12,17,13,18,14,19,15,20

	Logical Skew 
	------------
	None

	Stat Dsk: results from origin computer
	--------------------------------------
	2720 : 128 byte record capacity
	 340 : kilobyte drive capacity
	 128 : 32 byte directory entries
	 128 : checked directory entries
	 256 : records / extent
	  16 : records / block
	  80 : sectors / track
	   1 : reserved track

	Format 
	------
	Group 1		gap 4a	 24 * 4EH
			sync	 12 * 00H
			          3 * C2H
			index am      FCH
			gap 1	 40 * 4EH

	Group 2		sync	 12 * 00H
				  3 * A1H
			id am         FEH
			id 	  4
			id crc    2
			gap 2	  1 * 00H
				 28 * 4EH
			sync     12 * 00H
			          3 * A1H
			data am	      FBH
			data    512 * 1AH
			data crc  2
			gap 3     1 * 00H
				 30 * 4EH

	Gap 4a			  1 * 00H
		 greater than  	106 * 4EH

	Format obtained by track dumps.		Tony Fagg
						04747 2972
						16-APR-84