********** This File Contains Examples of Code Necessary to Interface an 
        Applications Program, in the Form of a Task, with MTASK. Typical Code in
        Assembly Language and PL/M Form is Given. ******************************

        ------- Example 1 - A Typical Task -------------------------------------

         In Assembly Language :-
             (Remember that MTASK has set up a Stack for each Task)
                PUBLIC TSK3
                TSK3:
                     etc.
                     etc.
                     RET ;End of Task

         In PL/M or PLMX :-
             (DO NOT Compile as a 'MAIN' Module, MTASK sets up the Stack)

                PROG3:
                DO;
                 TSK3:
                  PROCEDURE PUBLIC;
                   etc.
                   etc.

                 END TSK3;
                END PROG3;

        ------- Example 2 - TICK Interrupt Service Routine ---------------------

                TRAP:: ;Entry Point from 8085 TRAP Interrupt
                     ;Save Acc. & Flags as these are used by RCLKINT
                     PUSH  PSW
                     ;Declare RCKINT as External
                     EXTRN RCLKINT
                     ;RCLKINT is the subroutine to reset the Clock
                     ; Interrupt Latch
                     CALL  RCLKINT
                     ;Recover Acc. & Flags
                     POP   PSW
                     ;Declare as Public the Entry Point to MTASK
                     EXTRN TICK
                     ; and Jump to it (MTASK takes care of the Return)
                     JMP   TICK
                END

        ------- Example 3 - Task Activation using ACTSK ------------------------

         In Assembly Language :-

                LOWPRIORITY EQU 0
                HIPRIORITY  EQU 1
                TASKNUM     EQU 3
                TSK3_PRIORITY EQU HIPRIORITY
                ;
                ;Activate task3 with High Priority


                                        1








                   MVI  C,TASKNUM
                   MVI  E,TSK_PRIORITY
                   EXTRN ACTSK ;Declare ACTSK as External
                   CALL  ACTSK
                ;Task 3 is Active from here on
                ;If Acc. is 0FFh on return, TASKNUM is invalid,
                ; or the Task is already Active

         In PL/M or PLMX :-

                   |
                DECLARE HighPriority LITERALLY ' 01H';
                DECLARE LowPriority  LITERALLY ' 00H';
                   |
                ACTSK:
                 PROCEDURE (TaskNumber, TaskPriority) BYTE EXTERNAL;
                 DECLARE (TaskNumber, TaskPriority) BYTE;
                END ACTSK;
                   |
                   |
                /* Activate Task 3 with High Priority */
                Status = ACTSK (3, HighPriority);
                IF Status = 0FFh THEN /* 3 is an Invalid Task Number */
                   |
                   |

        ------- Example 4 - Reservation and Initialisation of RAM for ----------
        --------------------           use as an Exchange      -----------------

         In Assembly Language :-

                DSEG
                   ;
                EXMPL_EXCH:
                    DS 6 ;Save RAM for Exchange
                   ;
                   ;
                CSEG
                   ;
                   ;
                   LXI  B,EXMPL_EXCH ;Set up Pointer to Exchange
                   CALL INITEX##     ;Use External S/Routine to Initialise it
                   ;
                   ;

         In PL/M or PLMX :-

                   |
                DECLARE ExampleExchange (6) BYTE;
                   |
                   |
                INITEX:
                 PROCEDURE (ExchangeAddress) EXTERNAL;
                 DECLARE ExchangeAddress ADDRESS;
                END INITEX;


                                        2








                   |
                   |
                CALL INITEX (.ExampleExchange);
                   |
                   |

        ------- Example 5 - Use of MSEND ---------------------------------------

         In Assembly Language :-

                  ;
                  ;
                DSEG
                  ;
                MSGE1: ;Message No. 1 - the "True" Flag
                    DS 3
                    DB 0FFH
                  ;
                  ;
                EXCHG1:
                    DS 6
                  ;
                  ;
                CSEG
                ;Send "True" Message to Exchange No. 1
                ;Exchange has been Initialised
                   LXI  B,EXCH1
                   LXI  D,MSGE1
                   CALL MSEND##
                  ;
                  ;

         In PL/M or PLMX :-

                   |
                DECLARE TrueMessage (4) BYTE INITIAL ( 00,00,00,0FFh);
                   |
                   |
                DECLARE Exchange1 (6) BYTE;
                   |
                   |
                MSEND:
                 PROCEDURE (ExchangeAddress, MessageAddress) EXTERNAL;
                 DECLARE (ExchangeAddress, MessageAddress) ADDRESS;
                END MSEND;
                   |
                   |
                /* Send "True" Message to Exchange No.1 */
                /* Exchange No.1 has been Initialised */
                 CALL MSEND (.Exchange1, .TrueMessage);
                   |
                   |

        -------- Example 6 - Use of MWAIT --------------------------------------



                                        3








         In Assembly Language :-

                DSEG
                EXCH2:
                   DS 6
                   ;
                   ;
                CSEG
                   ;
                   ;
                ;Wait for a Message at Exchange No. 2 for 5 Clock Ticks 
                   LXI  B,EXCH2
                   LXI  D,5
                   CALL MWAIT##
                   ;
                   ;


         In PL/M or PLMX :-

                    |
                DECLARE Exchange2 (6) BYTE;
                    |
                    |
                MWAIT:
                 PROCEDURE (ExchangeAddress, DelayTime) EXTERNAL;
                 DECLARE ExchangeAddress, DelayTime ADDRESS;
                END MWAIT;
                    |
                    |
                /* Wait for a Message at Exchange No.2 for 5 Clock Ticks */
                CALL MWAIT (.Exchange2, 5);
                    |
                    |























                                        4