MON7                              ____

              Monitor for marvin seven and cpm2.2              ___________________________________


This  monitor  provides  debugging facilities for  machine  code 
programmes.

Upon  loading  it  will self relocate to just  below  the  bdos, 
overlaying the ccp area, MON7 when reloceted is approximately 7k 
including  a stack area and internal storage  requirements.  But 
can extend depending upon the size of any loaded symbol table.

The warm start vector in the bios jump table is re-vectored back 
into  mon7 therefore preventing warmstarts except under  control 
of MON7.

Single  stepping and tracing is achieved by causing an NMI  (Non 
Maskable  Interupt) after each instruction.  The  advantages  of 
this  method over that used by DDT and ZSID is that even illegal 
instructions are not corrupted by the insertion of a  programmed 
break  point,  execution  in  trace  mode is faster  and  it  is 
possible to single step through prom. There are however a number 
of  disadvantages,  the  first being that the  monitor  is  thus 
machine  specific  and the second being that the NMI vector  may 
not  be used by the programme being debugged whilst single  step 
is  active,  this  second  problem has been  minimised  by  only 
inserting the NMI vector during single step commands,  also  the 
monitor  dose not allow the user to single step through the bdos 
vector  at address 5 but instead inserts a programmed  break  at 
the  return  address.  great care must still be taken  with  any 
programme  segments  that  use addresses 66H 67H and  68H  (Note 
these bytes are inside the default FCB) and if this area is used 
it  is necessary to use break commands rather than  single  step 
type commands over any section which reads from or writes to any 
of the three bytes of the vector.

WORDS & BYTES
When  using the monitor it is often necessary to enter word  and 
byte  data  from the keyboard this data is normally 1 to  4  hex 
characters  (1 to 2 for bytes),  it is however possible to enter 
decimal  values if preceded by a hash character (note  the  hash 
character  prints  as  # on this printer),  also if  a  word  is 
preceded  by  an  @  symbol then this instigates  one  level  of 
indirection,  alternatively the sign ^ means take data from user 
stack (the user stack is that being used by the programme  being 
debugged),  also  `  (shifted @) may be used to input single  or 
double  byte ascii chars,  if the second character of  an  ascii 
pair  is  either  a  space  or  an end  of  line  then  this  is 
interpreted as a single char input,  hence it is not possible to 
input  a  double  byte ascii word if the ls byte  has  the  value 
space.  The  final method of data entry is as a symbol here a '.' 
character indicates the start of a symbol,  the value  associated 
with  the  first  match found in the symbol table  is  used,  the 
string  delimiter is any character with ascii value less than  or 

equal to space.  also the number may be preceded by any number of 
spaces. and is terminated by any inconsistent character.

0100 is the hex value for 256
   100 also  "    "    "    "
#256 is decimal 256
^ is the value pointed to by the user stack pointer.
^^ is the value next to the top of the user stack.
^^^ is the 3rd value (word) from the top of the user stack.
@0 is the word at address 0.
@^  is  the word pointed to by the word on the top of  the  user 
stack
@@8 is the word pointed to by the word stored at address 8
Note  this indirection operator is only available to  approx  10 
levels of indirection depending upon the command being executed.
`A gives 41H
`AB puts 41H in the ms byte and 42H in the ls byte
.test gives the symbol table entry associated with TEST.
.TeSt as above.

                            COMMANDS

Command  lines  are entered via the normal CPM line  input.  The 
first  character of this line is then regarded as a command  and 
the   following  characters  are  interpreted  as  the   command 
requires.

A          Single step.
B          Set break points.
C          Copy store.
D          Display store.
E          Execute.
F          Fill store.
G          Get sector from disk.
H          Hunt for string.
I          Input command line and file name.
J          Port I/O command.
K          Single step until return from routine to be called.
L          List in dissassembled form.
M          Modify memory.
P          Display and modify user registers.
Q          Quit back to CPM.
R          Read file from disk.
S          Single step.
T          Trace programme.
W          Write 128 byte sector to disk.
X          Hexadecimal arithmatic. and symbol list.
Y          Extend symbol table.
Z          Store test.


COMMAND    FORMAT     DESCRIPTION

A          A             Single  step  through  all  store.  One 
                         instruction  of  the user programme  is 
                         executed even if it lies above the base 
                         of MON7

B          Bn,a          Set  break point number n to address a, 
                         n is number in the range of 0 to 3 a is 
                         an  address  in the range  0  to  ffff, 
                         except  that  an address of  zero  will 
                         clear  that  break  point.   These  are 
                         permanent  in  that  they  will  remain 
                         active  until  explicitly cleared by  a 
                         Bn,0 command.

C          Cas,ae,ad     Copy  memory  block  as to  ae  to  the 
                         memory  block  starting  at  ad,   This 
                         command  will  copy  overlaping  blocks 
                         correctly.

D          Das,ae        Display  memory block starting from  as 
                         and ending at ae,  if as is not entered 
                         then it defaults to the last  displayed 
                         address+1  or the current value of user 
                         programme  counter,  whichever was  set 
                         last.  If ae is not present it  default 
                         to as+128. The form of the Display is:-

0100  31  00  02  2A   01  02  E5  D9    1 ^@ ^B  * ^A ^B  e  Y
0108  E1  D9  EB  2A   06  00  A7  ED    a  Y  k  * ^F ^@  '  m

                         The  first number is the address of the 
                         first  byte of that line in  hex,  then 
                         follow   8   pairs   of   hex    digits 
                         representing  the  value of  the  eight 
                         bytes starting at address,  then follow 
                         eight  ascii  representations of  those 
                         bytes,  if the character is preceded by 
                         a  ^  symbol then this means  that  the 
                         byte  is  a control code i.e  ^A  means 
                         control  A which is a value of  1.  N.B 
                         the top bit is ignored for the purposes 
                         of the ascii representation.

E          Ead,b4,b5,b6  Execute causes the user programme to be 
                         initiated  at  address ad  without  any 
                         single   step  but  break  points   are 
                         active.  B4,b5 and b6 are the addresses 
                         of temporary break points which will be 
                         cleared upon a return to MON7. If ad is 
                         not entered then the execute address is 
                         to   continue  from  where   the   user 
                         programme   last  stopped.   If  ad  is 

                         present  then the user stack is set  to 
                         100H.

F          FYas,ae,d     Fill  causes the ram between as and  ae 
                         inclusive to be filled with the data d. 
                         The  character Y must be present as  an 
                         extra  safe guard against  accidentally 
                         erasing store.

G          Gdt,s,sm      Get  from  disk,  into the default  dma 
                         buffer at 80H and display as in display 
                         mode,  the 128 byte sector from drive d 
                         (a  letter  in the range 'A'  to  'P'), 
                         track  t (a number) physical  sector  s 
                         and 128 byte segment of that sector sm. 
                         This  command does not check the DBP or 
                         the sector translation vector and  will 
                         therefore  allow  access to disk  who's 
                         parameters do not fully match the  DPB. 
                         In  fact sm forms the most  significant 
                         eight  bits of the sector number and  s 
                         forms the ls. See appendix.

H          Has,ae,dst    Hunt for dst through ram from as to ae. 
                         Dst is a data string of up to 18 bytes, 
                         which may be input as follows:
                         1/      a hexadecimal value for which a 
                                 match must be found.
                         2/      an  ascii  string for  which  a 
                                 match must be found.  the ascii 
                                 string   may  be  enclosed   in 
                                 either single or double quotes, 
                                 if  enclosed in single then  it 
                                 may  contain  double  and  vice 
                                 versa,  i.e.      "abc'xyz"  is 
                                 valid   as  is  'abc"xyz'   but 
                                 'abc'xyz" is not.
                         3/      a  ?  (question mark) which may 
                                 match any byte.
                         4/      if  the hex or string entry  is 
                                 preceded  immediately  by  a  ~ 
                                 symbol then that entry must  be 
                                 absent for a match.
                         5/      if  an  entry is preceded by  ! 
                                 (exclaimation  mark)  then  the 
                                 top bit is ignored.
                         When  a  match  has been  found  it  is 
                         displayed  with a similar form  to  the 
                         display command.

00A0  :  60 F5 FE CD BB 00 6C DB 6C 06       `  u  ~  M  ; ^@  l

                         The  first word is the address at which 
                         the  string  was  matched  (address  of 

                         first byte) then follows a :  then  two 
                         bytes  previous  to the  match  address 
                         then  the  first  match byte  then  the 
                         seven following match bytes,  the  same 
                         bytes  are  then displayed in the  same 
                         ascii format as in display mode.
                         E.G.  the  dst fe ? ~eb !d would  match 
                         FE 01 EF 0D  and  FE 05 04 8D  but  not 
                         FE 05 EB 0D  because  of  th  EB,  also 
                         F7 !"ABC" ?  would match F7 41 42 43 FF 
                         or F7 C1 42 C3 01.

I          Ist           Insert,  string will enter a sting into 
                         the  buffer at 80 and pars it into  the 
                         default  fcb N.B.  Only the first  file 
                         name is parsed.  It will also set st as 
                         a file name for any following file type 
                         actions.

J          JIad          Input byte from port. This command will 
                         read  a byte from port address  ad  and 
                         display it as two hex digits.
           JOad,da       output the data byte da to port address 
                         ad.

K          K             This   command  initiates  single  step 
                         commands  executing  from  the  current 
                         user programme counter,  and continuing 
                         until the user stack pointer returns to 
                         its current value. If it is required to 
                         step until the return from a subroutine 
                         then  this  command  must  be  executed 
                         immediately  before  execution  of  the 
                         call  instruction,   if  the  call  has 
                         already   been  executed  then  a   E,^ 
                         instruction  will insert  a  programmed 
                         break at the return address,  this will 
                         execute  faster but will only work  for 
                         normal  returns.  The K command is also 
                         useful  to find when a value  is  poped 
                         from  the stack,  issueing a K  command 
                         immediately  before a push will  return 
                         to MON7 on that value being poped.  N.B 
                         This  command will return to mon  after 
                         only   1  instruction  if   the   first 
                         instuction  does  not modify the  stack 
                         pointer.

L          Lra,la        List  programme in  dissassembled  form 
                         from address ra with offset to la. That 
                         is  programme  residing  at ra  may  be 
                         dissassembled  as though it was at  la. 
                         if  la  is  not specified  then  it  is 
                         assumed to be equal to ra, if ra is not 

                         specified  then  it is  assumed  to  be 
                         continuation  of  a previous L  command 
                         and  the dissassembly starts  from  the 
                         beginning  of the last line of the last 
                         dissassembly  or  100H if this  is  the 
                         first invocation.  The dissassembly  is 
                         16 lines at a time, and after each page 
                         pressing  space  will  print  the  next 
                         page,  pressing  return will return  to 
                         command  level  and typing L or N  will 
                         allow  the  entry  of  a  new   logical 
                         address (la). e.g.

 0100   LD SP,0200.STACK         1^@^B         310002
 .RESTART
 0103   LD HL,(0201.BUFFBASE)    *^A^B         2A0102
 0106   PUSH HL                  e             E5
 0107   EXX                      Y             D9
 0108   LD HL,(0500)             *^@^E         2A0005

                         The first field is the logical  address 
                         4  digit hex,  the second is the  zilog 
                         mnemonic  (relative  jumps are  printed 
                         with a logical address), the 3rd is the 
                         ascii  characters for each byte of  the 
                         code line with the top bit stripped and 
                         with  control  code represented  as  an 
                         upper case character preceded by ^. The 
                         final field consists of one pair of hex 
                         digits  for each byte of the  line.  If 
                         the  address  matches  a  symbol  table 
                         entry then that symbol is placed on the 
                         line above (as RESTART),  if a  sixteen 
                         bit  value matches a symbol table entry 
                         the name is printed following the value 
                         and separated from it be a '.'.
M          Mn            Modify memory from address n,  (default 
                         is  the last modified address  or  100H 
                         for  the  first invocation) The  modify 
                         command  prints the address  to  modify 
                         the contents of that address and awaits 
                         a command.
 .^D 0112    #132 84     
                         The  four fields of the printout are :- 
                         1       The ascii value of the contents 
                                 of the address,  the '.'  means 
                                 top  bit  set  the  ^  means  a 
                                 control  char and the D is  the 
                                 char.
                         2       Thisfield  is the address as  a 
                                 four digit hex number.
                         3       The third field is the contents 
                                 of the address in decimal.
                         4       The  fourth is the contents  of 
                         
                                 the address in hex.
                         If  the address matches a value in  the 
                         symbol  table then that name is printed 
                         on the previous line.
                         at  this  point a line may  be  entered 
                         which consists of data to be entered or 
                         a  command to move the current pointer. 
                         The commands are :- 
                         1       an  empty  line means  move  to 
                                 next address.
                         2       - (minus)    means   move    to 
                                 previous address.
                         3       Mn means jump to address n.
                         4       '.'  means  return  to  command 
                                 mode .
                         5       $n  means put in offset as  for 
                                 relative jump to address n i.e. 
                                 at  address 132H entering  $130 
                                 would  insert FEH into  address 
                                 132H.
                         6       "  or ' (shifted 7)  instigates 
                                 string  input mode this mode is 
                                 exited  by  a  matching   quote 
                                 mark, if the line is terminated 
                                 before  a  matching  quote  has 
                                 been   found,   then  a   cr,lf 
                                 combination   is  inserted  for 
                                 each  end of line  encountered. 
                                 N.B. single character input can 
                                 use   the  `  (shifted  @)   as 
                                 normal.
                         7       Otherwise any input is  assumed 
                                 to be a single byte and follows 
                                 the normal rules.
P          P             P  with  no command tail will print  the 
                         current state of all the registers. 
      FLAGS   HL   DE   BC   AF
 MAIN ------ 0000 0000 0000 0000
 ALT. ------ 0000 0000 0000 0000

  SP   PC   IY   IX  STK1 STK2 STK3 STK4
 0200 0103 0000 0000 3600 0019 0000 0000

 -2 -1 PC +1 +2 +3 +4 +5   0000 1052 9876
 00 02 2A 01 02 E5 D9 E1   C303 4F52 9625

 (BC) (DE) (HL) (IX) (IY)
 C303 C303 C303 C303 C303

 Brk0 Brk1 Brk2 Brk3
 0000 0000 0000 0000

 .RESTART
 0103   LD HL,(0201.BUFFBASE)    *^A^B         2A0102

                         The  first two lines are the normal and 
                         alternate  register  set.  flags  being 
                         indicated such that a C will appear  if 
                         the carry flag is set,  a Z will appear 
                         for  a  zero etc.  The next  lines  are 
                         obvious  except STK1/2/3 & 4 which  are 
                         the values on the user stack.  The next 
                         line  contains the current programme as 
                         a  series of pairs of  hex  characters. 
                         The next three words on the display are 
                         user  setable addresses and the  values 
                         underneath  are  the contents of  these 
                         addresses.  Following are the  contents 
                         of  the store as pointed too by each of 
                         the main register pairs ,  then  follow 
                         the  four permanent break points as set 
                         by the B command.

           Pr            In  this mode the contents of the  user 
                         registers  may be modified where r is a 
                         register form the following set : -
                         AF      sixteen bit acc & flags
                         BC DE HL IX IY  main sixteen bit pair
                         AF'     Alternate acc & flags
                         BC' DE' HL' Alt. 16 bit registers
                         SP      Stack pointer
                         PC      Program counter
                         0/1/2   User definable addresses 0/1/2.
                         A       8 bit register acc.
                         B/C/D/E/F/H/L Other 8 bit registers
                         A'      Alternate 8 bit acc
                         B'/C'/D'/E'/F'/H'/L'
                         IXL/IXH 8 bit sections of IX register
                         IYL/IYH "                 IY
                         If  it is a sixteen  bit  specification 
                         then  a sixteen bit value is  displayed 
                                 
                         and a new 16 bit value is accepted from 
                         the  keyboard  otherwise only an 8  bit 
                         section of a register is effected.

Q          Q             Quit back to CPM via the vector at 0.

R          Rn            Read  file  as set up with  previous  I 
                         command,  The file is read to address n 
                         if the file name extension is HEX  then 
                         it  is read as though it was intel  hex 
                         format.  if  n is not specified then  a 
                         hex  file  will load at  its  specified 
                         addresses  a non hex file will load  to 
                         100h.  Once  loaded  The end  address+1 
                         will  be printed on the screen.  If  it 
                         was  a .HEX file the three numbers  are 
                         printed,  the  end  address+1  the  run 
                         address of the hex file as specified in 
                         the end of file record,  end address +1 
                         as it would of been if a n had not been 
                         specified.   The  end  address  is  the 
                         address of the last byte in the program 
                         not the largest address loaded.

S          S             Single  step  1  instruction.   If  the 
                         address  of that instruction is 5  then 
                         there will be a programmed break placed 
                         at the address on the top of the stack, 
                         and  a jump to 5 will be  executed.  If 
                         the  address is above the base of  mon7 
                         then  the step commands  will  continue 
                         until  an  address value less than  the 
                         base of MON7 is reached.

T          Tb1,b2,b3     Trace  until address b1 or b2 or b3  or 
                         one of the four permanent break points, 
                         as  specified by the B command.  During 
                         the trace programme is executed at slow 
                         speed,   tracing   does  not   continue 
                         through  bios  calls,   therefore  disk 
                         accesses are still possible.

W          Wdt,s,blk     This  is the inverse of the  G  command 
                         and will write the sector stored at 80h 
                         onto   drive  d  (This  specifies   the 
                         physical  disk  and  density)  track  t 
                         sector s and 128 byte block within that 
                         sector  blk.  In fact blk forms the  ms 
                         half  of the sector address and s forms 
                         the ls half. see appendix.

X          Xn            Hex arithmatic.  If n is not  specified 
                         then  the symbol table will be  printed 
                         on  the screen.  Otherwise n may be  an 

                         expression   containing   addition   +, 
                         subtraction  -,  logical  anding &  and 
                         logical  oring | of the  operands.  The 
                         result is displayed:

hex=0000   ms char= ^@   ls char= ^@   decimal=   #0  .LABEL

                         LABEL is the first label found with the 
                         value of n.

Y          Ys v          If  no command tail is entered  then  a 
                         symbol  file as specified by a previous 
                         symbol  name s is put into  the  symbol                                  
                         table with the value v.

Z          Xx y          Test  store  between addresses x and  y 
                         the  store  between x and y  is  filled 
                         with a pattern which is the ms half  of 
                         the  address xored with the ls half  of 
                         the address and xored again with a pass 
                         number.  The pattern is then checked if 
                         it  does not match on any address  then 
                         the  failing address,  the pass  number 
                         the  data expected in that byte and the 
                         data  found is displayed,  if no  fails 
                         are  found  then  the  pass  number  is 
                         displayed  at  the completion  of  each 
                         pass.


                            APPENDIX

                  Marvin 7 sector transilation                  ____________________________

When  calling the marvin bios set sector command without a  call 
to sector transilate then the sector address word in the case of 
blocked floppy disks is split into two halves the ls 8 bits is a 
physical sector number,  this will normally range from 1 up i.e. 
1 to 26 for standard IBM 8" single density format.  Bits 8 to 14 
are  a  7 bit section number and specify which  section  of  the 
physical  sector  is to be refered to,  the value of this  would 
always  be  0  for  128 byte sectors and range 0  to  7  for  1k 
sectors.  The top bit is a side select bit =1 for side two of  a 
diskette,  this  is  only accepted by the operating system in  1 
special disk format.



                     Hardware requirements                     _____________________

The MON7 programme commands A,S,K and T require special logic in 
order  to  cause  a  single step  after  each  instruction.  The 
standarad  version  expects  this to occour 2  M1  cycles  after 
writing  to  port  11 (decimal),  but this  can  be  changed  be 
changeing  the value of the label SSPORT.  The hardware to cause 
this  is  a three stage shift register with asynch clear  and  a 
single inveretor.  For the Invertor any spare inverting gate may 
be used, or if a separate ic must be used then a 74LS04. For the 
shift register a 74LS174 or 74174 may be used.  The  connections 
of the 174 are as follows:-

Pin 1      'enss         This  is a negative pulse produced from 
                         an  I/O decode.  2 M1 cycles after this 
                         pulse  a Non Maskable Interupt will  be 
                         produced.

Pin 3      HI            If  the IC is an LS type then this  pin 
                         may  be connected to +5V else it should 
                         be  connected  via  a  resistor  (about 
                         1k)to  +5V.


The  IC is then connected as a three stage shift  register  with 
pin  3 as it's input and pin 7 as it's output which is an active 
high  NMI signal that needs inverting before being input to  the 
input of the Z80. This is acheived by connecting:-

Pin 2 to Pin 4  and  Pin 5 to Pin 6.

The  clock  input (Pin 9) should be connected to M1  or  'M1(not 
M1).

The  output  Pin 7 should then be connected to the  input  af  a 
spare  invertor the output of which goes to 'NMI ('means not) If 
a spare gate is not available then use pin 1 of a 74LS04 as  the 
input and pin 2 as the output.

If  NMI  is already used for some other purpose it will  not  be 
possable  to  and  the two NMI's together directly  but  a  more 
complex  circuit would be required.  where the shift register is 
extended  by  1 more stage (connect pin 7 to pin  11)  and  then 
instead of an ivertor a nand gate would be required (Replace the 
74LS04  by a 74LS00 connect pin 7 of the 74LS174 to pin 1 of the 
74LS00,  Pin 10 of the 74LS174 should be connected to pins 4 and 
5 of the 74LS00,  Pin 6 of the 74LS00 should be connected to Pin 
2  of  the 74LS00 then pin 3 of the 74LS00 is the  non  maskable 
interupt  connection  to the Z80 ) this produces a pulse  rather 
than  the edge that the simpler circuit produces.  This may then 
possably be anded with any existing NMI source assuming the  two 
NMI'S  will  never  clash,  (If the NMI has been used  for  disk 
access then there will probably never be a clash as MON7  normal 
step  commands  do  not  step through the  BIOS  or  BDOS  areas 

although  the  A command will this would only be used  for  some 
special purpose).

The  dissasembler decodes the commands that use  IXL,IYL,IXH,IYH 
(8  bit sections of the index registers) in a  sensable  format, 
I  would  be  very interested to hear of any  bugs  that  anyone 
finds.  I do beleve that the only glareing ommision from MON7 is 
an  assemble command,  this may be sorted some time,  and I will 
submit the result if it is.

Upon  invocation  MON7 modifies the warmstart vector within  the 
BIOS  to  point back into MON7 this allows jumps to zero  to  be 
trapped (I know some people frown upon this act, but this vector 
is  allways corrected upon an orderly exit,  and anyway  if  the 
exit  was that disorderly so as not to go through the  warmstart 
vector then someone is being even more diabolical than MON7).

The supplied .COM file does self relocate to just below wherever 
address  6  points but if it is nessesary to modify  the  source 
then the easies process is as follows.

This process assumes that a Relocating Z80 assembler and  linker 
capable of producing Page relocatable format files is available. 
Assemble  the  .ZSM file to produce a .REL file then  link  that 
file (If using the Digital research linker with the [op] option) 
to  proceduce a .PRL file.  Then invoke the .COM version of mon7 
then load LOADPRL.HEX into it's natural addresses (aprox 100H to 
1a7h).  Then load MON7.PRL into address 200 upwards with a  R200 
command then quit and save up to the end address of MON7.PRL.

If a relocating Z80 assembler is not available the there are two 
options 
1/         assemble  it  as  an absolute program  (  remove  the 
           pseudo   op  code  CSEG  from  the  begining  of  the 
           program and replace it with an ORG pseudo op), here a 
           small  loader will be required it only need copy  the 
           program  from 100H to it's running address  but  this 
           will  then  only run with a single size of  operating 
           system.

2/         Alternatively assemble it twice once at address  100H 
           and   once  att  address  200H  then  use  the   prog 
           HEXTOPRL.COM  to produce a page relocatable file  and 
           combine that with LOADPRL.HEX as above.



HEXTOPRL.COM
This  program expects two HEX files withe the same primary  name 
but different secondary names:

filename.HEX is a program file assembled to run at 100H.
filename.HX2 is the same program but assembled to run at 200H.

it is initiated by 

HEXTOPRL d:filename

It will expect the two files on drive d and return the result to 
drive d as a page relocatable file called filename.PRL.