***** MTASK - A MultiTasking Executive for 8080, 8085, & Z80 Systems ******

     W.S.J.Brice
     I.B.A. Harman Engineering Training College,
     Fore Street,
     Seaton, Devon.
     England


INTRODUCTION TO MTASK
	MTASK  is  a  Multitasking Operating System that  permits  the 
writing of  programs in the form of separate modules or  'Tasks'.  The 
Operating  System  divides the efforts of the microcomputer among  the 
Tasks in such a way that they appear to execute  simultaneously.  Each 
Task  can  be  in  one of several states during  the  execution  of  a 
program. These states are:-
     ACTIVE
     In this state the Task is either being executed,  or waiting      
     in  a queue of Tasks for its turn to be executed.  Each Task      
     is  given  either a High,  or Low,  Priority  Level  and  is     
     placed  on  one  of two queues  according  to  its  priority           
     level.  Tasks  from the Low Priority queue are not  executed           
     whilst  there  are  Tasks on the High  Priority  queue.  The      
     priority level of a Task is not fixed and must be  specified      
     each time a Task is put into the Active state.
     
     IDLE
     Idle  Tasks  are ones that exist in the program but are  not 
     required to run at that point in time.  An Idle Task must be 
     'Activated'  and  put onto the appropriate queue  of  Active 
     Tasks before it can be executed.

     DELAY LISTED
     Associated with each Task is a 16 bit delay value. If a Task 
     is put onto the Delay List,  then it is temporarily put into 
     an  idle  state until the time period defined by  the  delay 
     value has elapsed.  The Delay period is defined as a  number 
     of  pulses generated by an external clock source.  For  each 
     pulse  from that source,  the delay value is decremented  by 
     one until it reaches zero. The Delay Listed Task is put onto 
     the appropriate Active Task queue at that time.

     Intercommunication  between  Tasks is made possible by  means  of 
'Exchanges'.  The  facility to use Exchanges is a function built  into 
MTASK  which  allows Messages to be passed from Task to  Task.  Direct 
communication  between  Tasks  is not possible  since  Tasks  are  not 
executed simultaneously. The Exchange acts as a "Post Box" which holds 
the  message (or more accuratly,  the address of the Message) "posted" 
by  the  sending  Task,  until the receiving Task  is  ready  for  it. 
Exchanges  consist  of  a small area of memory (6 bytes)  in  the  RAM 
reserved  for  a  Task,  but the organisation of the sending  and  the 
receiving of Messages is carried out by MTASK.












USE OF MTASK
 1/ Task Format
     Each  Task  can  be  written as a  separate  Subroutine  or  PL/M 
procedure.  The RETURN at the end of the subroutine or procedure  will 
terminate  the  Task.  That Task will remain idle until  another  Task 
activates it (see Task Activation below).  All Tasks,  except for Task 
1,  are  idle  after the system initialisation which follows a  Reset. 
Task 1 is automatically activated after the initialisation so that  it 
may  be used to initialise data structures,  ports etc.  used by Tasks 
and to activate the other Tasks required at the start of the program.
     The  program making up a Task should not manipulate the stack  in 
any way,  except for the usual CALLs,  RETURNs,  and matched PUSHs and 
POPs.
     The  Operating  System expects Task entry points to  be  given  a 
Public label of the form TSKn, where n is the Task number.

     Refer to Example 1 in EXAMPLES.TXT.


     Note  that a Task can terminate itself and go into the Idle state 
by CALLing or JUMPing to the Public Label ENDTASK from within the body 
of the program.

 
 2/ Reset 
     On Reset and after any initialisation necessary, the entry to the 
Operating System is via the Global Label "MTASK". The Operating System 
sets  up  a Stack for its own use and a Stack for each of  the  Tasks. 
Task  1 is then executed and should carry out any  initialisation  and 
must also activate any other tasks required at this time. 


 3/ Stacks
     The  Stack  areas used by the Operating System and by  each  Task  
are defined in GLDATA.MAC. The Task Stacks are equally divided between 
1KByte of RAM.  On the completion of the development of Task Software, 
the  size  of  individual  Task Stacks can be altered  to  suit  their  
requirements  if  economy of RAM is necessary.  This can  be  done  by 
changing  the  appropriate part of the file defining the Stack  sizes. 
This is GLDATA.MAC.   Each Task Stack is identified by a Public  Label 
of  the  form  STn,  where n is the Task  number.  After  any  changes 
GLDATA.MAC  should  be  reassembled to produde a .REL  file  with  the 
required size of Task stacks.












     The  Stack required by each Task must include space to store  the 
CPU status and 4 bytes for use by the Operating System, in addition to 
the Stack area required by the Task itself.

     Space for CPU Status   <10 Bytes> if 8080 version
                            <12 Bytes> if 8085 version
                            <22 Bytes> if Z80 version
     Space used by MTASK      6 Bytes
     Space used by the Task   ? Bytes
                         __________
     Task Stack Size =       ** Bytes

****  When calculating the size of Stacks,  remember that an error  on 
the  high side is far less disasterous than an error on the low  side. 
****

 4/ Clock Interrupts
     To function properly, this Operating System requires an interrupt 
that  is  driven by a pulse train with a regular and accurate  period. 
The  function of this interrupt is both to provide a timing  reference 
for the built-in delay provided by the Operating System and to  regain 
control  from  Tasks to ensure a sharing of CPU time among the  Tasks. 
This interrupt MUST NOT be masked at any time. The period of the pulse 
train is the timing unit of the Operating System, for example, a delay 
of  10   units  will result in a real time delay of 5 Seconds  if  the 
pulse train has a frequency of 2 Hz.
     The  interrupt service routine must clear any  interrupt  latches 
etc.  and  JUMP  to  the Global Label TICK.  Any code  used  for  this 
purpose,  between  the  the Interrupt occurring and the Jump to  TICK, 
must preserve all CPU registers and flags. The interrupted Task is put 
onto  the appropriate queue of active Tasks and the next waiting  Task 
is executed.

     Refer to Example 2 in EXAMPLES.TXT



 5/ Task Activation
     Built in to MTASK is a Public Subroutine or Procedure to activate 
a  Task.  Entry  to  this  Procedure is by  the  Public  Label  ACTSK. 
Parameters  must  be  passed  to ACTSK in the C  and  E  registers  to 
indicate the number of the Task to be activated and the Priority Level 
it is to be given.  A priority code of 0 sets low priority and a  code 
of 1 high priority.  The Accumulator will contain 0FFH on return if an 
invalid Task number is given (e.g.  A Task number of 0 or greater than 
TOTALTASKS), or if an attempt is made to activate an already active or 
delay listed Task.  Examples of the use of ACTSK are given in Assembly 
Language and in PL/M in Example 3 of EXAMPLES.TXT.







 6/ The Use of Exchanges for Task to Task Communication
     The primary use of Exchanges is as post boxes for the passing  of 
Messages  from one Task to another.  The Messages can be of many types 
and may be used for the transfer of data, or simply as flags to enable 
Task  synchronisation.   A  secondary  use  of  exchanges  is  in  the 
generation of fixed time delays.  This is described in further  detail 
below.
     An  "Exchange" consists of a 6 byte block of RAM used by MTASK to 
store  pointers  that  enable it to keep track  of  Messages  awaiting 
collection,  or  of  Tasks waiting for a Message.  The  Exchanges  are 
created  by the programmer to meet his needs.  Each Exchange  consists 
RAM  reserved  by  the programmer for this purpose and  this  must  be 
initialised before it is used. Each Exchange is initialised by using a 
public subroutine which exists within MTASK called "INITEX". 

**** After initialisation,  the data stored in the Exchange should not 
be altered in any way. ****

     The examples in Section 4 of EXAMPLES.TXT show the generation  of 
an   Exchange  by  the  processes  of  memory  reservation  and   then 
initialisation.


     The  Messages  handled by MTASK have a format which  is  flexible 
enough to meet many needs.  A message consists of a data structure  in 
RAM with the following format :-

     Bytes  #0 & 1 :-        LINK POINTER *
     Byte   #2     :-        MESSAGE TYPE *
     Byte   #3 and above are optional and may be used  to  convey 
                             single data bytes, or blocks of data.
MTASK does not move the data, but transfers the address of the Message 
which is the address of Byte #0.

****  The  contents  of the first two bytes of a Message are  used  by 
MTASK  and should not be altered in any way by the programs making  up 
the Tasks. ****

     The  third  byte is reserved as an indicator of message type  and 
may  be  set  when the message is delivered to  a  waiting  Task.  The 
remainder  of  the message can consist of any data structure that  the 
programmer  requires.  In  most cases it will consist of  single  byte 
codes and flags.
                               ________________
          MESSAGE ADDRESS --> | LINK POINTER   | (2 Bytes) }
                              |----------------|           } Necessary
                              | MESSAGE TYPE   | (1 Byte ) }
                              |----------------|
                              |                |  }
                              |--  Message ----|  } Optional
                              |    |     |     |  }
                              |--- v --- v ----|

     MTASK  provides two public subroutines to permit the  passing  of 
Messages between Tasks.  These are "MSEND" and "MWAIT".  MSEND is used 
to send a Message to an Exchange and MWAIT is called by a Task wishing 
to  fetch  a  mesage from an Exchange.  Examples of the use  of  these 
Subroutines are shown below. MSEND is called with parameters in the BC 
and  DE  registers  indicating the Exchange address  and  the  Message 
address.


     MWAIT  is  called  with  parameters in the BC  and  DE  registers 
indicating  the Exchange address at which the Task is to wait and  the 
length of time for which it is to wait.  The latter "Delay"  parameter 
can  have  any value between 0000h and FFFFh.  If the Delay is  0000h, 
then the Task will return immediatly, either with a message, if one is 
stored at the Exchange,  or with a dummy "Timeout" Message  if none is 
available.  The  Timeout Message can be distinguised by  the  "Messgae 
Type" byte being 03h.

     Sections 5 and 6  of EXAMPLES.TXT contains examples of the use of 
MSEND and MWAIT in Assembly Language and PL/M form.

     If  the Delay parameter is in the range 0001h to FFFEh,  the Task 
will wait at the Exchange until a Message becomes available (which may 
be  immediatly,  if a Message is already stored at the  Exchange),  or 
until the number of clock ticks specified in the Delay parameter  have 
occurred. This is acheived by putting the waiting Task into the "Delay 
Listed" state.
     A Delay parameter of FFFFh is an indefinite delay.  If a  Message 
is  already waiting at the Exchange,  the Task will return  immediatly 
with  that  Message,  otherwise  a  Task with  this  delay  will  wait 
indefinitly  for a Message to appear at the Exchange.  The task is put 
into  the  "Idle"  state  until  such  time  that  a  message  becomes 
available.
        The MWAIT entry point to the Operating System may also be used 
to   provide   two  other  facilities  which  are  necessary  in   the 
Multitasking environment. These are the provision of fixed delays in a 
program  and the ability of a Task to return control to the  Operating 
System without terminating itself.
	The  first  is necessary since the use of techniques  such  as 
decrement loops to generate delays is undesireable for two reasons.  A 
delay  program within a Task will be interrupted randomly by the Clock 
Tick interrupt and as a consequence the time delay generated will vary 
in a random manner.  The 'time wasting' inherent in a delay program is 
also a waste of CPU time whilst other Tasks are likely to be waiting.
	The second facility of temporarily returning to the  Operating 
System  from within a program is similar to the effect of a Clock Tick 
interrupt.  This  is  usful  in allowing other  waiting  Tasks  to  be 
executed  before a return to the original Task.  Strategic use of this 
facility  can  provide very efficient multiplexing  of  Tasks.  As  an 
example, a Task could contain a loop repetetively testing a flag until 
an  external  event occurs.  The Task  will use a lot of CPU  time  in 
testing this flag. If speed of response to the  change of state of the 
flag is not vital,  a return to the Operating System placed within the 
loop  will  allow other Tasks to be executed between each test of  the 
flag  status.  In consequence better use will be made of the CPU  time 
and smoother Task multiplexing will result.


     The  main use that will be made of MSEND and MWAIT is the passing 
of  flags  between  Tasks.  These flags are necessary  to  enable  the 
synchronisation and scheduling of Tasks and may also be used to ensure 
that only one Task at a time has access to a shared resource,  such as 
a  block  of memory.  Further information on the use of  messages  for 
these  purposes is given in the Intel Application Note  AP33,  'RMX/80 
Real-Time MultiTasking Executive', pages 5 - 6.

 7/ The MTASK disc contains the following files :-
      1/ Two explanatory text files:-
        README.DOC    - This file
        EXAMPLES.DOC  - A  text  file  containing  examples  of  code 
                         used  to  interface with MTASK and  which  is 
                         used as a reference in this file.
      2/   Three   Assembly  Language  Modules   (Microsoft   M80 
                                                       compatible)
	MNPROG.MAC   - Initialisation & Main Prog. Loop.
	RUNTASK.MAC  - Routines used by CASETASK to Initiate & 
			Terminate Tasks.  The parameter 'CPU'  in 
                        this can be set to 8080,  8085, or Z80 to 
                        allow assembly to suit these processors.

	GLDATA.MAC   - Global Data Structures & Variables

     3/ Nine compiled PL/M Modules **

	ACTIVATE.ASM  - Activates a Task by Placing it on the Ready List.

	ACTDEL.ASM    - Places a Task on the Delay List.

	DISPATCH.ASM  - Used in the Main Prog. Loop to Execute Tasks in turn.

	DECDEL.ASM    - Used to Decrement Delay counts of Delay Listed Tasks.
			When a Task has timed out, it is placed on the 
			appropriate Ready List.

	CASETASK.ASM  - Used by DISPATCH to Execute Tasks from the Ready Lists.

        SEND.ASM      - A  routine  used  to  send  Messages  to 
                        Exchanges.

        WAIT.ASM      - A routine to produce the Task 'Wait  for 
                        Message' function.

        MISC.ASM      - Contains miscellaneous procedures used by 
                        WAIT and by SEND.

        UNDEL.ASM     - A routine used to remove a Task from the 
                        Delay List.



     4/The Following Relocatable Code Files

        MTASK.REL   - A  File containing the  Relocatable  Code 
                         for all of MTASK except for the modules 
                         listed  below.  This file is a 'Library' 
                         file  and is composed of  the  following 
                         .REL files in this order :-
                         MNPROG.REL
                         DISPATCH.REL
                         CASETASK.REL
                         ACTDEL.REL
                         ACTIVATE.REL
                         DECDEL.REL
                         UNDEL.REL
                         SEND.REL
                         WAIT.REL
                         MISC.REL                         

        RUN8080.REL  - The  Relocatable Code File generated  from 
                         RUNTASK.MAC for use with 8080 CPUs.
        RUN8085.REL  - The  Relocatable Code File generated  from 
                         RUNTASK.MAC for use with 8085 CPUs.
        RUNZ80.REL   - The  Relocatable Code File generated  from 
                         RUNTASK.MAC for use with Z80 CPUs.

        GLDATA.REL    - The  Relocatable  Code File for  the  RAM 
                         areas used by MTASK and as Task stacks.







** The following modules of MTASK contain a parameter TOTALTASKS 
which sets the number of Tasks to be used. 
     MNPROG.MAC
     RUNTASK.MAC
     GLDATA.MAC
The above relocatable code files have been assembled for use with 
10 Tasks. If a different number of Tasks are required, then these 
modules  should  be  reassembled with the  appropriate  value  of 
TOTALTASKS, up to a maximum of 16. **





 7/ Generation of Machine Code
     Tasks  should  be written and  Assembled,  or  Compiled,  as 
Relocatable Code files following the conventions described above. 
The  same should be done for any code necessary to vector  Resets 
and to service Interrupts.  The Relocatable Code files  generated 
in  doing  this  should  then  be Linked  and  Located  with  the 
following files from the MTASK disc.

     1/ MNPROG.REL *

     2/ MTASK.REL

     3/ RUN8080.REL *
        or
        RUN8085.REL *
        or
        RUNZ80.REL *
        (The  File  appropriate to the CPU in the  Target  System 
         should be used)

     4/ GLDATA.REL *

     The resulting Machine Code will then be a combination of the 
Task software and the Operating System.
     Modules  marked with a '*' on the list above contain code for  up 
to  10 Tasks.  If a different number of Tasks are required,  then  the 
Assembly  Source  code  in each module should  be  modified  and  then 
reassembled.
     Note that RUN8080,  RUN8085 and RUNZ80 are derived from  RUNTASK, 
with different settings of the 'CPU' parameter.