OPT: A Three Pass Optimiser for Small C


          Opt is a simple optimiser which improves the execution speed of the 
          assembler output of the Z80 Small C compiler.  It normally gives a net 
          reduction in the size of the assembled program.

          To call the optimiser use a command of the form:

              opt filename

          Opt assumes that the file has the extension .ZSM and produces its output 
          in FILENAME.OPT.  Note that after optimisation FILENAME.ZSM contains the 
          output of the second optimiser pass, not the original assembly language 
          code.

          Using the optimiser on a variety of programs such as itself, the Z80 
          Small C compiler and a number of utilities has been found to give an 
          improvement in run time of 15-20%.  The resulting programs are also 
          slightly smaller.

          The following optimisations are applied.  The left-hand column gives the 
          original code, the optimised code is on the right.


          1.1) Negative constant


                  LD HL,<number>                  LD HL,0-<number>
                  CALL ccneg


              This avoids a particular stupidity of the Small C compiler, which 
              loads the absolute value of a negative constant and then negates it 
              rather than using the assembler to do the negating.  Saves 3 bytes.



          1.2) Double constant


                  LD HL,<number>                  LD HL,2*<number>
                  ADD HL,HL


              A further stupidity of the assembler is that it calculates constant 
              array offsets at run-time rather than at compile time.  Here we use 
              the assembler to do the sum for us.  Saves 1 byte.










                                           -  1  -








          1.3) Push and pop around LD HL


                  PUSH HL                         EX DE,HL
                  LD HL,<anything>                LD HL,<anything>
                  POP DE


              The compiler tends to load everything through the HL register pair 
              and get things into DE as an afterthought.  The above example is 
              better accomplished by exchanging the DE and HL registers.  The 
              previous contents of DE are lost in both the above fragments.  Saves 
              1 byte.



          1.4) Zero subscript


                  EX DE,HL                        LD D,H
                  LD HL,<0 or 2*0>                LD E,L
                  ADD HL,DE


              The above construct is frequently used to find the address of the 
              first element of an array.  There is no reason to suppose that the 
              new contents of DE (the base address of the array) will ever be 
              used, but I put them there anyway, just in case.  Saves 3 bytes.



          1.5) One subscript


                  EX DE,HL                        LD D,H
                  LD HL,1                         LD E,L
                  ADD HL,DE                       INC HL


              This construct is used to find the address of the second element of 
              a character array (with a constant index 1).  It's quicker just to 
              increment the base address.  Saves 2 bytes.



          1.6) Two subscript


                  EX DE,HL                        LD D,H
                  LD HL,<2 or 2*1>                LD E,L
                  ADD HL,DE                       INC HL
                                                  INC HL


              Constant subscripts of 2 are improved by the above substitution.  
              Saves 1 byte.


                                           -  2  -








          1.7) Fetch integer from top of stack


                  LD HL,0                         POP HL
                  ADD HL,SP                       PUSH HL
                  CALL ccgint


              Local variables in Small C are kept on the stack and fetched by 
              adding an offset to the stack pointer to get an address from which 
              the value is fetched.  If the required variable is at the top of the 
              stack it is quicker to pop it off.  Note that this is the fastest 
              way of fetching an integer, so the most frequently used variable in 
              a routine should be the last one to be defined.  Saves 5 bytes.



          1.8) Fetch second top integer from stack


                  LD HL,2                         POP BC
                  ADD HL,SP                       POP HL
                  CALL ccgint                     PUSH HL
                                                  PUSH BC


              This is similar to 1.7).  The BC register does not seem to be used 
              for much in the Small C compiler, so it's safe to trample all over 
              it.  Saves 3 bytes.



          2.1) Double EX DE,HL


                  EX DE,HL                        <nothing>
                  EX DE,HL


              Obvious, isn't it?  Save 2 bytes



          2.2) DE <- HL followed by EX DE,HL


                  LD D,H                          LD D,H
                  LD E,L                          LD E,L
                  EX DE,HL


              If DE and HL contain the same thing there's no point in swapping 
              them.  Saves 1 byte.





                                           -  3  -








          2.3) DE <- HL followed by LD HL


                  LD D,H                          EX DE,HL
                  LD E,L                          LD HL,<anything>
                  LD HL,<anything>


              Loading DE from HL and then overwriting HL is the same as swapping 
              DE and HL and overwriting HL.  You still lose what used to be in DE.  
              Saves 1 byte.



          2.4) Expand ccpchar


                  CALL ccpchar                    LD A,L
                                                  LD (DE),A


              The run-time routine to store a character from HL to the address 
              pointed to by DE is only two bytes long - shorter than a CALL to it.  
              Saves 1 byte.



          2.5) Expand ccgint to DE


                  CALL ccgint                     LD E,(HL)
                  EX DE,HL                        INC HL
                  LD HL,<anything>                LD D,(HL)
                                                  LD HL,<anything>


              The run-time routine ccgint fetches the integer pointed to by HL and 
              puts it in HL.  If a call to ccgint if followed by a swap and load 
              to HL it is equivalent to loading the integer pointed to by HL 
              straight into DE.  Saves 1 byte.



          2.6) Expand ccgint


                  CALL ccgint                     LD A,(HL)
                                                  INC HL
                                                  LD H,(HL)
                                                  LD L,A


              The run-time routine ccgint on its own can be expanded to the above 
              in-line code.  Uses 1 extra byte.




                                           -  4  -








          2.7) Expand ccpint


                  CALL ccpint                     LD A,L
                                                  LD (DE),A
                                                  INC DE
                                                  LD A,H
                                                  LD (DE),A


              The run-time routine ccpint stores the integer in HL at the address 
              in DE.  This can be expanded to in-line code.  Uses 2 extra bytes.



          2.8) Expand ccgchar to DE


                  CALL ccgchar                    LD A,(HL)
                  EX DE,HL                        LD E,A
                  LD HL,<anything>                RLCA
                                                  SBC A,A
                                                  LD D,A
                                                  LD HL,<anything>


              The run-time routine ccgchar fetches and sign extends into HL a 
              character from the address pointed to by HL.  If a call to ccgchar 
              is follwed by a swap and load to HL it is equivalent to a load 
              directly to DE.  Uses 1 extra byte.



          2.9) Expand ccgchar


                  CALL ccgchar                    LD A,(HL)
                                                  LD L,A
                                                  RLCA
                                                  SBC A,A
                                                  LD H,A


              The run-time routine ccgchar on its own can be expanded to in-line 
              code.  Uses 2 extra bytes.













                                           -  5  -








          3.1) LD HL; EX: LD HL  ->  LD DE; LD HL


                  LD HL,<thing>                   LD DE,<thing>
                  EX DE,HL                        LD HL,<thing2>
                  LD HL,<thing2>


              This another case where the compiler loads things into DE through 
              HL.  It's quicker to load directly into DE, unless <thing> is an 
              explicit memory address.  Saves 1 byte.



          3.2) JZ around unconditional jump


                  JP Z,<where>                    JP NZ,<else>
                  JP <else>                where:
           where:


              A conditional jump around an unconditional jump is the same as a 
              jump to the destination of the unconditional jump, but with the 
              condition reversed.  (The corresponding case for JNZ does not seem 
              to occur in Small C output and is not tested for.)  Saves 3 bytes.



          3.3) Store followed by load


                  LD <x>,<y>                      LD <x>,<y>
                  LD <y>,<x>


              After storing <y> in <x> there is no need to load <y> from <x>.  The 
              number of bytes saved depends on the particular LD instructions.  It 
              is either one or three.  For accounting purposes the optimiser 
              program assumes a saving of 2 bytes.


















                                           -  6  -