If you are interested in making your computer talk,
you should consider the SP0256-AL2.   Radio Shack sells the
chip for $12.95 and the total project should be less than
$25 and 2 hours of construction time.   The SP0256-AL2 gener-
ates allophones, basic word fragments.   Using combinations
of these 59 allophones, an unlimited, if somewhat mechanical
sounding, speech can be created.   Allophones are very frugal
with the memory, only 100 bits per second.  You could hold an
hour of speech in 50k bytes!

	Requirements:

	7 output lines   6 data, ald* (active low write strobe)
	1 input line     lrq* (active low busy signal)
	gnd
	+5v		 power supply

	parts list

	sp0256-al2		(Radio Shack #276-1784)
	lm386			audio amp, RS#276-1731
	3.12 mhz crystal 	(I used a 3 mhz crystal)
	speaker
	10k petentiometer	volume control
	misc. capacitors,
	resistors, sockets,
	protoboard

	The 18 pages of documentation are supplied by Radio
Shack.   Their circuit contains a number of errors.

1) unlabeled audio amp - lm386
2) '-5Y' should be '+5V'
3) A7, A8 should/can be grounded
4) PIC1665A could read 'any ttl compatible parallel computer
	port'
5) sby reset can be tied to reset
6) the discrete components between the sp0256 and the pic1665a
	can be eliminated except for the 100k resistor connected
	between the reset pin and +5v ('-5Y') and the .01uf
	cap between the reset pin and ground.   This eliminates
	2 transistors, 2 diodes, 4 resistors and 1 capacitor.

					good luck


thought for the day:  I expect speech synthesis to become very
important.   The two most cost effective devices for presenting
information are the crt and the speech processors.   One device
was developed before the transistor and the other is the stuff
of science fiction.