RM80 V2.0 User's Guide
 
   RM80 is a PROM-resident monitor for an 8080 (or Z80) system. It
supports one console, one modem, and two cassette decks interfaced
with a Tarbell Tape Interface, with relays. There are four main 
groups of commands:
 
     1) The hex monitor (edit memory in hex or ASCII)
     2) Standard Tarbell driver (read/write standard tapes)
     3) SDC Format tape driver (read/write RM80 tapes)
     4) Communications executive (allow link to remote CPU)
 
   All data entered from the console has the following editing
facilities available before hitting the CR key:
 
     1) CTRL-U will abort the current line
     2) DEL (RUBOUT) will discard the previous character,
        and echo it to the console.
 
   Memory is allocated as follows (in the 24K version):
 
     0000-57FF   User program and buffer area
     5800-5BFF   Default system tape buffer
     5900-590A   Default system filename buffer
     590B-590B   Tape unit number buffer
     590C-590C   Physical record number buffer
     590E-5C8D   System input buffer
     5C8E-5CCD   System stack
     C000-CBFF   3K PROM containing RM80
 
   Once a program has been loaded in, and execution begun, assuming
the stack pointer has the same value as when execution began, a
simple RET will return you to RM80. At any point, a jump to location
C000 will restart RM80.
 
   The commands are all in the same format:
 
     <KEYWORD> <BLANKS> <PARAM> <BLANKS> <PARAM>
 
<KEYWORD> - is an up to 5 character word in the list of commands
<BLANKS>  - is a string of one or more blanks
<PARAM>   - is an up to 4 digit hex number
 
   Some commands will require further data before execution. These
will prompt the user for that data. The MOVE command requires a
destination address, so a valid response to the 'TO?' prompt is a
<PARAM> as above. Anytime the prompt 'FILENAME?' occurs, any legal
CP/M filename may be typed. A CP/M filename is of the form
 
     <name>   or   <name>.<type>
 
<name> is any group of up to 8 ASCII characters
<type> is any string of up to 3 ASCII characters
 
Standard CP/M file types are as follows:
 
     ASM - Assembler source file
     HEX - Intel hex object file
     COM - Memory image object file (loads at 100H)
     BAS - BASIC source file
     FOR - FORTRAN source file 
 
************************************************************************
 
RM80 Hex Monitor Commands
 
DUMP fwa lwa
 
     Dump memory in hex and ASCII starting at fwa, ending at lwa.
     Control characters are printed as periods. Dumping may be
     aborted at any time by typing any character.
 
TYPE fwa lwa
 
     Type memory in ASCII starting at fwa ending at lwa. All 
     control characters print as themselves (exercise caution).
 
ENTER fwa
 
     Allow user to enter memory contents in Hex. A four digit
     prompt 'xxxx?' will be printed at the start of each input
     line, to show the user where the first byte typed on that
     line will be loaded into memory. The user may return to RM80
     by typing an empty line (CR right after prompt).
 
MOVE fwa lwa
 
     Move block of memory starting at fwa ending at lwa to the
     area starting at the destination address (supplied in response
     to the TO? prompt. Blocks may overlap either way.
 
FILL fwa lwa
 
     Fill memory with constant supplied in response to 'WITH?'
     prompt, starting at fwa ending at lwa.
 
GO fwa
 
     Jump to address fwa. Default is 100H.
 
************************************************************************
 
Standard Tarbell Tape Handler Commands
 
STORE fwa lwa
 
     Store memory starting at fwa ending at lwa to tape in Tarbell
     standard format (data bytes then checksum).
 
FETCH fwa lwa
 
     Fetch standard Tarbell file into memory starting at fwa, and
     ending at lwa. Note that the file size (lwa-fwa+1) must be
     the same as the file size used in creating the file with
     STORE (or equivalent). The message 'CHECKSUM ERROR' indicates
     that data was lost (or user specified fwa and lwa wrong for
     this file).
 
CHECK fwa lwa
 
     Same as FETCH, but data is not loaded into memory . Good
     for checking quality of files written with STORE.
 
UNIT n
 
     Sets unit number for above commands (default = 1)
 
Notes on using cassette tapes with RM80:
 
     Before writing data to tape, the user should put the recorder
     into RECORD and allow a reasonable leader (count to 10). The
     REMOTE cable (motor control) may be re-inserted and the WRITE
     command issued. Further files may be written without additional
     leader. When reading tapes, the cassette may be positioned
     any length of leader (and/or blank tape) before the actual data.
     Port FF lights will display data being written to or read from
     cassette tape.
 
************************************************************************
 
SDC Tape Handler commands
 
WRITE n
 
     Writes n pages (256 bytes each) starting at 100H, to tape
     in SDC format. A filename will be requested with the 'FILENAME?'
     prompt. When the entire file is written, RM80 will respond with
     'xxxx BYTES WRITTEN' and then provide a command prompt.
 
WRITE fwa lwa
 
     As above, but the user nay specify any addresses.
 
READ fwa
 
     Read next SDC format file into memory starting at fwa.
     Reading may be aborted at any time by typing any character.
     Default fwa is 100H. Header info is printed as each
     record is read into memory.
 
LOAD 
 
     Load Intel Hex Object Format file in SDC Format into memory
     at addresses specified in object file. Loading may be aborted
     at any point by typing any character.
 
DUMP 
   
     Dump next SDC format file to console in Hex and ASCII.
     Header info is printed as each record is read. Conventions are
     the same as the memory dump command. Dumping may be aborted
     as usual.
 
TYPE
 
     Type next SDC format file to console in ASCII. Conventions are
     the same as the memory TYPE command. Typing may be aborted
     as usual.
 
SCAN
 
     Read SDC tape and print header info until interrupted by any
     character from the console.
 
UNIT n
 
     Select tape unit for all tape commands until respecified.
 
Header info when printed, is in the following form: 
 
     NAME = aaaaaaaa  TYPE = aaa  SIZE = dddd  PRN = dd  CRC = ssss
 
     aa...aa  is an ASCII character string
     dd...dd  is a Hex number
     ss...ss  is the string 'GOOD' or 'BAD'
 
 
The SDC physical record format is as follows:
 
     FIRST   NUMBER     NAME     CONTENTS
 
     BYTE    OF BYTES   
 
      00      01        SOH      ASCII Start Of Header
      01      08        FN       ASCII file name
      09      03        FT       ASCII file type
      12      01        PRN      Integer Physical record number
      13      02        PRS      Integer Physical record size (HI/LO)
      14      01        STX      ASCII Start Of Text
      15      prs       DATA     Data Bytes (normally 1024 of them)
      15+prs  01        ETX      ASCII End Of Text
      16+prs  02        CRC      Integer Cyclic Redundancy Checksum (HI/LO)
 
************************************************************************
 
Communications Link Executive
 
LINK
 
     Establish communications link with remote computer. Characters from
     console are sent to the modem. Characters from the modem are 
     typed on the console. Various control characters allow tape files
     to be sent or received, or downloaded. To return to RM80 at any 
     time, type CTRL-X. This will not break the link, which may be
     re-entered by typing LINK again from RM80.
 
          CTRL-O     Enable Object File Loader
          CTRL-N     Disable Object File Loader
          CTRL-R     Enable Text File Loader
          CTRL-Q     Disable Text File Loader and write to tape
          CTRL-X     Return to monitor
 
************************************************************************