***************************************************************************
** COPYRIGHT (C) MASSACHUSETTS INSTITUTE OF TECHNOLOGY AND HARVARD       **
** UNIVERSITY, BIOMEDICAL ENGINEERING CENTER 1977.  ALL RIGHTS RESERVED. **
***************************************************************************

THE STOIC ASSEMBLER FOR THE INTEL 8080
J. SACHS 2/2/77

CODE DEFINITIONS

	STOIC PROVIDES THE USER WITH A MEANS OF DEFINING
A NEW WORD IN TERMS OF THE ASSEMBLY LANGUAGE FOR THE
PARTICULAR MACHINE ON WHICH IT IS EXECUTING.  THIS IS
PROVIDED BY THE ASSEMBLER AND THE CODE DEFINITION.

'NAME CODE< A1 A2 ... >

	HERE A1, A2, ... ARE WORDS DEFINED WITHIN THE
ASSEMBLER AND "NAME" IS THE NAME OF THE WORD BEING
DEFINED.  AS WITH EVERYTHING ELSE IN STOIC, THE
ASSEMBLER USES REVERSE POLISH NOTATION, GIVING THE
ADDRESSES AND ACCUMULATOR SPECIFIERS BEFORE THE
OPCODE.

	THE ASSEMBLER WORDS DO NOT EXECUTE MACHINE
INSTRUCTIONS DIRECTLY; THEY MERELY CAUSE INSTRUCTIONS
TO BE ASSEMBLED ONTO THE END OF THE DICTIONARY.  THUS
BEFORE MACHINE LANGUAGE INSTRUCTIONS CAN BE EXECUTED
FROM THE KEYBOARD THEY MUST FIRST BE ASSEMBLED INTO A
CODE DEFINITION.

ADDRESSES

	AN ADDRESS IS NORMALLY THE NAME OF A WORD, OR AN
ABSOLUTE LOCATION.  AN ADDRESS MAY HOWEVER BE ANY EXPRESSION
WHICH EVALUATES TO AN INTEGER.

ACCUMULATORS

	WITHIN THE ASSEMBLER, THE NORMAL INTEL ACCUMULATOR
NAMES (A,B,C,D,E,H,L,M,SP,PSW) ARE USED TO SPECIFY 8080
REGISTERS.

INSTRUCTIONS WITHOUT ADDRESS OR ACCUMULATOR

	INTEL		STOIC

	NOP		NOP,
	HLT		HLT,
	RLC		RLC,
	RRC		RRC,
	RAL		RAL,
	RAR		RAR,
	DAA		DAA,
	CMA		CMA,
	STC		STC,
	CMC		CMC,
	RET		RET,
	RNZ		RNZ,
	RZ		RZ,
	RNC		RNC,
	RC		RC,
	RPO		RPO,
	RPE		RPE,
	RP		RP,
	RM		RM,
	XTHL		XTHL,
	PCHL		PCHL,
	SPHL		SPHL,
	XCHG		XCHG,
	DI		DI,
	EI		EI,


INSTRUCTIONS WITH ACCUMULATOR

	INTEL		STOIC

	RST N		N   RST,
	DAD ACC		ACC DAD,
	DCX ACC		ACC DCX,
	STAX ACC	ACC STAX,
	LDAX ACC	ACC LDAX,
	INR ACC		ACC INR,
	DCR ACC		ACC DCR,
	POP ACC		ACC POP,
	PUSH ACC	ACC PUSH,
	INX ACC		ACC INX,


INSTRUCTIONS WITH AN ACCUMULATOR AND A 16-BIT VALUE

	INTEL		STOIC

	LXI ACC,VALUE	VALUE ACC LXI,


INSTRUCTIONS WITH TWO ACCUMULATORS

	INTEL		STOIC

	MOV AC1,AC2	AC2 AC1 MOV,

INSTRUCTIONS WITH AN ADDRESS

	INTEL		STOIC

	SHLD ADR	ADR SHLD,
	LHLD ADR	ADR LHLD,
	STA ADR		ADR STA,
	LDA ADR		ADR LDA,
	JMP ADR		ADR JMP,
	CALL ADR	ADR CALL,
	JNZ ADR		ADR JNZ,
	JZ ADR		ADR JZ,
	JNC ADR		ADR JNC,
	JC ADR		ADR JC,
	JPO ADR		ADR JPO,
	JPE ADR		ADR JPE,
	JP ADR		ADR JP,
	JM ADR		ADR JM,
	CNZ ADR		ADR CNZ,
	CZ ADR		ADR CZ,
	CNC ADR		ADR CNC,
	CC ADR		ADR CC,
	CPO ADR		ADR CPO,
	CPE ADR		ADR CPE,
	CP ADR		ADR CP,
	CM ADR		ADR CM,
	

INSTRUCTIONS WITH ONE ACCUMULATOR AND ONE 8-BIT VALUE

	INTEL		STOIC

	MVI ACC,VALUE	VALUE ACC MVI,


INSTRUCTIONS WITH ONE ACCUMULATOR

	INTEL		STOIC

	ADD ACC		ACC ADD,
	ADC ACC		ACC ADC,
	SUB ACC		ACC SUB,
	SBB ACC		ACC SBB,
	ANA ACC		ACC ANA,
	XRA ACC		ACC XRA,
	ORA ACC		ACC ORA,
	CMP ACC		ACC CMP,

INSTRUCTIONS WITH ONE 8-BIT VALUE

	INTEL		STOIC

	ADI VALUE	VALUE ADI,	
	ACI VALUE	VALUE ACI,
	SUI VALUE	VALUE SUI,
	SBI VALUE	VALUE SBI,
	ANI VALUE	VALUE ANI,
	XRI VALUE	VALUE XRI,
	ORI VALUE	VALUE ORI,
	CPI VALUE	VALUE CPI,
	OUT N		N OUT,
	IN N		N IN,

EXAMPLES:

STOIC ASSEMBLER		INTEL ASSEMBLER

HLT,			HLT
0 H LXI,		LXI H,0
A B MOV,		MOV B,A
M CPI,			CPI M
H DCX,			DCX H
. JMP,			JMP $

FORWARD AND BACKWARD JUMPS

	SINCE THE STOIC ASSEMBLER HAS NO LABELS, SPECIAL
ASSEMBLER WORDS ARE USED TO CONTROL FORWARD AND BACKWARD
JUMPS.

BACKWARD JUMPS ARE ACCOMPLISHED USING THE FOLLOWING CONSTRUCTION:

	.  ...  JMP,

	"." IS USED TO SAVE THE CURRENT LOCATION ON THE
	STACK; THE FOLLOWING INSTRUCTIONS ARE ASSEMBLED
	NORMALLY, AND THE "JMP," ASSEMBLES A JUMP BACK
	TO THE SAVED LOCATION COUNTER VALUE.  A CONDITIONAL
	JUMP COULD JUST AS EASILY BE USED.  SUCH BACKWARD
	JUMPS MAY BE NESTED FOR MULTI-LEVEL LOOPS.

FORWARD JUMPS ARE ASSEMBLED USING THE FOLLOWING WORDS:

IF,	UNCONDITIONAL FORWARD JUMP
IFNZ,	FORWARD JUMP IF NON-ZERO
IFZ,	FORWARD JUMP IF ZERO
IFNC,	FORWARD JUMP IF NO CARRY
IFC,	FORWARD JUMP IF CARRY
IFPO,	FORWARD JUMP IF PARITY ODD
IFPE,	FORWARD JUMP IF PARITY EVEN
IFP,	FORWARD JUMP IF PLUS
IFM,	FORWARD JUMP IF MINUS

THEN,	SUPPLY TARGET FOR FORWARD JUMP

ELSE,	GENERATE AN UNCOUNDITIONAL FORWARD JUMP
	AND SUPPLY TARGET FOR PRECEDING FORWARD
	JUMP.

THE NORMAL CONSTRUCTION FOR A FORWARD JUMP IS:

	IF,  ...  THEN,

THE "IF," ASSEMBLES A "0 JMP," AND SAVES ON THE STACK THE
ADDRESS OF THE 0.  "THEN," STORES THE VALUE OF THE CURRENT
LOCATION COUNTER (.) AT THE ADDRESS ON THE TOP OF THE
STACK, THUS COMPLETING THE ASSEMBLY OF THE JMP INSTRUCTION.
FORWARD JUMPS MAY BE NESTED IN EXACTLY THE SAME WAY AS
BACKWARD JUMPS.

"ELSE," IS USED AS FOLLOWS:

	IF,  ...  ELSE,  ...  THEN,

	HERE, THE "IF," GENERATES A FORWARD JUMP TO THE
INSTRUCTION IMMEDIATELY FOLLOWING THE "ELSE,".  THE "ELSE,"
IN TURN CAUSES AN UNCONDITIONAL JUMP TO BE ASSEMBLED TO THE
INSTRUCTION FOLLOWING THE "THEN,".  THE "IF," COULD, OF
COURSE, BE A CONDITIONAL JUMP.


EXAMPLES:

	'TEST CODE<  H POP,  H A MOV,  IFP,  -1 H LXI,  ELSE,
	  0 H LXI,  THEN,  PUSH JMP,  >

	THIS DEFINES A WORD CALLED "TEST" WHICH, IF
	THE TOP OF THE STACK IS POSITIVE, PUSHES A 0,
	OTHERWISE PUSHES A -1.  THE GENERATED CODE IS:

	POP H
	MOV A,H
	JP L1
	LXI H,-1
	JMP L2
L1:	LXI H,0
L2:	JMP PUSH


	'WAIT CODE<  H POP,  .  H DCX,  H A MOV,  L ORA,  JNZ,
	  NEXT JMP,  >

	THE WORD "WAIT" IS DEFINED WHICH COUNTS DOWN ITS
	ARGUMENT AND RETURNS WHEN THE RESULT IS 0.  THE
	GENERATED CODE IS:

	POP H
L1:	DCX H
	MOV A,H
	ORA L
	JNZ L1
	JMP NEXT


DEFINING SUBROUTINES

	SOMETIMES A BLOCK OF INSTRUCTIONS MUST BE EXECUTED FROM
SEVERAL DIFFERENT CODE DEFINITIONS; IN THIS CASE IT IS FREQUENTLY
EFFICIENT TO DEFINE A SUBROUTINE.  THIS IS DONE AS FOLLOWS:

	. ASSEMBLER<
	BODY OF SUBROUTINE
	>
	'SUBROUTINE-NAME CONSTANT

THE "." PUSHES ON THE STACK THE ADDRESS OF THE BEGINNING OF THE
SUBROUTINE, SUPPLYING THE VALUE FOR "CONSTANT".  "ASSEMBLER<"
ACTIVATES THE ASSEMBLER VOCABULARY; NOTE THAT IT MUST BE FOLLOWED
BY A CARRAIGE RETURN.  THE BODY OF THE SUBROUTINE FOLLOWS, WITH
RETURN INSTRUCTIONS INCLUDED.  FINALLY, ">" DE-ACTIVATES THE
ASSEMBLER VOCABULARY AND THE CONSTANT IS DEFINED.  SUBSEQUENTLY,
THE SUBROUTINE MAY BE INVOKED DIRECTLY BY:

	SUBROUTINE-NAME CALL,


ASSEMBLING STRINGS

	TO ASSEMBLE A STRING ONTO THE END OF THE DICTIONARY, THE
FOLLOWING TECHNIQUE IS USED:

	. "STRING" S,

THIS PUSHES A POINTER TO THE BEGINNING OF THE STRING ON THE STACK,
AND COPIES THE GIVEN STRING FROM THE COMPILE BUFFER ONTO THE END
OF THE DICTIONARY.


REPEATING INSTRUCTIONS

	INTERATION BRACKETS AND/OR DO LOOPS MAY BE USED WITHIN
THE ASSEMBLER TO PERFORM REPETITIVE ASSEMBLY:

	'DELAY CODE<  100 ( NOP, ) >

THIS ASSEMBLES A WORD "DELAY" WHICH EXECUTES 100 NOP'S.

	.  10 0 DO I , LOOP

THIS EXAMPLE LEAVES ON THE STACK THE ADDRESS OF THE BEGINNING OF
A TABLE OF NUMBERS FROM 0 TO RADIX - 1.


CONDITIONAL ASSEMBLY

	CONDITIONAL ASSEMBLY IS OBTAINED BY USING THE NORMAL STOIC
"IF", "ELSE", AND "THEN".  FOR EXAMPLE, SUPPOSE WE HAVE A VARIABLE
"TEST" WHICH THE USER WILL SET TO EITHER 0 OR -1:

	'PARAM CODE<  TEST @ IF 100 ELSE 200 THEN H LXI,  PUSH JMP,  >

HERE, THE CODE DEFINITION, "PARAM" IS DEFINED TO PUSH A 100 IF TEST
IS NON-ZERO, A 200 OTHERWISE.


MACROS

	ASSEMBLER MACROS ARE PROVIDED BY USING COLON DEFINITIONS
AS FOLLOWS:

	ASSEMBLER< DEFINITIONS
	'-HL, : H A MOV,  CMA,  A H MOV,  L A MOV,  CMA,  A L MOV,
		H INX,  ;
	> DEFINITIONS

THUS,

	'MINUS CODE<  H POP,  -HL,  PUSH JMP,  >

	DEFINES A WORD WHICH NEGATES THE TOP OF THE STACK.


LOCATIONS INTERNAL TO STOIC WHICH ARE AVAILABLE TO THE USER:

-HL CALL,	NEGATES (H,L)
HL 1+ CALL,	COMPLEMENTS (H,L)

-DE CALL,	NEGATES (D,E)
DE 1+ CALL,	COMPLEMENTS (D,E)

-BC CALL,	NEGATES (B,C)
BC 1+ CALL,	COMPLEMENTS (B,C)

-HLDE CALL,	NEGATES (H,L,D,E)

(TTI) CALL,	GET A CHARACTER FORM THE KEYBOARD;
		CHARACTER RETURNED IN A REGISTER.

(TTO) CALL,	TYPE A CHARACTER ON THE TERMINAL;
		CHARACTER PASSED IN A REGISTER.
		RETURN AUTOMATICALLY FOLLOWED BY LINE FEED.

(MSG) CALL,	TYPES A MESSAGE ON THE TERMINAL;
		POINTER TO STRING PASSED IN (H,L).

MUL CALL,	UNSIGNED MULTIPLY
SMUL CALL,	SIGNED MULTIPLY
		(H,L)*(D,E) -> (H,L,D,E)

DIV CALL,	UNSIGNED DIVIDE
SDIV CALL,	SIGNED DIVIDE
		(H,L,D,E)/(B,C) -> (H,L) REMAINDER; (D,E) QUOTIENT

(B,) CALL,	OUTPUT A REGISTER TO END OF DICTIONARY
(,) CALL,	OUTPUT (H,L) TO END OF DICTIONARY

ERROR JMP,	SIMULATES "STRING" ERR
		ADDRESS OF STRING IN (H,L).

(READ) CALL,	READ A BLOCK FROM MASS STORAGE DEVICE
(WRITE)	CALL,	WRITE A BLOCK TO MASS STORAGE DEVICE
		(H,L) = BLOCK #
		(D,E) = BUFFER ADDRESS
		ON RETURN, A = ERROR CODE (0 = OK)

(RBLOCK) CALL,	BLOCK # IN (D,E), BUFFER
(WBLOCK) CALL,	ADDRESS RETURNED IN (D,E).

T1		TEMPORARY #1
		9 ADDITIONAL 16-BIT TEMPORARIES FOLLOW


	IN MAKING A CODE DEFINITION OF HIS OWN, THE USER
SHOULD BE AWARE OF THE FOLLOWING FACTS:

1) THE PARAMETER STACK POINTER IS PASSED IN SP.  SP
   MUST CONTAIN THE STACK POINTER ON EXIT.

2) PARAMETERS ON THE STACK ARE AVAILABLE BY INDEXING OFF
   SP.  THE TOP OF THE STACK IS AT OFFSET 0, NEXT TO TOP
   AT OFFSET +2, ETC.

3) TEN TEMPORARIES, STARTING AT "T1" ARE AVAILABLE IF
   NECESSARY.

4) ALL CODE DEFINITIONS MUST EXIT BY JUMPING TO ONE OF
   THE FOLLOWING ADDRESSES IN THE STOIC INTERPRETER:

	NEXT	NORMAL TERMINATION

	PUSH	PUSH (H,L), JUMP TO NEXT

	DPUSH	PUSH (D,E), PUSH (H,L), JUMP TO NEXT

	PUSHD	PUSH (D,E), JUMP TO NEXT

	@PUSH	PUSH @(H,L), JUMP TO  NEXT

	0PUSH	PUSH 0, JUMP TO NEXT

	-1PUSH	PUSH -1, JUMP TO NEXT

5) A POINTER TO THE PARAMETER FIELD OF THE CURRENT WORD
   IS PASSED IN (D,E).  (D,E) NEED NOT BE PRESERVED.


EXAMPLES OF CODE DEFINITIONS:

	'+ CODE<  H POP,  D POP,  D DAD,  PUSH JMP,  >

	THE WORD "+" ADDS THE TOP TWO STACK ENTRIES
	AND LEAVES THE RESULT ON THE STACK.

	'ABS CODE<  H POP,  H A MOV,  A ORA,  IFP,
	  -HL CALL,  THEN,  PUSH JMP,  >

	THE WORD "ABS" REPLACES THE TOP OF THE STACK
	WITH ITS ABSOLUTE VALUE.


;CODE<

	THE WORD ";CODE<" IS USED TO DEFINE NEW CLASSES
OF WORDS.  "VARIABLE", "CONSTANT", AND "USER", FOR
EXAMPLE ARE DEFINED USING ";CODE<".  THE FORMAT FOR ITS
USE IS AS FOLLOWS:

	'NAME : ... ;CODE< ... >

	THE WORDS BETWEEN "NAME" AND ";CODE<" ARE IN
HIGHER LEVEL STOIC; THE WORDS BETWEEN ";CODE< AND ">"
ARE ASSEMBLER WORDS.

	WHEN EXECUTED, ";CODE<" OUTPUTS THE ADDRESS OF
"(;CODE<)" TO THE COMPILE BUFFER, TERMINATES THE CURRENT
COLON DEFINITION, AND PUSHES THE ADDRESS OF "ASSEMBLER<" ON
THE VOCABULARY STACK.

	THE NAMELESS DICTIONARY ENTRY "(;CODE<)"
SETS THE CODE ADDRESS WORD OF THE MOST RECENTLY
DEFINED WORD TO THE CONTENTS OF "I" + 2, AND POPS
"I" FROM THE RETURN STACK.

EXAMPLE:

	'VARIABLE : CONSTANT ;CODE< PUSHD JMP, >

	THIS IS THE DEFINITION OF "VARIABLE".  THE
	DICTIONARY ENTRY FOR "VARIABLE" THEN LOOKS
	AS FOLLOWS:

		<8>V
		AR
		IA
		LINK TO PREVIOUS ENTRY
		ADDRESS OF (:)
	VAR:	ADDRESS OF CONSTANT
		ADDRESS OF (;CODE<)
	(VAR):	JMP PUSHD

	NOW, SUPPOSE THAT X IS DEFINED AS FOLLOWS:

	20 'X VARAIBLE

	"VARIABLE" INVOKES "CONSTANT" WHICH BUILDS A
	DICTIONARY ENTRY CALLED "X", STORES THE
	VALUE "20" IN THE PARAMETER FIELD, AND SETS
	THE CODE ADDRESS WORD TO POINT TO MACHINE
	INSTRUCTIONS WHICH PUSH THE VALUE OF THE
	PARAMETER FIELD ON THE STACK.  ";CODE<" THEN
	OVERWRITES THE CODE ADDRESS WORD WITH THE
	ADDRESS OF (VAR).  THUS, THE RESULTANT
	DICTIONARY ENTRY FOR "X" IS:

		<1>X
		0
		0
		LINK TO PREVIOUS ENTRY
		(VAR)
	X:	20

	WHEN "X" IS IN TURN EXECUTED, CONTROL PASSES
	TO (VAR) VIA THE CODE ADDRESS WORD, WITH THE
	ADDRESS OF "X" IN (D,E), THE ADDRESS OF "X" IS
	PUSHED, AND CONTROL PASSES TO "NEXT".


;:

	";:" IS ANALOGOUS TO ";CODE<" EXCEPT THAT IT
USES HIGHER LEVEL STOIC TO DEFINE THE ACTION TAKEN
BY THE CLASS OF WORDS BEING DEFINED.  THE SYNTAX IS
AS FOLLOWS:

	'NAME : ... ;: ... ;

	HERE, BOTH SETS OF WORDS ARE IN HIGHER LEVEL
STOIC.

EXAMPLE:

	0> 'SQPRINT : ;: DUP * = ;
	0> 5 'X SQPRINT
	0> X
	25

	";:" IS MAINLY USEFUL IN DEFINING A NUMBER OF WORDS WHICH
DIFFER ONLY IN A SINGLE CONSTANT VALUE, E.G. ASSEMBLER WORDS WITH
DIFFERENT OPCODES.



***EOF***


ER OF WORDS WHICH
DIFFER ONLY IN A SINGLE CONSTANT VALUE, E.G. ASSEMBLER