TWO VDM CBIOS FRAGMENTS
                         R.C. Minnick
                            Box 306
                        Ouray, CO 81427
                               



      There are a couple features in my CBIOS which I find very
useful, and which might be of interest to others in the  CPMUG.
Rather than bore you with a complete CBIOS listing (it occupies
5K  of  EPROM plus the standard RAM), the two interesting parts
are shown below as code fragments.  

      The first is a VDM paging function which is added to  the
standard  VDM  software  driver.    In the code below, bit 0 of
IOCVDM stores the paging flag.  If  it  is  on,  the  VDM  will
display  16  lines  and  then pause until a CON: input.  If the
input is any character BUT a 'P', the process of stopping every
16 lines continues; if a 'P' is entered,  the  paging  flag  is
turned  off.   The code below does not show the TOGPG function,
since it is certain that you will do the job differently than I
have.  


; SCROLL SCREEN UP
SCRL:  LXI     H,BOTL  ;BEGINNING OF TEXT LINE
       PUSH    H
       LDA     IOCVDM
       ANI     1       ;0=PAG OFF
       XRI     1       ;0=PAG ON
       ORA     M       ;0= " & BOTL=0
       JNZ     $+6
       CALL    CHAR    ;ANY BUT P RESTARTS
       CPI     'P'
       PUSH    D
       CZ      TOGPG   ;P REMOVES PAGING
       POP     D
       MOV     A,M
       INR     M
       SUB     M
       LXI     B,0
       CALL    CLNA
       LXI     B,2040H ;B=SPACE, C=CTR=64
SCRL2: MOV     M,B     ;CLEAR BOTTOM LINE
       INR     L
       DCR     C
       JNZ     SCRL2
       POP     H
       MOV     A,M
       ANI     0FH
       MOV     M,A
; SET BOSL & BOTL IN SCROLL REGISTER
VDMOT: LDA     BOSL
       RLC
       RLC
       RLC
       RLC
       LXI     H,BOTL
       ORA     M
       OUT     VDMDEV  ;SCROLL REGISTER PORT
       RET





      In the second code fragment, a hard copy is  produced  of
the  information  on the VDM screen.  That is, the current CON:
display is sent to LST: without  any  disturbance  (except  the
appearance  of  the prompt character--which is later erased) to
CON:.  This fragment is actually an addition to code  published
by  Dan  S.  Parker  in DDJ [V2 N4 P10, April 1977].  The cited
code has been improved by the suppresion of blanks to the right
of non-blank text on each line.  My  code  below  is  not  very
elegant,  but it works.  Furthermore, I find the feature useful
to have.  


;
; HARD COPY OF VIDEO SCREEN TO DURA
;
HCOPY: LDA     BOTL    ;VDM BEG. OF TEXT LINE
       LXI     H,VDMBASE       ;BOTTOM VDM RAM
       LXI     D,40H   ;CHAR/LINE (16-BIT)
HCOPY1:DAD     D
       DCR     A
       JNZ     HCOPY1  ;HL NOT AT START OF TEXT
       MVI     E,11H   ;E=1+LINES/SCREEN
NXTLN: MVI     C,CR
       CALL    LIST    ;DO CRET
       MOV     A,H
       CPI     0D0H    ;STILL WITHIN VDM RAM?
       JNZ     $+6     ;YES
       LXI     H,VDMBASE       ;WRAP-AROUND
       DCR     E       ;LINE COUNT
       JNZ     HCOPY3  ;NOT DONE
       RET
HCOPY3:MVI     D,40H   ;RESET CHAR COUNT
       MVI     C,3FH   ;LOCAL CTR
       PUSH    H       ;SAVE BEG. OF LINE PTR.
       MOV     A,L
       ADD     C
       MOV     L,A     ;HL POINTS TO END OF LINE
HCOPY5:MOV    A,M
       CPI     20H     ;SPACE?
       JNZ     HCOPY4  ;NO, EXIT THIS CALC.
       DCR     D
       DCX     H
       DCR     C       ;TO KEEP ON THIS LINE
       JNZ     HCOPY5  ;CONTINUE REMOVING SPACES
HCOPY4:POP     H       ;RESTORE BEG. OF LINE PTR.
HCOPY2:PUSH    H       ;SAVE BEG. OF LINE
       MOV     C,M     ;DATUM
       CALL    LIST    ;PRINT IT
       INX     H
       DCR     D       ;CHAR COUNT
       JNZ     HCOPY2+1        ;CONTINUE
       POP     H       ;BEG. OF THIS LINE
       LXI     B,40H
       DAD     B       ;HL NOT POINTS TO NEXT LINE
       JMP     NXTLN