CP/M DISK I/O PACKAGE

		VERSION 2.X   08/17/78

	   COMPATIBLE WITH MICROSOFT FORTRAN

				DICK CURTISS
				843 NW 54TH
				SEATTLE, WASHINGTON
						98107
				(206) 784 8018

  FORTRAN USAGE:
	INTEGER  DOPEN , DCLOSE , GCLOSE
	INTEGER  BREAD , BWRITE
	INTEGER  LREAD , LWRITE
	INTEGER  DATABYTE , LINE(40) , STATUS
	INTEGER  MCOUNT , ACOUNT
	INTEGER  FILETABLE(83) , FILENAME(6) 
 
	DATA     FILETABLE(1) , FILETABLE(2) / 0 , 'XX' /
 
	DATA     FILENAME / 'B:' , 'FN' , 'AM' , 'E.' , 'TX' , 'T ' /

    OPEN DISK FILE:
						 1
	STATUS = DOPEN  ( FILETABLE , FILENAME , 2 )
						 3
			1 READ ACCESS
			2 WRITE ACCESS - NO DELETE
			3 WRITE ACCESS WITH DELETE
	IF ( STATUS .NE. 0 ) GO TO ...... ERROR

    CLOSE DISK FILE:
	STATUS = DCLOSE ( FILETABLE )
	IF ( STATUS .NE. 0 ) GO TO ...... ERROR

    CLOSE ALL OPEN FILES
	STATUS = GCLOSE ( 0 )

    READ BYTE FROM DISK FILE:
	DATABYTE = 0
	STATUS = BREAD ( FILETABLE , DATABYTE )
	IF ( STATUS .EQ. 255 ) GO TO ...... END OF FILE
	IF ( STATUS .NE.  0  ) GO TO ...... ERROR

    WRITE BYTE TO DISK FILE:
	STATUS = BWRITE ( FILETABLE , DATABYTE )
	IF ( STATUS .EQ. 255 ) GO TO ...... END OF MEDIUM
	IF ( STATUS .NE.  0  ) GO TO ...... ERROR
 
    READ LINE FROM DISK FILE:
	MCOUNT = 80
	STATUS = LREAD ( FILETABLE , LINE , MCOUNT , ACOUNT )
	IF ( STATUS .EQ. 255 ) GO TO ...... END OF FILE
	IF ( STATUS .NE.  0  ) GO TO ...... ERROR

    WRITE LINE TO DISK FILE:
	ACOUNT = 80
	STATUS = LWRITE ( FILETABLE , LINE , ACOUNT )
	IF ( STATUS .EQ. 255 ) GO TO ...... END OF MEDIUM
	IF ( STATUS .NE.  0  ) GO TO ...... ERROR


	NOTES:
	  1. EACH FILE MUST HAVE ITS OWN "FILETABLE" OF
	     165 BYTES.

	  2. THE "FILETABLE" SHOULD NOT BE ALTERED BY THE USER
	     EXCEPT DURING PROGRAM INITIALIZATION WHEN THE FIRST
	     2 BYTES SHOULD BE SET TO ZERO AND THE FOURTH BYTE
	     SET TO SOME CHARACTER WHICH WILL BE DISPLAYED IN
	     ANY ERROR MESSAGES.

	  3. "FILENAME" IS A CHARACTER STRING REPRESENTING A
	     VALID CP/M FILE NAME WITH OPTIONAL DISK SELECT AND
	     FILE TYPE.  LEADING SPACES ARE IGNORED AND THE
	     MAY BE TERMINATED BY A SPACE, CARRIAGE RETURN,
	     ",", OR "=".  STORAGE MUST BE A CONTIGUOUS STRING
	     OF BYTES - NOT ONE CHARACTER PER INTEGER WORD.

	  4. TWO OPTIONS ARE AVAILABLE FOR WRITE ACCESS.  IF
	     THE FILE ALREADY EXISTS AND THE ACCESS CODE IS 2,
	     AN ERROR WILL RESULT AND THE FILE WILL NOT BE
	     OPENED.  IF THE ACCESS CODE IS 3, AN EXISTING FILE
	     WILL BE DELETED BEFORE OPEN.

	  5. OPERATION "STATUS"
		0	NORMAL
		1-254	ERROR CODE - NOT PRESENTLY SPECIFIED
		255	END OF FILE ON READ
		255	END OF MEDIUM ON WRITE

	  6. LREAD  --
		CARRIAGE RETURN IS END OF LINE
		LINE FEED, NULL AND RUBBOUT ARE IGNORED
		CONTROL Z IS END OF FILE
		ASCII PARITY BIT IS REMOVED

	  7. LWRITE  --
		LINES ARE AUTOMATICALLY TERMINATED BY
		  CARRIAGE RETURN - LINE FEED

	  8. "DATABYTE" STORAGE FOR READ AND WRITE IS A SINGLE
	     BYTE AS FAR AS THE ROUTINES ARE CONCERNED.  PRIOR
	     TO READ THE MOST SIGNIFICANT BYTE OF "DATABYTE"
	     SHOULD BE SET TO ZERO IF THE DATA IS TO BE USED
	     IN INTEGER COMPARES, ETC.

	  9. "MCOUNT" AND "ACOUNT" ARE SINGLE BYTE INTEGERS
	     AS FAR AS THE ROUTINES ARE CONCERNED.



  ASSEMBLER USAGE:

	FILETABLE:
		DB	0	; ACCESS CODE STORAGE
		DB	0	; STATUS CODE STORAGE
		DS	1	; BUFFER INDEX OR POINTER
		DB	'X'	; FILE ID FOR ERROR MESSAGES
		DS	33	; CP/M FILE CONTROL BLOCK
		DS	128	; DATA BUFFER STORAGE

			1	  READ ACCESS
	ACCESS:   DB    2	; WRITE ACCESS - NO DELETE
			3	  WRITE WITH DELETE
	FILENAME: DB	'B:FNAME.TXT '
	DATABYTE: DS	1	; STORAGE FOR DATABYTE
	MCOUNT:	  DB	80	; LENGTH OF READ BUFFER
	LINE:	  DS	80	; LINE BUFFER
	ACOUNT:	  DS	1	; LINE READ ACTUAL COUNT


   OPEN DISK FILE:
		LXI	H,FILETABLE
		LXI	D,FILENAME
		LXI	B,ACCESS
		CALL	DOPEN		; OPEN FILE
		JNZ	ERROR


   CLOSE DISK FILE:
		LXI	H,FILETABLE
		CALL	DCLOSE		; CLOSE FILE
		JNZ	ERROR


   CLOSE ALL OPEN FILES:
		CALL	GCLOSE		; CLOSE ALL OPEN FILES
		JNZ	ERROR


   READ BYTE FROM DISK FILE:
		LXI	H,FILETABLE
		LXI	D,DATABYTE
		CALL	BREAD		; READ A BYTE
		INR	A
		JZ	ENDOFFILE
		DCR	A
		JNZ	ERROR


   WRITE BYTE TO DISK FILE:
		LXI	H,FILETABLE
		LXI	D,DATABYTE
		CALL	BWRITE		; WRITE A BYTE
		INR	A
		JZ	ENDOFMEDIUM
		DCR	A
		JNZ	ERROR

 

   READ LINE FROM DISK FILE:
		LXI	H,FILETABLE
		LXI	D,LINE
		LXI	B,ARGLIST
		CALL	LREAD		; READ A LINE
		INR	A
		JZ	ENDOFFILE
		DCR	A
		JNZ	ERROR

	ARGLIST:
		DW	MCOUNT
		DW	ACOUNT


   WRITE LINE TO DISK FILE:
		LXI	H,FILETABLE
		LXI	D,LINE
		LXI	B,ACOUNT
		CALL	LWRITE		; WRITE A LINE
		INR	A
		JZ	ENDOFMEDIUM
		DCR	A
		JNZ	ERROR




	NOTES:
	  1. EACH FILE MUST HAVE ITS OWN "FILETABLE" OF
	     165 BYTES.

	  2. THE "FILETABLE" SHOULD NOT BE ALTERED BY THE USER
	     EXCEPT DURING PROGRAM INITIALIZATION WHEN THE FIRST
	     2 BYTES SHOULD BE SET TO ZERO AND THE FOURTH BYTE
	     SET TO SOME CHARACTER WHICH WILL BE DISPLAYED IN
	     ANY ERROR MESSAGES.

	  3. "FILENAME" IS A CHARACTER STRING REPRESENTING A
	     VALID CP/M FILE NAME WITH OPTIONAL DISK SELECT AND
	     FILE TYPE.  LEADING SPACES ARE IGNORED AND THE STRING
	     MAY BE TERMINATED BY A SPACE, CARRIAGE RETURN,
	     ",", OR "=".

	  4. TWO OPTIONS ARE AVAILABLE FOR WRITE ACCESS.  IF
	     THE FILE ALREADY EXISTS AND THE ACCESS CODE IS 2,
	     AN ERROR WILL RESULT AND THE FILE WILL NOT BE
	     OPENED.  IF THE ACCESS CODE IS 3, AN EXISTING FILE
	     WILL BE DELETED BEFORE OPEN.

	  5. OPERATION STATUS (HL), (A) AND (Z)
		(HL)
		(A)	(Z)
		0	1	NORMAL
		1-254	0	ERROR CODE - NOT PRESENTLY SPECIFIED
		255	0	END OF FILE ON READ
		255	0	END OF MEDIUM ON WRITE


	  6. LREAD  --
		CARRIAGE RETURN IS END OF LINE
		LINE FEED, NULL AND RUBBOUT ARE IGNORED
		CONTROL Z IS END OF FILE
		ASCII PARITY BIT IS REMOVED

	  7. LWRITE  --
		LINES ARE AUTOMATICALLY TERMINATED BY
		  CARRIAGE RETURN - LINE FEED