Getting Started for the STAGE2 Novice
								3/20/81

Step 1.	Print the following files:
		HELP.DOC
		USE.DOC
		INTRO.DOC
		DEMO.S2M

Step 2.	Read through INTRO.DOC but do not get bogged down in trying to under-
	stand it.  The idea on this first pass is to become a little familiar
	with what is there.

Step 3.	Run STAGE2 using DEMO.S2M for input.
		A>STAGE2 DEMO.S2M		; make sure printer is on
			or
		A>STAGE2 CON:,CON:=DEMO.S2M	; if you do not have a printer

		STAGE2 error messages go to channel 4 which is defaulted to
		the list device if nothing is specified on the command line.

Step 4.	Type the following examples and carefully observe the results.  Go
	through all of the examples once to become familiar with them but do
	not try to understand what is going on.  Then start over and do each
	example while referring to the listings DEMO.S2M and INTRO.DOC in an
	effort to understand the operations being performed.  Don't get dis-
	couraged as it may not make sense at first.  Perseverance is in order.

		HELP
		C0 ABC			; simple copy
		C1 ABC			; symbol undefined in memory
		F3 ABC=XYZ		; defines symbol in memory
		C1 ABC			; symbol now defined -
					;   note difference from previous C1 
		F3 ABC=IJK		; new value for ABC in memory
		C1 ABC
		S			; next symbol from generator
		S
		S
		C2 ABC			; similar to C1 except if symbol is not
					;   defined it will be given the next
					;   value from the symbol generator
		C2 PDQ
		S
		C2 PDQ
		C4 2+3*(4-7/3)		; expression evaluation
		C4 PDQ-6		; will use value of PDQ from memory
		C4 XXX+3		; XXX is undefined so value is 0
		C4 ABC+3		; causes error message to channel 4
					;   because ABC has non-numeric value
					;   in memory
		C5 ABCDEFGHIJK		; length of string
		C6 MAGIC		; parameter redefinition
		C7 ONE,TWO;THREE	; scanner operation
		C8 A
		C8 B			; internal code for character
		F1			; output request
		F7 2+3			; count controlled iteration
		F7 PDQ
		FE			; error trace back
		F0			; terminates - WARM BOOT