APPENDIX A

               RELATIONSHIPS BETWEEN CIRCUITS & MATRICES

1.0 TWO PORT PARAMETERS
    -------------------
    Two port parameters  are  network  equation  coefficients  derived  by
    making  various  short  and open circuit measurements on a "black box"
    circuit that contains  two  separate  input  and  output  connections.
    signal  return connections may be common (3 terminal device) or may be
    separate (4 terminal device). If all circuit  values  are  known,  the
    coefficients may be calculated instead of measured. these coefficients
    may be arranged in a matrix form so that two or more two port networks
    can  be  mathematically  combined  into  a  single two port equivalent
    device.    The  individual  matrices  are  mathematically  manipulated
    according to the rules of matrix algebra presented in section 2.0 .  

    The two port s parameters are derived from measurements  of  incident,
    reflected  and  transmitted  power  instead  of open and short circuit
    measurements.  

    A.  Z PARAMETERS
        ------------
    
           I1              I2
               ---------
       ^ 0-->--!       !--->----O !
    V1 !       !  [Z]  !          ! V2
       ! O-----!       !--------O V
               ---------
    
    V1 = Z11*I1 + Z12*I2   ( V1 )   ( Z11    Z12 )   ( I1 )
                           (    ) = (            ) * (    )
    V2 = Z21*I1 + Z22*I2   ( V2 )   ( Z21    Z22 )   ( I2 )
    
           WITH OUTPUT OPEN (I2 = 0)       WITH INPUT OPEN (I1 = 0)
           -------------------------       ----------------------
           Z11 = V1/I1                     Z12 = V1/I2
           Z21 = V2/I1                     Z22 = V1/I2
    
    B. Y PARAMETERS
       ------------
    
           I1              I2
               ---------
       ^ O-->--!       !--->----O !
    V1 !       !  [Y]  !          ! V2
       ! O-----!       !--------O V
               ---------


    
    I1 = Y11*V1 + Y12*V2   ( I1 )   ( Y11    Y12 )   ( V1 )
                           (    ) = (            ) * (    )
    I2 = Y21*V1 + Y22*V2   ( I2 )   ( Y21    Y22 )   ( V2 )
    
           WITH OUTPUT SHORTED (V2 = 0)    WITH INPUT SHORTED (V1 = 0)
           ----------------------------    --------------------------
           Y11 = I1/V1                     Y12 = I1/V2
           Y21 = I2/V1                     Y22 = I2/V2
    
    C. H PARAMETERS    (HYBRID)
       ------------
    
           I1              I2
               ---------
       ^ O-->--!       !--->----0 !
    V1 !       !  [H]  !          ! V2
       ! O-----!       !--------O V
               ---------
    
    V1 = H11*I1 + H12*V2   ( V1 )   ( H11    H12 )   ( I1 )
                           (    ) = (            ) * (    )
    I2 = H21*I1 + H22*V2   ( I2 )   ( H21    H22 )   ( V2 )
    
           WITH OUTPUT SHORTED (V2 = 0)    WITH INPUT OPEN (I1 = 0)
           ----------------------------    -----------------------
           H11 = V1/I1                     H12 = V1/V2
           H21 = I2/I1                     H22 = I2/V2
    
    D. X PARAMETERS   (TRANSMISSION)
       ------------
    
           I1              I2
               ---------
       ^ O-->--!       !--->----O ^
    V1 !       !  [X]  !          ! V2
       ! O-----!       !--------O !
               ---------
    
    V1 = A*V2 + B*I2       ( V1 )   ( A      B   )   ( V2 )
                           (    ) = (            ) * (    )
    I1 = C*V2 + D*I2       ( I1 )   ( C      D   )   ( I2 )
    
           WITH OUTPUT OPEN (I2 = 0)       WITH OUTPUT SHORTED (V2 = 0)
           -------------------------       ---------------------------
           A = V1/V2                       B = V1/I2
           C = I1/V2                       D = I1/I2
    
    E. S PARAMETERS
       ------------
    
           A1-->         <--A2
                 ---------
         O-------!       !-------O
    ZG    V1,I1  !  [S]  ! V2,I2   ZL
         O-------!       !-------O
                 ---------
            <--B1         B2-->
    
    ZO = IMPEDANCE OF TRANSMISSION LINE SYSTEM USED FOR
         MEASUREMENT (NORMALLY 50 OHMS)
    
    A1 = V1 + I1*ZO = VOLTAGE WAVE INCIDENT ON PORT 1
         ----------   -------------------------------
           2*ZO            2*ZO
    
    A2 = V2 + I2*ZO = VOLTAGE WAVE INCIDENT ON PORT 2
         ----------   -------------------------------
           2*ZO            2*ZO
    
    B1 = V1 - I1*ZO = VOLTAGE WAVE EMENATING FROM PORT 1
         ----------   ----------------------------------
           2*ZO            2*ZO
    
    B2 = V2 - I2*ZO = VOLTAGE WAVE EMENATING FROM PORT 2
         ----------   ----------------------------------
           2*ZO            2*ZO
    
           FOR ZL = ZO (A2 = 0)    FOR ZG = ZO (A1 = 0)
           --------------------    --------------------
           S11 = B1/A1             S12 = B1/A2
           S21 = B2/A1             S22 = B2/A2
    
    S11 = Z1 - ZO                  S12 = I1   (Z1 - ZO)
          -------                        -- * ---------
          Z1 + ZO                        I2   (Z2 + ZO)
    
    S21 = I2   (Z2 - ZO)           S22 = Z2 - ZO
          -- * ---------                  -------
          I1   (Z1 + ZO)                  Z2 + ZO
    
    Z1 = ZO   (1 + S11) INPUT Z WITH OUTPUT TERMINATED IN ZO
            * ---------
              (1 - S11)
    
    Z2 = Z0   (1 + S22) OUTPUT Z WITH INPUT TERMINATED IN ZO
            * ---------
             (1 - S22)

    
2.0 TWO PORT MATRIX ALGEBRA
    -----------------------
    A. GENERAL
       -------
    The following algebraic relations hold when manipulating     two  port
    matrices.  Any or all quantities may be complex.   The general network
    representation is:  
    
           EQUATIONS               MATRIX REPRESENTATION
           ---------               ---------------------
           X1 = A11*P1 + A12*P2   ( X1 )   ( A11    A12 )   ( P1 )
                                  (    ) = (            ) * (    )
           X2 = A21*P1 + A22*P2   ( X2 )   ( A21    A22 )   ( P2 )
           X = [A] * [P]
           (SENDING END MATRIX) = (NETWORK MATRIX) * (RECEIVING END MATRIX)
    
    B. ADD-SUBTRACT
       -----------
    
        ( M11    M12 )   ( N11    N12 )   ( (M11 + N11)  (M12 + N12) )   ( Q11    Q12 )
        (            ) + (            ) = (                          ) = (            )
        ( M21    M22 )   ( N21    N22 )   ( (M21 + N21)  (M22 + N22) )   ( Q21    Q22 )
    
        [M] + [N] = [Q]
    
    C. MULTIPLICATION
       --------------
       ( M11    M12 )   ( N11    N12 )   ( (M11*N11 + M12*N12)  (M11*N12 + M12*N22) )
       (            ) * (            ) = (                                          )
       ( M21    M22 )   ( N21    N22 )   ( (M21*N11 + M22*N21)  (M21*N12 + M22*N22) )
    
       [M] + [N] = [Q]
    
       NOTE: Multiplication must be taken in specific order
    
       [M] * [N] IS NOT EQUAL TO [N] * [M]
    
    D. DIVISION
       --------
       Not normally used in analysis. Included for information only.
    
       ( M11    M12 )   ( N11    N12 )   ( Q11    Q12 )
       (            ) = (            ) * (            )
       ( M21    M22 )   ( N21    N22 )   ( Q21    Q22 )
    
       [M] = [N] * [Q]
    
          -1
          -1
        [N] * [M] = [Q]
    
    
    
                             ( N22   -N12 )
          -1                 (            )
       [N]  = ADJOINT [N]  = (-N21    N11 )
             -----------    --------------------------
               DET [N]       ( N11*N22 - N12*N21 )
    
            ( Q11    Q12 )   ( N22   -N12 )   ( M11    M12 )
            (            )   (            )   (            )
       [Q]= ( Q21    Q22 ) = (-N21    N22 ) * ( M21    M22 )
                            --------------
                              DET [N]
    
             ( N22/DEL -N12/DEL )   ( M11    M12 )
       [Q] = (                  ) * (            )
             (-N21/DEL  N11/DEL )   ( M21    M22 )
    
       DEL = DET [N]  = (N11*N22 - N12*N21)
    
3.0 COMBINING NETWORK MATRICES
    --------------------------

    A. PARALLEL NETWORKS
       -----------------
    
             ---------
       ------!       !------
       !     !  [YA] !     !
       !  ---!       !---  !
       !  !  ---------  !  !
       !  !             !  !
       !  !  ---------  !  !
    O--O--!--!       !--!--O--O
          !  !  [YB] !  !
    O-----O--!       !--O-----O
             ---------
    
    [YC] = [YA] + [YB]
    
    B. SERIES NETWORKS
       ---------------
    
             ---------
    O--------!       !--------O
             !  [ZA] !
        -----!       !-----
        !    ---------    !
        !                 !
        !    ---------    !
        -----!       !-----
             !  [ZB] !
    O--------!       !--------O
             ---------
    
    [ZC] = [ZA] + [ZB]
    
    C. CASCADE NETWORKS
       ----------------
    
             ---------         ---------
    O--------!       !---------!       !---------O
             !  [XA] !         !  [XB] !
    O--------!       !---------!       !---------O
             ---------         ---------
    
    [XC] = [XA] * [XB]
    
4.0 MATRIX CONVERSIONS
    ------------------
    Analysis of networks  containing  even  a  few  series,  parallel  and
    cascade  circuits will require conversion of matrices from one type to
    another. subroutines SMATX.SRT, XMATS.SRT, ZXXZ.SRT AND  YZZY.SRT  are
    provided for this purpose.