MESSAGE.BAS

THIS IS A SIMPLE PROGRAM FOR SENDING A MESSAGE FROM YOUR
COMPUTER TO THE PRINTER IN ENLARGED (5 CPI) LETTERS.
AT THE END OF THE TEXT IT PERFORMS A FORM FEED AND SETS THE
PRINTER BACK TO NORMAL (10 CPI) SIZE.
 
YOU CAN CHANGE THE CHARACTERS PER INCH BY CHANGING CHR$(53)
IN LINE 180 AS FOLLOWS:
CHR$(54)= 6 CPI
CHR$(56)= 8.25 CPI
CHR$(52)= 16.5 CPI (CONDENSED PRINT)
CHR$(50)= 12 CPI (PICA SIZE)

Other bells and whistles can be added by inserting
similar escape commands:

ESC K = turn on a subscript (or turns off a superscript)
ESC L = turn on a superscript (or turn off a subscript)
For example:
"H";CHR$(27);"K";"2";CHR$(27);"L";"O"
Will print out as H2O with the "2" printed half a line lower 
than the H and O. 
CHR$(27)=ESC

"PI r";CHR$(27);"L";"2";CHR$(27);"K" 
Will print PI r2 with "2" half a line higher than PI r, and
then sets the line back to the center again. Without the 
ESC K at the end, the rest of the line would be printed
on the same level as the "2".

ESC [4m starts underlining
ESC [m  stops underlining

If you really want to blow away a Centronics printer, send it

ESC % 0

That will send it into graphics mode, where instead of printing
letters, it will print dot patterns which correspond to the
binary ASCII codes for each character. 

To recover from graphics mode, give the printer an

CHR$(15) (SI)

-Howard Stateman
5/84