.PO 0 
                 DOCUMENTATION FOR RFORMAT AND TRACKRD
                      A TRANSIENT FORMAT PROGRAM
 
       A formatting program to generate any machine disk format:
 
                                 By
                          Rich Harrington
                           31 Blade Way
                      Walnut Creek, CA 94595
 
To use the RFORMAT program of Rich Harrington it is merely necessary to
place the disk containing RFORMAT.COM in drive say A and from
the A> prompt type RFORMAT.  This will allow you to format a disk for
the MicroMate on the drive you select and continue to do so until you
exit the program at the prompt.  The following will be displayed on your
console with a <CR> (carriage return) after the RFORMAT command.
 
TRANSIENT FORMAT PROGRAM 12-31-84 BY
Rich Harrington 31 Blade Way Walnut Creek, CA 94595
*************** MICROMATE FORMAT ***************
*.FMT File required to change formats.
WHICH DRIVE? (A - D ALLOWED) __ ;Type in the drive for formatting
Q or X or E to exit  CR or F or Y to format __ ;Type in your choice
SIDE 0
0123456789012345678901234567890123456789
SIDE 1
0123456789012345678901234567890123456789
Q or X or E to exit  CR or F or Y to format -- ;Type in your choice
;i.e., Q or X or E will put you back to CP/M. While CR or F or Y
;will allow you to format another MicroMate disk in the same drive you
;have selected.
 
If you wish to format a different format you must have a *.FMT file
on disk corresponding to the given different format, i.e., KAYPRO2.FMT.
 
The command at the A> prompt is as follows, with the resultant display.
Where <CR> equals a carriage return.
 
A>RFORMAT KAYPRO2<CR>
 
TRANSIENT FORMAT PROGRAM 12-31-84 BY
Rich Harrington 31 Blade Way Walnut Creek, CA 94595
KAYPRO2 SSDD FORMAT
WHICH DRIVE?  (A - D ALLOWED) __ ;Type in your choice as above
Q or X or E to exit  CR or F or Y to format __ ;Again, type in your
choice, repeat to format another KAYPRO2 disk in the same drive.
 
---------------------------------------------------------------------------
 
Next, use TRACKRD.COM to obtain the disk format data you will need
later.  The use of TRACKRD allows you to read the tracks of a disk
to obtain the data needed to establish a .FMT file for formatting
that particular machine format.
 
With TRACKRD.COM on disk, type the following at the prompt:Š 
A>TRACKRD<CR>
;The following will be displayed:

DISK TRACK READ PROGRAM BY RICH HARRINGTON VER 1.0 08-06-84
VER 1.1 11-12-84 REMOVED FILE WRITE ADDED CLOCK SPEED
VER 1.2 01-18-85 ADDED SECTOR READ FILE WRITE

				OPTIONS
LOG DISK	L DRIVE NAME
SET TRACK	T TRACK NUMBER DECIMAL
CLOCK RATE	C 5 or 8
SET SIDE	H 0 or 1
SET DENSITY	Z S or D
SET SECTOR	S SECTOR NUMBER IN DECIMAL
SET SECTOR SIZE	U 0=128 1=256 2=512 3=1024
WRITE SECTOR	W d:filename
READ TRACK	R
READ SECTOR	P
DUMP TRACK	D MUST HAVE READ FIRST
                  ^X TO STOP DUMP
EXIT PROGRAM    ^C TO EXIT TO CP/M


$
 
At the $ prompt type in the data for the disk format you are
interested in and for which you will develop a .FMT file.
Follow the listing displayed answering each after the $ prompt.
A <CR> indicates a carriage return.
The following examples are data for the MicroMate format.
 
$L B<CR>  ;Where B is the drive which has the formatted disk to
          ;be read.
 
$T 0<CR>  ;This will allow the setting of track 0.
 
$C 5<CR>  ;This sets for the disk size, i.e. 5 or 8.  The default
          ;is 5 so leaving out the $C causes the program to
          ;assume that the disk is 5 inch.
 
$H 0<CR>  ;This sets the side to be read, i.e., in this case
          ;zero.  The alternative of course is 1 for side 1,
          ;which you will use later to read side 1.  The default
          ;is to 0.
 
$Z D<CR>  ;This sets the disk density, in this case double.
          ;For single density it would be S instead of D.
 
$S 0<CR>  ;This selects the sector to be read...the result
          ;will be the true sector data as written.  A deter-
          ;mination of the number of the sectors is obtained
          ;from an R read & D dump.
 
$U 3<CR>  ;The U input is the sector size which will vary withŠ          ;the format and can be ascertained with an R read &
          ;D dump.  Look at the outline above where this data,
          ;when obtained, is placed, i.e.,SECSIZE.  In the ex-
          ;ample shown the 3 or 03 is equal to a 1024 sector
          ;size.
 
$W d:filename.ext<CR>  ;When you wish to write the sector data
          ;to disk use the W command.  Determine which drive &
          ;and the name of the file to which the data will be
          ;written and employ with the W command as shown.  As
          ;can be seen the standard CP/M notation is used for
          ;the drive and filename.
 
$R<CR>    ;This causes the disk to seek to, and read the entire
          ;track.

$P<CR>    ;This reads the sector selected by the number you have
          ;entered using the S command.  It does not move the
          ;head, i.e., it doesn't change tracks.  In case you
          ;select a specific track number and the dump shows a
          ;different track number you are probably faced with the
          ;reality that someone (a software artist) has put a
          ;copy protect scheme onto the disk.
 
$D<CR>    ;With this command the read disk format is "DUMP"ed
          ;so the disk read is locatable by tracks with the
          ;read-out in hex.
          ;NOTE!! At the <CR> be prepared to ^S (control S)
          ;to stop the scrolling or you will miss the first
          ;addresses.  A ^Q (control Q) will continue the scroll.
          ;The ^S/^Q is an off/on toggle for scrolling.
          ;NOTE!! It's a good idea to obtain a hard copy of
          ;this dump so you should turn on you printer and
          ;^P (control P) before you send the <CR>.  Or you can
          ;use W to write the data to a file.
 
^X        ;A control X will stop the dump and give you the $
          ;prompt.
 
$^C       ;The ^C (control C) will put you back to CP/M prompt.
 
------------------------------------------------------------------------------
 
DEVELOPING A *.FMT FILE:
 
This program allows the user to define different machine disk formats by
generating an *.FMT file.
 
NOTE!! NOTE!! It follows that wherever you see the *.FMT throughout this
documentation you must replace the * with the name of your file.
 
It should be understood that the *.FMT is used in conjunction with RFORMAT
as previously explained.
 
First, obtain a disk (no data, unused preferred) which has been formattedŠin the format in which you want to develope the *.FMT file.
 
Read the format data with TRACKRD.  See above for instructions on the use
of TRACKRD.COM.

Remove your foreign formatted disk from the B drive!
 
To obtain an exemplar track read it would be a good idea to follow the
same TRACKRD instructions indicated above using a formatted MicroMate disk.
Thió wilì givå yoõ á referencå tï makå comparisons®  Leavå thió MicroMate  
disk in drive B.

Now, you should have 2 hard copies of track reads; one, your *.FMT and the
MicroMate.

The next 3 pages of data is reference material which we will apply to your
developing your *.FMT.  Included are the single and double (dual) density
IBM formats, the MicroMate format and the *.FMT outline to be used in
developing your *.FMT.  The data in the outline is for the MicroMate so it
can be used as a guide in developing your *.FMT.
 
To provide some basic information the following data shows the single and
double density disk formats of IBM 3740 and 34 respectfully:
------------------------------------------------------------------------------
THE IBM 3740 FORMAT - 128 BYTES/SECTOR
 
Shown below is the IBM single-density format with 128
bytes/sector.  In order to format a diskette, the user must
issue the Write Track command, and load the data register
with the following values.  For every byte to be written,
there is one Data Request.
 
NUMBER OF BYTES    HEX VALUE OF BYTE WRITTEN
 
       40          FF (or 00)*
        6          00
        1          FC (Index Mark)
    ** 26          FF (or 00)*
ü--------
ü       6          00
ü       1          FE (ID Address Mark)
ü       1          Track Number
ü       1          Side Number (00 or 01)
ü       1          Sector Number (1 thru 1A)
ü       1          00 (Sector Length)
ü       1          F7 (2 CRC's written)
ü      11          FF (or 00)*
ü       6          00
ü       1          FB (Data Address Mark)
ü     128          Data (IBM uses E5)
ü       1          F7 (2 CRC's written)
ü      27          FF (or 00)*
ü--------
      247***       FF (or 00)*
 Š*   Optional '00' on 1795/7 only.
**  Write bracketed field 26 times.
*** Continue writing until FD179X interrupts
    out.  Approx. 247 bytes.
------------------------------------------------------------------------------
IBM SYSTEM 34 FORMAT - 256 BYTES/SECTOR
 
Shown below is the IBM dual-density format with 256
bytes/sector.  In order to format a diskette the user must
issue the Write Track command and load the data register
with the following values.  For every byte to be written,
there is one Data Request.
 
NUMBER OF BYTES    HEX VALUE OF BYTE WRITTEN
 
       80          4E
       12          00
        3          F6 (Writes C2)
        1          FC (Index Mark)
    *  50          4E
ü--------
ü      12          00
ü       3          F5 (Writes A1)
ü       1          FE (ID Address Mark)
ü       1          Track Number (0 thru 4C)
ü       1          Side Number (0 or 1)
ü       1          Sector Number (1 thru 1A)
ü       1          01 (Sector Size)
ü       1          F7 (2 CRC's written)
ü      22          4E
ü      12          00
ü       3          F5 (Writes A1)
ü       1          FB (Data Address Mark)
ü     256          DATA
ü       1          F7 (2 CRC's written)
ü      54          4E
ü--------
      598**        4E
 
*  Write bracketed field 26 times
** Continue writing until FD179X interrupts out.
   Approx. 598 bytes.
------------------------------------------------------------------------------
Now we present the same type of format information as it is used in the
MicroMate machine.
 
Format programs write a full track at one time.
A full track typically has a header, sectors, and a tail filler.
 
THE MICROMATE DSDD DISK FORMAT IS:
 
NAME    COUNT   DATA    COMMENT
HEADER
        80      4EH
        12      00Š         3      F6      WRITES C2
         1      FC      WRITES INDEX MARK
        50      4E
SECTOR                  REPEAT 5 TIMES FOR MICROMATE
        12      00
         3      F5      WRITE A1
         1      FE      INDEX MARK
         1      TN      TRACK NUNBER 0 - 39
         1      SN      SIDE 0 or 1
         1      SN      SECTOR NUMBER 1 - 5
         1      03      SECTOR SIZE
                        00(00)=128, 01(01)=256, 10(02)=512, 11(03)=1024
         1      F7      WRITES 2 CRC
        22      4E
        12      00
         3      F5      WRITES A1
         1      FB      DATA ADDRESS MARK
      1024      E5      DATA
         1      F7      WRITES 2 CRC
        54      4E
TAIL
      1792      4E      WRITES 4E UNTIL END OF TRACK
 
If the MicroMate format were an *.FMT file it would look like:
; 256 BYTES OF FORMAT SPACE OVER-WRITE WITH *.FMT FILE
; TO CHANGE FORMAT TYPE
;
---------THE *.FMT FILE BEGINS BELOW THIS LINE--------------------------------
XX00:
        DB      80,4EH, 12,00, 03,0F6H, 01,0FCH, 50,4EH, 00,0FFH
        DW      0,0
XX10:
        DB      12,00, 03,0F5H, 01,0FEH, 00,00
        DW      0,0,0,0
XX20:
        DB      01
TRACK:
        DB      00
        DB      01
SIDE:
        DB      00
        DB      01
SECTOR:
        DB      01
        DB      01
SECSIZE:
        DB      03, 01,0F7H, 22,4EH, 12,00, 03,0F5H
XX30:
        DB      01,0FBH, 00,0E5H, 00,0E5H, 00,0E5H, 00,0E5H
        DB      01,0F7H, 54,4EH, 00,0FFH
XX40:
        DB      00,4EH, 00,4EH, 00,4EH, 00,4EH
        DB      00,4EH, 00,4EH, 00,4EH, 00,0FFH
XX50:
SIDES:Š        DB      1
TS01:
        DB      0
TS0L:
        DB      39
TS11:
        DB      0
TS1L:
        DB      39
DENS:
        DB      0       ; 0 = DOUBLE  40H = SINGLE
SIZE:
        DB      0       ; 0 = 5 INCH  80H = 8 INCH
        DB      0,0,0,0,0,0,0,0,0
XX60:
S0SECT:
        DB      1,2,3,4,5,0FFH
        DW      0,0,0,0,0,0,0,0,0,0,0,0,0
XX80:
S1SECT:
        DB      1,2,3,4,5,0FFH
        DW      0,0,0,0,0,0,0,0,0,0,0,0,0
XXA0:
        DB      '*************** MICROMATE FORMAT ***************'
        DB      0DH,0AH,'*.FMT File required to change formats.$'
 
----------------THE LINE ABOVE THIS LINE ENDS THE *.FMT-----------------------
 
Now lets develope your *.FMT file

Your disk in drive A must contain the following files:
MAKE.SUB
RFORMAT.COM
RFORMAT.DOC
RFORMATA.SUB
RFORMATF.SUB
SUBMIT.COM
TRACKRD.COM
WIPE.COM
 
PIP the data between the two indicated lines, i.e., "THE *.FMT FILE BEGINS
BELOW THIS LINE" and "THE LINE ABOVE THIS LINE ENDS THE *.FMT", with the
following command:
 
(Type in exactly as shown.  Do not change the TEST.FMT to the name of your
FMT as the submit file uses TEST.  If you wish you can use the file
extension .ASM instead of .FMT as the file will have to be renamed event-
ually for the purposes to assembling with MAC.  In the latter case use the
second command line below).
 
Use the Submit files provided on this disk, RFORMATF.SUB contains the PIP
command below for the FMT, while the RFORMATA.SUB contains the PIP command
below for the ASM.  To use the Submit merely type RFORMATF or RFORMATA at
the prompt.  Of course you must have the SUBMIT.COM and the RFORMAT.DOC files
available. You will note that the destination is B: therefore your filesŠwill be on A: and the new TEST file will be PIP'ed to B:.
 
PIP B:TEST.FMT=RFORMAT.DOC[SXX00:^ZQ$'^Z]
PIP B:TEST.ASM=RFORMAT.DOC[SXX00:^ZQ$'^Z]
 
No÷ yoõ wilì havå á filå oî disë witè youò nameä .FMÔ oò .ASÍ whicè you
caî ediô changinç thå appropriatå sectionó tï corresponä tï thå ne÷ data
yoõ havå obtaineä froí thå tracë read®  Don'ô forgeô tï renamå thå comment
linå froí MicroMatå tï thå namå oæ youò FMÔ anä enä iô witè $§ makå sure
that the comment ending with the $' is before XXFF.

Usinç youò texô editoò writå youò owî *.FMÔ filå usinç thå TRACKRÄ  prograí �
oî  á  knowî formatteä disë (Iô woulä bå betteò iæ thå disë haó nï datá  oî �
it)®  Thió shoulä have beeî donå before¬  iæ not¬ dï iô now®  Witè thå datá �
obtaineä  yoõ  arå readù tï takå thå "Dump¢ oæ thå  MicroMatå  TRACKRÄ  anä �
comparå  witè  thå  filå iî thå MicroMatå outlinå above®   Usinç  youò  FMÔ �
"dump¢  yoõ  wilì builä á filå likå thå onå abovå onlù foò thå  ne÷  formaô �
usinç thå outlinå anä replacinç thå necessarù datá obtaineä froí thå  tracë �
reaä usinç youò editor.
 
Note 00 00 = goto the next XXX0. That is if you are at XX06 then
the next data would come from XX10.
 
Note that 00 FF = end of header, sector or tail.

Note that starting at XX00 there should be about 80 4E's (see the IBM dual-
density and MicroMate formats above), the H in 80,4EH stands for hex.
 
Next, the "Dump" should have 12 00's
then,                         3 F6's (which show up as C2's)
then,                         1 FC and
                             50 4E's
This ends the header - note how this is put into the *.FMT outline for the
MicroMate and that the 00,0FFH shows the end of the header.  
 
       DB (defined byte)     80,4EH(Hex), 12,00, 03,0F6H, 01,0FCH, 50,4EH,
                             00,0FFH
       DW (defined word)      0,0  This is a filler so that the total of the
DB and DW equal 16 decimal or 10H.  In this way the ten lines between XX00
and XX10 will be filled.  The DB line counts 12 and the DW counts 4 (2 bytes
per word or 0) for a total of 16.   
	 
Now, comes the Sector which is repeated 5 times for the MicroMate.

At XX10: 
           DB is            12 00's
 
                              3 F5's  this is written as A1, sometimes a 
				      different byte will show indicating
                                      that the disk is out of sync. in later
                                      sectors this should be aligned and show 
                                      the 3 A1's but don't be concerned if it
                                      doesn't.

and,                          1 FE    This is an index mark.Šand,                         00,00    This is for the programmer to expand
                                      later if so desired.  Do not change.
then,       DW which is      0,0,0,0  Again, these are fillers to make up the
                                      total bytes for the space between XX10
                                      and XX20.  In this case they represent
                                      8 and with 8 in the DB line we have a
                                      total of 16 or 10H.
Now, we are at
XX20:
and,                          1 TN    0 to 39
and,                          1 SN    0 or 1
and,                          1 SN    1 - 5
and,                          1 03    Sector size - 00, 01, 02 or 03
                                      (see above under MicroMate format
                                      for description)
then,                         1 F7    this will appear differently, not as
                                      F7.
then,                        22 4E's
and,                         12 00's
and,                          3 F5's  A1's but all I've been able to get
                                      is 14 A1 A1 for the MicroMate!  Don't
                                      worry if you do too!!
Now, at
XX30:
then,                         1 FB    is the data address mark.
and,                       1024 E5's  is the data block.  It will be E5's and
				      in one of the following configurations:
				      4 x 20H or  32 decimal= 128 bytes
                                 or,  4 x 40H or  64 decimal= 256 bytes  	
                                 or,  4 x 80H or 128 decimal= 512 bytes
                                 or,  4 x 00H or 256 decimal=1024 bytes
                                      this last is what is seen for the 
                                      MicroMate in the outline.
and,                          1 F7    two bytes are written
then,                        54 4E's  Mine writes 85 4E's instead of 54 but
                                      it works.
This ends the Sector:	              Note that the sector ends with 00,00FFH
 				      Notice also that defined bytes between
                                      XX30: and XX40: is also 16 or 10H.

The Tail is                1792 4E's  and is represented by the data in XX40:
 				      again, 16 defined bytes.

At this point you should be at XX50:
 
Under SIDES:
for the defined byte, i.e.,
        DB      1                     enter a 0 or a 1
 
TS01:   DB      0                     this is Track 1 Side 0 or the first
                                      track on side 0
TS0L:   DB      39                    this is the last track on side 0
 
TS11:   DB      0                     the first track on side 1
 ŠTS1L:   DB      39                    the last track on side 1
 
DENS:   DB      0                     "0" = DOUBLE  "40H" = SINGLE
 
SIZE:   DB      0                     "0" = 5 INCH  "80H" = 8 INCH
                                      in both cases above do not put in the
                                      " " when you enter the data.
	DB	0,0,0,0,0,0,0,0,0     All of the defined bytes above this are
 				      7 so with 9 more we have the 16 or 10H.

At XX60 is the Sector Translation Table (Sector order) for side 0 which ends
with FF, the Flag that indicates there are no more sectors.
The number sequence is ascertained from the dump reading the byte for the
number of the sectors.  When the sequence is established it is placed here
with each number separated by commas.  It should be noted that the DB line
must contain an even number including the 0FFH.  Therefore, if necessary you
must add a ,0 following the 0FFH
The 26 bytes of 0's are fillers.  This time instead of 16 defined bytes 32
are needed (20H) because we need 20 lines between XX60: and XX80: thus the
6 defined bytes in the first line and the 13 0's (defined words) in the 
second line representing 26 bytes makes a total of 32 or 20H.

XX80: is the same as above but for side 1, in both cases it should be noted
that 5 sectors are shown.  Again the 26 bytes of 0's represent fillers.
 
Then at XXA0: the text of what format the .FMT represents is shown.  The
second line follows the 0DH,0AH'.  The ending must be $' as shown and be
before XXFF.  In any event the comments are restricted to a total of 96
characters.  The example in the MicroMate outline has 50 in the first line 
and 45 in the second for a total of 95.  Note that the hex notations ODH
and OAH are each one character.
 
Next, you should proof-read your data and if everything is OK then follow
the indicated procedure below using MAC, the CP/M assembler.
 
Make sure your new *.FMT has the .ASM extension, RENAME the file if it's
necessary.  Then give the following command at the prompt or go to the #
sign below for an alternate method.
 
A>MAC *.ASM
 
This will assemble the *.ASM file and create a .SYM, .PRN, & .HEX file.
Print your .PRN file and make sure XX-- is really XX-- which conforms to
the outline above.
 
Next, at the prompt type in the following:
 
A>HEXCOM *.HEX
 
This will create the .COM file
 
now,
 
A>RENAME *.FMT=*.COM
 Šand you will have your new *.FMT file.
 
A>RFORMAT *.FMT
 
To execute see above (1st page of this documentation).
 
This will ask for the drive you wish to use to format the new format...just
follow the directions given and you will have a newly formatted disk in your
new .FMT configuration...if it doesn't work call Rich Harrington anytime!!!!
 
# Alternate assembly using a submit file MAKE.SUB which resides on this disk.
The alternate method also requires the files WIPE.COM & SUBMIT.COM to be on
disk.  At the prompt, type as indicated:  Don't forget * = the name of your
FMT.
 
A>MAKE *.FMT
 
A>DIR
 
You should find your new *.FMT residing on disk with no extraneous files.
 
Good luck,
 
Ed Miller, Librarian
EastBay MicroMate Users' Group
February 7, 1985