KERMIT-CMS(1C)   UCB Microcomputer Users Manual    KERMIT-CMS(1C)



NAME
     _K_e_r_m_i_t-_C_M_S - Microcomputer to _C_M_S file transfer program

SYNOPSIS
     Use `set ibm on' on the micro _K_e_r_m_i_t, connect to CMS using
     CAL mode at 300 or 1200 baud, logon to CMS and give the KER-
     MIT command.  _K_e_r_m_i_t-_C_M_S is interactive and prompts with
     `KERMIT-CMS>':

     RECeive [FN FT [FM]]
     SENd FN FT [FM]

     CMS <cms-command>
     CP  <cp command>
     SET END-of-line 00-31
     Exit
     HELP
     SET LRECL 1-133
     SET PACket-size 26-94
     Quit
     SET QUOTE <char>
     SET RECFM  V | F
     SHOw [ RECFM | END of line | QUOTE | LRECL | PACket-size ]
     STATUS

     The commands and keywords can be abbreviated, CAPITAL
     letters must be entered, small letters are optional.  Typing
     a `?' in place of a command or keyword will display the
     options.

DESCRIPTION
     _K_e_r_m_i_t is a file transfer and terminal emulation utility
     distributed by Columbia University.  It has been implemented
     for many different computers, including microcomputers.  Any
     two machines running _K_e_r_m_i_t can reliably exchange files over
     normal character terminal lines.  For file transfers, a _K_e_r_-
     _m_i_t program must be running in the microcomputer to exchange
     data packets with the _K_e_r_m_i_t program on _C_M_S.  Micro versions
     differ slightly from one to another and only a few are
     currently supported by UCB, however, in principle, with any
     other microcomputer or mainframe _K_e_r_m_i_t.  At this time, only
     UCB micro _K_e_r_m_i_t versions can communicate with UCB _K_e_r_m_i_t-
     _C_M_S ( see IMPLEMENTATION).

     RECeive [FN FT [FM]]
          In receive mode, also called uploading, _K_e_r_m_i_t-_C_M_S
          attempts to store the file with the name supplied by
          the sending micro.  A file specification on the
          _K_e_r_m_i_t-_C_M_S receive command can specify the full name of
          a single file to be received or a single file to col-
          lect multiple files received (use `set file ascii' on
          the micro to avoid imbedded ^Z's).  The file mode can



Printed 2/13/84         13 February 1984                        1






KERMIT-CMS(1C)   UCB Microcomputer Users Manual    KERMIT-CMS(1C)



          specify the disk on which files are to be received (`=
          = D').  CAUTION: if the file already exists with the
          same record format, the incoming file will be appended,
          otherwise Kermit-CMS will abort.  BUG: if `%' or `*'
          used in name or type field, _K_e_r_m_i_t-_C_M_S does not abort
          until the micro _K_e_r_m_i_t attempts to send, then several
          error messages preceed an abort for `disk full'.

          _K_e_r_m_i_t-_C_M_S cannot receive files without a type field
          from the sender (a period plus at least one following
          character), unless the full name is specified on the
          receive command.  _K_e_r_m_i_t-_C_M_S only accepts letters,
          digits and `#$+-:@_' in file names.  Lower case letters
          are converted to upper case.

          The received ASCII characters are converted to seven
          bit EBCDIC (see table in Kermit Users Guide).
          Carriage-return alone, line-feed alone, or carriage-
          return and line-feed togeather will be interpreted as
          an end-of-record and will be removed.  BUG: if a record
          does not end with carriage-return or line-feed, the
          partial record is held by _K_e_r_m_i_t-_C_M_S and is prepended
          to the next file received.

          BUG: Kermit-CMS cannot write zero length files, but
          will accept them as if it had.

          If the record format is variable (the default, recfm
          V), the record length can be up to 256.  Records longer
          than 256 are broken into multiple records.  BUG:
          records that are exact multiples of 256 bytes are writ-
          ten as multiple records of length 256 followed by sin-
          gle a blank record of length 1.

          If the record format is fixed (recfm F), any record
          longer than the logical record length (lrecl) will be
          truncated.  If shorter, it is padded to lrecl with
          blanks.  The record length can be set up to 133
          (default is 80).  BUG: if the record length received is
          greater than 256, _K_e_r_m_i_t-_C_M_S will truncate the first
          256 bytes to lrecl then act as though the next record
          begins with the 257th character.  BUG: if the record
          received is exactly 256 bytes, _K_e_r_m_i_t-_C_M_S writes one
          record of length lrecl then aborts for `disk full'.

     SENd FN FT [FM]
          In send mode, also known as downloading, files are sent
          from _C_M_S to your microcomputer.  Multiple files may be
          sent by using "*" or "%" as wildcard characters (`*'
          matches any number of characters, `%' matches exactly
          one).  If the file-mode (FM) is not specified _K_e_r_m_i_t-
          _C_M_S assumes the A disk, and sets the file mode to A1.



Printed 2/13/84         13 February 1984                        2






KERMIT-CMS(1C)   UCB Microcomputer Users Manual    KERMIT-CMS(1C)



          For a different  disk, the  filemode  must  be  cited.
          If filemode `*' is used, _K_e_r_m_i_t-_C_M_S will send only the
          first matching file.

          Bytes are converted from EBCDIC characters to seven bit
          ASCII characters for sending (see table in Kermit Users
          Guide).  Trailing blanks are removed from each record
          and carriage-return and line-feed are appended.  The
          maximum record length is 256 and only fixed (F) and
          variable (V) records are allowed.  (?? what happens if
          longer than 256 ??).

          Kermit-CMS must wait 15 seconds before sending the
          first packet to allow time for the user to escape back
          to the micro and enter the receive command.

     SET RECFM  V | F
          Sets the record format to be used when receiving a
          file.  Only fixed (F) and variable (V) length records
          are allowed, variable is the default.

     SET LRECL 1-133
          Sets the logical record length (default is 80).  BUG: 0
          is allowed and if set, gives `Disk full' during
          receive.

     SET QUOTE <char>
          The quote character to be used for escaping control
          characters in packets (default `#').  It must be a sin-
          gle, printable character from among the following: 33-
          62, 96, or 123-126 (decimal).  Note that `(' and `)'
          are word separators on the input line and do not count
          as characters.

     SET END 00-31
          Sets the end-of-line character (default is carriage-
          return, 13 decimal) to any ASCII character from 00 to
          31 decimal.

     SET PACket-size 26-94
          Sets the packet size the micro _K_e_r_m_i_t should use when
          sending to _K_e_r_m_i_t-_C_M_S (default is 94).  _K_e_r_m_i_t-_C_M_S
          itself always sends one record per packet.  If the
          record is longer than 91, _K_e_r_m_i_t-_C_M_S sends packets of
          length 94 followed by a short packet.

     SHOw [ RECFM | END of line | QUOTE | LRECL | PACket-size ]
          Displays the current value of any one SET parameter.

     STATUS
          Displays the status of the last previous receive or
          send command.  BUG: `Disk full' is the last status



Printed 2/13/84         13 February 1984                        3






KERMIT-CMS(1C)   UCB Microcomputer Users Manual    KERMIT-CMS(1C)



          given for almost any file error.

     CMS <cms-command>
          Issues a CMS command from within _K_e_r_m_i_t-_C_M_S.  If the
          cms command fails, _K_e_r_m_i_t-_C_M_S says only `Command rc
          equals nn'.

     CP  <cp command>
          Issues a CP command from within _K_e_r_m_i_t-_C_M_S.  If the cms
          command fails, _K_e_r_m_i_t-_C_M_S says only `Command rc equals
          nn'.

     Some micro kermits do not send an error packet when they
     "abort", so _K_e_r_m_i_t-_C_M_S does not always know that the micro
     has stopped.  When connected back to CMS, _K_e_r_m_i_t-_C_M_S may
     still be  sending packets (they will appear on the screen).
     Type carriage-returns until _K_e_r_m_i_t-_C_M_S has done the maximum
     number of retries and aborts.  The error message will not
     indicate the micro abort, but rather that _K_e_r_m_i_t-_C_M_S gave
     up.

     If _K_e_r_m_i_t-_C_M_S must terminate a send or receive abnormally,
     an error packet is sent to the micro.  The _K_e_r_m_i_t-_C_M_S status
     command will display the same message.  _K_e_r_m_i_t-_C_M_S will
     retry 20 times on initialization packets and 5 times on
     other packets.

EXAMPLES  (see micro kermit manuals)
     Micro Kermits are interactive and will prompt for commands.
     The micro command connect initiates or continues a terminal
     connection with _C_M_S and a connect-escape character followed
     by `c' closes the connection and returns to the micro kermit
     (`^]c').  Each micro may use a different first character for
     the connect-escape, so the connect-escape is displayed at
     each connect.

     For the example below, the micro is turned on and booted
     with the disk containing the micro _K_e_r_m_i_t in drive A and a
     formatted data disk in drive B.  What you type is in bold-
     face; annotations appear in italics.

     A>                            # _M_i_c_r_o _p_r_o_m_p_t, _d_e_f_a_u_l_t _d_i_s_k _A:
     A>b:                          # _S_w_i_t_c_h _t_o _t_h_e _d_a_t_a _d_i_s_k.
     B>a:mkermit                   # _R_u_n _m_i_c_r_o _k_e_r_m_i_t.
     Kermit-80>                    # _T_h_e _c_p/_m _k_e_r_m_i_t _p_r_o_m_p_t.
     Kermit-80>set ibm on          # _S_e_t _f_o_r _I_B_M _C_A_L _m_o_d_e.
     Kermit-80>connect             # _C_o_n_n_e_c_t _t_o _t_h_e _c_o_m_m. _l_i_n_e.
                                   # _N_o_w _t_h_e _m_i_c_r_o _a_c_t_s _a_s _a
                                   # _n_o_r_m_a_l _t_e_r_m_i_n_a_l.
                                   # _D_i_a_l-_i_n _o_r _p_r_e_s_s _p_o_r_t-_s_e_l_e_c_t_o_r
                                   # _b_u_t_t_o_n _a_n_d _s_e_l_e_c_t _C_A_L _m_o_d_e.
                                   # _L_o_g_i_n _t_o _y_o_u_r _C_M_S _a_c_c_o_u_n_t.



Printed 2/13/84         13 February 1984                        4






KERMIT-CMS(1C)   UCB Microcomputer Users Manual    KERMIT-CMS(1C)



     ...                           # _C_M_S _m_e_s_s_a_g_e_s, _e_t_c.
     .                             # _N_o_w _y_o_u _a_r_e _t_a_l_k_i_n_g _t_o _C_M_S,
     .                             # _a_s _a _l_i_n_e _m_o_d_e _t_e_r_m_i_n_a_l.
     .kermit                       # _C_a_l_l _i_n_t_e_r_a_c_t_i_v_e _K_e_r_m_i_t-_C_M_S.
     Kermit-CMS>                   # _K_e_r_m_i_t-_C_M_S prompt.

     Kermit-CMS> receive           # _S_e_t _u_p _C_M_S _t_o _r_e_c_e_i_v_e _f_i_l_e_s.
     . ^[c                         # _C_M_S waits, return to micro.
     Kermit-80>send  *.for         # _S_e_n_d _a_l_l _f_o_r_t_r_a_n _f_i_l_e_s _t_o _C_M_S.
     ...                           # _M_i_c_r_o _d_i_s_p_l_a_y_s _s_e_n_d _p_r_o_g_r_e_s_s.
     Kermit-80>                    # _S_e_n_d _i_s _f_i_n_i_s_h_e_d.

     Kermit-80>connect             # _C_o_n_n_e_c_t _b_a_c_k _t_o _K_e_r_m_i_t-_C_M_S.
     Kermit-CMS> send frog file    # _S_e_t _u_p _C_M_S to send `frog file'.
     ^[c                           # _C_M_S waits, return to micro.
     Kermit-80>receive             # _R_e_c_e_i_v_e `_f_r_o_g._f_i_l' _o_n _m_i_c_r_o.
     ...                           # _M_i_c_r_o _d_i_s_p_l_a_y_s _r_e_c_e_i_v_e _p_r_o_g_r_e_s_s.
     Kermit-80>                    # _R_e_c_e_i_v_e _i_s _f_i_n_i_s_h_e_d.

     Kermit-80>connect             # _C_o_n_n_e_c_t _b_a_c_k _t_o _K_e_r_m_i_t-_C_M_S.
     Kermit-CMS> exit              # _E_x_i_t _f_r_o_m _K_e_r_m_i_t-_C_M_S.
     .^[c                          # _R_e_t_u_r_n _t_o _m_i_c_r_o.
     Kermit-80>exit                # _E_x_i_t _f_r_o_m _m_i_c_r_o _K_e_r_m_i_t.
     A>                            # _M_i_c_r_o _p_r_o_m_p_t, _d_e_f_a_u_l_t _d_i_s_k _A:

FEATURES
     The Kermit file transfer protocol uses 96 character check-
     summed packets, with ACK/NACK packet responses and timeouts.
     Only printing ASCII characters, control-A, carriage-return,
     line-feed are used for transmission, hence, packets should
     pass through most modems and networks unharmed.  Control
     characters are mapped into two characters, an escape charac-
     ter (usually `#') and a printing character corresponding to
     the control character (control-character exclusive or'ed
     with 40 hex).  _C_M_S does not preserve the eighth bit of each
     byte and is limited to text data.

IMPLEMENTATIONS
     Various microcomputer kermit versions are available from the
     CS Microcomputer Consultant (262 Evans Hall, 642-4072).
     Currently, IBM-PC, TRS-80 II (Pickles and Trout CP/M),
     KAYPRO II and Morrow MICRO DECISION versions are available.
     Versions for the Apple II, Apple II with cp/m card and the
     Compupro are under developement.  Source for many other
     machines with UCB changes is available, but versions built
     from them cannot be supported by UCB, since machines and
     staff time for testing are not available.

     Micro kermits to be used for file transfer with UCB CMS must
     have local modifications.  The UCB port selector echos
     received characters.  This requires that the micro kermit
     not echo locally.  More important, the echoed start-of-



Printed 2/13/84         13 February 1984                        5






KERMIT-CMS(1C)   UCB Microcomputer Users Manual    KERMIT-CMS(1C)



     header from a packet sent is received and retained by the
     serial port circuitry and confuses the packet driver into
     thinking its own tail is the next packet to be received.
     These UCB modifications should not interfere with use on
     other CMS systems except that `set local on' should be used
     after `set ibm on' since UCB ibm does not set local echo.

SEE ALSO
     kermit(1c), kermit-80(1c), kermit-86(1c), upload(1).

     _K_e_r_m_i_t _U_s_e_r_s _G_u_i_d_e, Fourth Edition (19 July 83), Frank da
     Cruz, Daphne Tzoar, Bill Catchings

     _K_e_r_m_i_t _P_r_o_t_o_c_o_l _M_a_n_u_a_l, Fourth Edition (4 November 83),
     Frank da Cruz, Bill Catchings

BUGS
     Most file or file name errors give a good message to the
     terminal, but _K_e_r_m_i_t-_C_M_S says only `Disk full' in the error
     packet to the micro.

     When ^Z or ^X are used to terminate a send or receive,
     _K_e_r_m_i_t-_C_M_S does not stop immediately or may even abort or
     hang.  This is due to protocol differences with our older
     _K_e_r_m_i_t-_C_M_S.

     If the record length sent is greater than 256, _K_e_r_m_i_t-_C_M_S
     will truncate to lrecl then act as though the next record
     begins with the 257th character.  If the record is exactly
     256 bytes, _K_e_r_m_i_t-_C_M_S writes one record of length lrecl then
     aborts for `disk full'.

     If `%' or `*' used in name or type field, _K_e_r_m_i_t-_C_M_S does
     not abort until the remote _K_e_r_m_i_t attempts to send, then
     several error messages preceed an abort for `disk full'.

     CMS Kermit will abort out of CMS into CP for various errors,
     including timeouts.  If you get the CP prompt, type BEGIN to
     restart _K_e_r_m_i_t-_C_M_S or IPL CMS to restart CMS.

     When connected to UCB cal, a BREAK must be used to interrupt
     terminal output since cal is half-duplex.  Many kermit ver-
     sions cannot generate a BREAK.

     CMS Kermit will not write zero length files, but will accept
     them.

     CMS Kermit cannot receive eight bit image files.

     Individual microcomputer Kermit bugs are listed in their
     documentation.




Printed 2/13/84         13 February 1984                        6






KERMIT-CMS(1C)   UCB Microcomputer Users Manual    KERMIT-CMS(1C)



     Please report other problems to micros@opal or the CS Micro-
     computer Consultant (262 Evans Hall, 642-4072).





















































Printed 2/13/84         13 February 1984                        7