R T T Y 2 0 0 1.3(CP/M) 9/01/83
                        by PERRY TAYLOR, W0SE.

           Prior to using this version of RTY.COM, please remove
      or erase any previous RTY.CFG file. This version will not work
      with an old RTY.CFG file.
           Set INTERUPT 5 on the RTTY PORT.
           When calling up RTY.COM for CP/M, the first thing that
      will be shown is the "CONFIGURATION" screen. Enter the values
      on this screen to fit your station. This builds a configur-
      ation record.  This configuration record can be saved on disk
      by pressing the "RED" key (ESC-Q).  The next time the program
      is called, this configuration record will be read from disk.
           The "SPLIT" on the screen can be set on the "CONFIGURE"
      screen. In the middle of the line is the time in hours and
      minutes. At the right of the line it will say "RELAY" if the
      relay mode is activated (it comes up that way).  If the mode
      is in use, the word "ON" will appear next to "RELAY".
           The line length can be set to any two digit length. Be
      aware that the RY's and the Quick Brown Fox, will not be
      shortened by this setting. 72 characters is maximum for RTTY
      operation with Teletype machines.
           This program can "LOG" both incomming and outgoing copy.
      In the field "DISK OUT MODE", "R" means "RECEIVE", "T" means
      "TRANSMIT", "B" means "BOTH" and "N" means "NEITHER". If it
      is "N" and the "CTRL-Y" is pressed, the "N" will change to "R".
      "DISK COPY MODE" comes up automatically if "CONFIGURED" for
      "R" or "T" or "B" and a fname.ext has been entered in the
      DISK COPY field. It is suggested that a fname.ext such as
      "SEPT01.AAA" be used so that each day's DISK COPY can be
      easily identified.
           Program the "PROGRAMABLE LINES "A" AND "B". Line "A"
      will be put in the "CONFIGURATION" record, line "B" will not,
      so it must be re-programed each time the program is called up.
           After finishing with the configuration record, begin the
      operation of the program by pressing the "f1" (ESC-S) key on
      the H-19.
           At the lower right corner of the screen will show
      "Receive Mode" if receiving and "Send Mode" if transmitting.
      Just to the left of the Mode indication there is a letter
      "B"or"A" and a number.  These are from the configuration
      screen and indicate Baudot or ASCII and the divisor for
      RTTY input and output speed.
           If the printer has been programmed "ON" and the middle
      of the 24th line says "PRINTER", that means that the printer
      is not "READY" or the "HANDSHAKE" line is not properly set.
           One of the newest features of this program is called
      3rd and 4th level BAUDOT. 3rd and 4th level BAUDOT is a prog-
      ramming method of sending the full ASCII character set over
      a BAUDOT channel. This program always transmits with 3rd and
      4th level characters, and is always available. Unlock the
      "CAPS LOCK", to send lower case data. The print on a TTY
      machine, or on a CRT (with other than this program), will show
      as if it were normal Baudot.  Of course, normal ASCII at 100
      WPM, can also be used, if desired. Turn on 3rd and 4th level
      receive by hitting the "RED KEY", (while in "RUN") and note
      the "X" on the left of the Split line.









                             Page 2.

           Only send lower case when the receiving program can copy
      them as the lower case puts in extra blanks, and makes a TTY
      machine work extra cycles, with no productive output. QRM and
      poor band conditions limit the accuracy of 3rd and 4th level
      reception, therefor 3/4 level reception may be turned OFF by the
      "RED KEY". These errors will be evident when lower case is rece-
      ived when upper case has been sent,or vice versa.
            Irv Hoff's IRTTY HDOS program will receive 3rd and 4th
      level Baudot and some of his HDOS and CP/M drivers will send
      3rd and 4th level.
           When using "Disk Copy or Disk Transmit", a word in the
      left half of the 24th line will show "IN" or "OUT", meaning
      "Disk INput or Disk OUTput".  If there is an error, then the
      error will be indicated next to the "IN" or "OUT" depending
      on which has the problem.
           From the "RUN" screen, the "WHITE" key (ESC-R) will
      allow you to enter a "fname.ext" to send without going
      to the "CONFIGURE" screen.  The entry made will be placed
      into the field called "Filename for Sending".  End by typing
      RETURN. "CTRL-D" calls up the file to be sent, and a second
      "CTRL-D",stops or aborts the file. Call up the file where
      ever in the pre-typing or transmit, the file should be sent.
           From the operation screen, type "CTRL-A" to see all
      of the controls that are available from the operation
      screen.  Type RETURN to exit this Help screen. No incomming
      data will be lost when looking at the control menu. The un-
      sent pre-typed data will be scrolled back into the pre-type
      area when the "RETURN" is hit.
           The FAST BREAKIN mode, toggled by the "ERASE" key, is avail-
      able. The letter "B" in reverse video will appear on the left of
      the split line, when operating "BREAKIN".The "CTRL-G" will send
      "-BK-", and turn off the transmitter with out the 4 N's. "CTRL-X"
      will send only 4 diddles, and then the pretyped data, when in
      this mode.
           The "DELETE" key  or "BACKSPACE" key may be used to erase
      data to make corrections in the pre-type area. Data in the pre-
      type area can be erased, including prior lines, until the char-
      acters being transmited are reached. Prior to transmitting data
      24 lines of the pre-type area is available for changes.






















                             Page 3.

      Following are the controls for RTTY 2001.3 (CP/M)

      CTRL-x means key x, while holding down the CONTROL key

              CTRL-A - Display this Help
              CTRL-B - Reset Receive and Print Buffers
              CTRL-C - Enter twice to return to CP/M
              CTRL-D - Toggle Disk Input to Transmit ON/OFF
              CTRL-E - Manual Relay Control (ZC)
              CTRL-F - Replay Previous or Manual (ZR)
              CTRL-G - Go to Receive After NNNNN (or -BK- fast bk)
              CTRL-K - Play Ident + Time/Date
              CTRL-L - Play String "A"
              CTRL-M - Same as RETURN Key
              CTRL-N - Plays Quick Brown Fox
              CTRL-R - Play RYRY (U*U* in ASCII)
              CTRL-T - Play Time/Date
              CTRL-U - Send WRU
              CTRL-V - Go to Receive Mode without NNNNN
              CTRL-W - Force DISK COPY write.
              CTRL-X - Go to Send Mode 32 (or 4 fast-bk) DIDDLES
              CTRL-Y - Toggle Disk Copy ON/OFF
              CTRL-\ - Clear Transmit Buffer
              CTRL-] - Transmitter Off Immediately
              @     - Play BELL
              ^     - Play String "B"
              ]     - Play line with fancy margin

              ESC RETURN - Send bare CR (PIX only)

              f2 Key or ESC T - 45.45 baud (Baudot 60 WPM)
              f3 Key or ESC U - 50 baud (Baudot 67 WPM)
              f4 Key or ESC V - 74.2 baud (Baudot 100 WPM)
              f5 Key or ESC W - 110 baud, (ASCII 100 WPM)

              ERASE Key - Toggle FAST BREAKIN mode ON/OFF
              BLUE Key  - Toggle RELAY mode ON/OFF
              RED Key   - Toggle 3/4 level receive ON/OFF
              WHITE Key _ Enter fname.ext for Disk Input


      This version for CP/M will respond to the following incomming
      commands, if preceeded by either a CR or LF.

              call signZC - Set RELAY to copy incoming,end with 4N's
              call signZR - Relay message, with VIA etc.
              call signZP - Replay previous t to the following incomming
      commands, if preceeded by either a CR or LF.

              call signZC - Set RELAY to copy    (colon)TIME       - Play WRU
              (colon)DISK       - Play WRU if in DISK COPY



W0NW AND W0SE....
 4N's