CLOCK  : A program to read the internal clock in KayPro 4-84 and
	 1985 versions of the KayPro 2X.

To call up the program just type CLOCK at the system prompt.
The program will give you a reading of the time and date as
stored on your internal clock.

The major source of this program is from the KAY*FOG bulletin
board in San Francisco.  I have modified it to run under
C/80 (Software Toolworks) by adding the assembly language
functions inp() and outp().  Functions are included to set the
clock but are not implemented at this time (i.e. you can hack
it yourself).

For owners of other computers:  You can alter this to work with your
machine by changing the port assignments, etc.  The #defines are
at the top of the source code.  You will need to know/change:

     a) PIO Initialization Port (if clock is attached to processor
	via the PIO, otherwise .. ).
     b) Clock function Port.
     c) Clock data I/O Port.

Also, the functions numbers given are for the NS-MM58167A clock
chip used in the KayPro's.  If your machine uses a different
clock chip it is your responsibility to check to see if these
codes are correct and to chnage them if not!

- Rick Warner
- 415-321-9446