Here are some things I found out about the Exec.          

1)  DOCINDEX.DOC- I  wrote  this the first month I had  my  Exec, 
   since,  as you know,  the write-ups for all the various  CP/M+      
   utilities  are scattered throughout the six books we  received  
   with the Exec. (and people thought the Osborne 1 book was hard
   to  use!)  If  you didn't get volumes 0-4  and  the  looseleaf 
   "Reference Guide", GET THEM! You can circumvent this scattered 
   approach  somewhat by buying the complete CP/M+  documentation 
   from Digital Research ($40. and maybe worth it), but even then
   you don't get write-ups of the programs written by OCC:  COPY, 
   CHARGEN,  COPYSYS,  and SETUP.  Voila!  my one page index.  It 
   tells  where the write-ups are and also on which of the  three    
   system disks the program appears.
     Also, at the bottom of the page is a quick translation guide 
   to let you converse with OsOne and other CP/M 2.2 users.

2) After you push the reset button, you have three choices:
  A) press return- normal load process
  B) press T- run the self-test until you press reset again
  C) press Tab- this inverts the drives; your top drive is now B: 
     and your bottom drive is A: (where your CP/M+ system disk  
     needs to be)
  X) The Exec will load any program you rename EXECST.COM as it
     loads the system.

3)Alternate character fonts
  A) first, load one; there are three on this disk. CHARGEN.COM
     on  your first CP/M+ disk will let you "read a file into the 
     character  set." Use INVERTED.CHR from this  disk- go  ahead 
     and  "write  the character set to the system tracks" as  the 
     Alternate character set.   Unless you  have already modified 
     your character fonts, your main and alternate character sets
     were identical. (you can un-do this later, if you want.)
  B) now, Reset, Return. (You probably call this "Booting", but I
     call it initial program load or "I.P.L.ing", so let's use
     terms we all understand) This loads your original (Main) and
     new (Alternate) character sets to the font RAM.
  C) Now,  as you keystroke,  hitting Control Tab will toggle you 
     back  and forth from your Main to Alternate  fonts.  If  you 
     used my INVERTED.CHR, isn't this a lot easier than using
     SETUP.COM each time you want inverted characters? 
  D)  The  other  fonts  I have  included  are  BOLDFACE.CHR  and 
     BOLDINVR.CHR,  which  I  find somewhat easier  to  read.  Be 
     creative! If you invent a nice font, please get it into this
     FOG library.

4)  Hardware- The Zilog Z-80A SIO2 Serial Input/Output Controller  
    is a monster! Let me quote from Zilog's Data Book:  
    "Two independant full-duplex channels,  with separate control 
    and status lines for modems or other devices. 
    "Data  rates of 0 to 800k bits/second with a 4.0  MHz  clock.   
    "Asynchronous  protocols:  everything necessary for  complete    
    messages in 5,  6,  7, or 8 bits/character.     
    "Synchronous protocols: everything necessary for complete bit 
    or byte oriented messages in 5, 6, 7 or 8 bits/character, in- 
    cluding IBM Bisync,  SDLC, HDLC, CCITT-X.25 and others. Auto-     
    matic CRC generation/checking, sync character and zero inser-
    tion/deletion, abort generation/detection and flag insertion"
    Etc. I'm not even sure what all of that is, but     what I do     
    understand really verifies what Ron Brown said at the January
    MtDOG  meeting;  that  is,  the Exec was intended  to      be     
    neither an improved OsOne nor an IBM-PC clone, but a communi
    cation machine.  (For comparison, the OsOne uses a 6850 Motor
    ola  asynchronous  communication interface  adapter,  with  a     
    speed  of  1200 bits/sec or less) Have you watched  a  Modem7      
    download at 9600 or 19200 bps? it's FAST!
       So,  since  the Data Book I quoted from above was the 1981  
    edition, why hasn't the UTE Universal Terminal Emulator prog-
    ram been released yet?  OCC isn't the only company using  the  
    Z80A SIO2,  is it?  I mean, the wheel must have been invented  
    already by somebody, and I want it. 
    
   5)Hardware- the  OsOne has a Western Digital 1793 floppy  disk 
    controller, while the OsEx has a 1797. The difference is side 
    select.  So come on,  aftermarket!  sell me some  half-height    
    double-sided drives with a modified BIOS or BDOS so I can use 
    them.  That's all that's needed.  That says 366K of formatted  
    storage per disk to me.

   6)Hardware- Parallel  printer connection. The documentation is 
    a mess, so pay attention.                
    Look  at  your IEEE 488 connector closely.  The  top  row  of 
    contacts is labled 12-1 (left to right), while the bottom row 
    is labled 24-13.  This is just like the picture on page R-443 
    (R means Reference Guide), and this matches the listing on p. 
    R-442.  BUT,  the  signal descriptions on R-442 are IEEE 488,    
    and  not Centronics or other printer manufacturers.
      The listing on R-445 matches the listing on 2-210, but the
    only  picture that matches these lists is in the Osborne  One  
    Reference Guide! 
      Using the listings on R-445 and 2-210, use this picture:

           23 21 19 17 15 13 11  9  7  5  3  1

           24 22 20 18 16 14 12 10  8  6  4  2  
_________________________________________________________________



     OSBORNE EXECUTIVE                           PARALLEL PRINTER      
     
     pins 1-8           Data Bits >>>>>>>>>>>>>>>>
     pin 11             Strobe >>>>>>>>>>>>>>>>>>>
     pin 15  <<<<<<<<<< Busy
     pin 19  <<<<<<<<<< Select, Ready, Demand
     pins 10, 12 14 16 18 20 22 24  Ground.

     Select,  Ready,  Demand, Service Request are different names 
     for  the  same signal.  My printer,  and maybe all  printers 
     alternate this signal with Busy. 


That's all I know for now, and the more I know, the more I know I
 don't know.  I'm Clark Wood, aka CWOOD, and I am a member of East
Bay Chapter of FOG, and a systems engineer for Kaiser Permanente
Medical Care Program, Oakland. I may be reached for talk or data
(at 300 bps) at (415)724-6668, evenings.     CWOOD       17FEB84