Free disk space in CP/M 3.0
 		by Kenji Nakadegawa 2/15/84

	While reading the february issue of the Foghorn I noticed a
plea for help with the problem of determining free space on disk drives
under CP/M 3.0.  I just finished converting a version of XDIR.COM to
run under both 2.2 and 3.0 so I'll tell you what I found out.

	Many "extended" directory programs use something called the
allocation vector to determine the used and free space on a disk.
The allocation vector is effectively a map of the used and free blocks
on the disk.  Reading through my CP/M 3.0 documentation I found that
banked 3.0 systems ( any system with more than 64K ram e.g. OsExec1 )
often keep the allocation vector in bank 0 which cannot be accessed by
transient programs.  That is why you get strange answers for space 
remaining when using programs like XDIR and SWEEP.  Fortunately there
is a new BDOS function number 46 that returns free space on a specified
drive.


	Here is an example of 8080 assembly code which shows a good way
to get the free space of a drive under CP/M 3.0.  I took this code straight
from the source listing of SUPER DIRECTORY PROGRAM v7.2 10/16/83 by
Bruce R. Ratoff.  I hope he doesn't mind.

	Bear in mind that all symbolic labels in this example were set by 
equates or ds statements elsewhere in the program.  For example in the CALL
CPM statement, CPM is a subroutine which calls bdos (location 05h) after 
saving all registers and VERFLAG is a memory location specified by a 
ds statement at the end of the program.

;
EXCERPT 1,
( This bdos call gets the version # for later conditional actions. )
;
	MVI	C,12		;get and save the cp/m version #
	CALL	BDOS
	MOV	A,L
	STA	VERFLG		;( The current cp/m version number is stored 
  	CPI	20H		   here.  See your documentation. )
	;
	; a carry flag set after the cpi 20h means you have cp/m 1.4

;
EXCERPT 2,
( The routine FREE20 gets the free space on the drive by the old method. )
;
FREE:	LDA	VERFLG		;check version #
	CPI	30H		;3.0?
	JC	FREE20		;use old method if not
	LDA	FCB		;get drive #
( The drive number is stored as A-P = 1-16 in this program.  CP/M wants the
  drive number as 0-15.  )
	DCR	A
	MOV	E,A		;use new compute free space bdos call
	MVI	C,46
	CALL	CPM

( The number of free sectors is returned as a 3 byte binary number in 
  the first three bytes of the current DMA buffer which is in this case
  the default buffer at 80h.  The format is lsb in 80h, midsb in 81h, and
  msb in 82h.  Since the number represents 128 byte sectors and we want
  it in 'K' we have to divide it by 8 which in binary is 3 shift rights. )

	MVI	C,3		;answer is a 24-bit integer
;
FRE3L1:	LXI	H,BASE+82H	;answer is in 1st 3 bytes of dma adr
	MVI	B,3		;convert it from sectors to k
	ORA	A		;by dividing by 8
;
FRE3L2:	MOV	A,M
	RAR
	MOV	M,A
	DCX	H
	DCR	B
	JNZ	FRE3L2		;loop for 3 bytes
	DCR	C
	JNZ	FRE3L1		;shift 3 times
	LHLD	BASE+80H	;now get result in k
	SHLD	SAVFRE		;store it
 
( We now have the free space on the drive stored at location SAVFRE in
  binary or hex.  You can use the hex word to 4 decimal digit output
  routine which I assume you already have somewhere else in the program
  to output this number to the console or whatever. )

			END