HOSTCM.BAS is an Osborne specific terminal 
interface program to the HOSTCM mainframe comms
program distributed by WATSOFT, Inc.  It is a 
little crude, but will allow error free uploading
(the only thing I needed) of a file to an IBM 
mainframe running VM/CMS.  After establishing
comms with the mainframe, and booting HOSTCM on
it, load up BASIC on your OZZY (make sure disk
is SETUP for your modem's proper baud rate) and
run HOSTCM.BAS.  Everything you type will be sent
to the mainframe, with the needed checksum and line
end chracter appended.  It will also be echoed
to your screen in half-intensity.  TYPE "BYE" to
halt the program, and type "FILESEND" to send a 
file, all other input typed at the } prompt will
be sent to the mainframe.  Note that replies
from the IBM will take a few seconds to be 
processed by the program.  It uses a novel scanning
method to get the host response.  This is needed
since the program talks to the modem by switching
the console to the serial port.  If it didn't 
timeout, a missed host response would lock the
keyboard.  The program will retransmit a record
if negative acknowledged by the host, and will
beep the bell if an error or text message is 
sent by the host during a file transfer.  The 
message will of course be displayed on the screen.
Press the "/" key to abort a file xfer.  The >
prompt is displayed when the program looks for 
this signal, but just hold the key down until you
get the } prompt back (less than five seconds).
  For further information, check with your mainframe
system manager, or WATSOFT.  You'll need a list of
the valid HOSTCM commands at least.

Enjoy!

Bob Scott
Silicon Valley Chapter
FOG
July  1983

(edited by Jim Woolley)