OSPLNK70  version 7.0  dated 11/82
         by Jim Woolley, FOG Disk Librarian

OSPLINK is a CP/M transient program which allows the 
user to send/receive ASCII text files to/from a 
remote computer using a modem.  Text data will be 
displayed on the console and may be optionally 
printed on the CP/M list device.  No error checking 
protocol (such as MODEM7) is accomodated.

OSPLINK is intended primarily for the business user 
who wants a simple program for communication with a 
corporate computer or with a service bureau such as 
The Source, CompuServe, or Dow Jones.  ASCII text is 
generally the only transmission of interest in such 
cases.  Files are usually small, and the impact of a 
lost bit during communication is not disastrous.  
Besides, the host computer probably does not support 
a special protocol like MODEM7.

OSPLINK is customized especially for the Osborne 1 
portable business computer.  One unique feature of 
this version is buffered printing on the CP/M list 
device interfaced via the Osborne IEEE-488 or 
Centronics parallel port.  Such printers may include 
Epson MX, NEC 8023, C. Itoh 8510, or Okidata 
Microline.  Another feature is use of direct Osborne 
serial/modem port input/output (I/O) routines and 
BIOS console and printer I/O functions for improved 
communication speed and reliability.

Text files may be transmitted from either disk drive 
to the host.  The host computer's line 
acknowledgment prompt during file transmission 
(normally linefeed) may be dynamically defined.  
Text from the host may be captured in memory buffer 
(about 38K bytes, or over 20 continuous minutes at 
300 baud), then saved on disk.  The bell will sound 
when memory buffer is within 1k bytes of full.  
Incoming text capture will be discontinued before 
the buffer overflows.

All transmission is via 7-bit ASCII code; therefore, 
8-bit data such as .COM files or MBASIC compressed 
.BAS files will not transmit properly.  The 
fundamental test is:  If use of the CP/M TYPE 
command with the file of interest produces garbage 
on the screen, then the file may not be sent using 
OSPLINK.  WordStar Document mode files may be 
transmitted; however, the result is similar to a 
Non-Document mode file.  In other words, the result 
may be simulated using PIP CON:=filename.typ[Z].

OSPLINK was derived from the public domain program 
PLINK originally written by L.E.Hughes (EDCAM) 7/77, 
with revisions by Keith Petersen (W8SDZ), Tom 
Jorgenson, Steve Vinokuruff (Vanc CBBS), Dennis 
Breckenridge (Burnaby CBBS), Bruce Ratoff (Iselin 
RCPM), and Ben Reagan (Lynnwood, WA).

OSPLINK version 6.4 was submitted to the First 
Osborne Group (FOG) Disk Library by Byron McKay 
(OxGate, PicoNet, and FOG).  That version used 
direct Osborne serial/modem port I/O.  The author 
was not identified.

Significant additions and corrections were made by 
Jim Woolley, FOG Disk Librarian, to create version 
7.0.  In particular:

 1.  Added buffered printer output to the CP/M list     
     device configured on the Osborne parallel port. 

 2.  Corrected text file transmit routine.

 3.  Added ability to change host acknowledge 
     (trigger) character during session.

 4.  Added help reminder of control commands.

 5.  Cleaned up read-console-string routine.

 6.  Cleaned up modem routines. Added runtime logic 
     to move code above 4000h (shadow memory), 
     thereby keeping size of .COM file to minimum.

 7.  Improved user interface.

 8.  Eliminated non-Osborne related code.


An OSPLINK session is initiated by placing 
OSPLINK.COM in drive A.  At the A> prompt, type 
OSPLINK followed by <RETURN>.  Modem connection with 
the host computer may be made before or after 
starting OSPLINK.

The following control codes (commands) may be 
initiated from the keyboard during a session: 

Control-E      Exit OSPLINK to CP/M "warm-boot".

Control-T      Transmit ASCII file to remote 
               system.  Asks for drive (A or B) and 
               filename.typ.

Control-C      Aborts transmission of file to remote 
               system.  If used when asked for 
               drive, aborts ^T or ^W.

Control-Y      Switches between saving and ignoring 
               incoming ASCII data in RAM buffer, 
               for later transfer to disk.

Control-W      Writes RAM buffer to disk.  Asks for 
               drive and filename.typ.

+ + + + +      Revisions by Jim Woolley, 11/82

Control-P      Toggles list device (printer) on/off. 
               A 256 character buffer is used to 
               accomodate printer busy conditions.  
               Printer interface must be on Osborne 
               parallel (IEEE-488 or Centronics) 
               port, which is assumed much faster 
               than the modem.

Control-A      Permits reset of host computer's 
               acknowledgment character.  Default is 
               linefeed. May be changed to, for 
               example, > or * or ? or @ or # or &, 
               etc. Acknowledge prompt is only used 
               during ^T file trasnmission.

Control-R      Displays reminder of commands.

Following apply when prompted for filename (similar 
to keyboard entry at CP/M level):

Control-H      Backspace when in command mode 
or <-- arrow   (e.g. ^T or ^W).

Control-U      Aborts current line when in 
or Control-X   command mode.

+ + + + +

Note: all other control codes are passed to modem 
output and may be interpreted by the remote system 
as various control functions.

A "trigger" character is a response (acknowledgment) 
sent by the host following receipt of a line 
(carraige return character) indicating that it is 
ready for the next line.  The "trigger" charcater is 
set to "lf" (linefeed) by default.  An optional 
trigger character may be passed via the command 
line; for example,

     OSPLINK B      will set trigger to "bell"

The following options are allowed on the command 
line:

	1. B = bell  07h

	2. X = xon   11h

	3. U = upload; no trigger check at all (this 
               option may only be entered via 
               command line)


Any other ascii character on the command line will 
be converted to upper case and taken literally as 
the trigger.  Only the first character is scanned.  
Examples are > or * or ?.  Control-A permits trigger 
character to be reset during a session.