(METTS-G.OKI)

OKITALIC.COM
for CP/M & Okidata 92/93

AUTHOR: Glenn Metts
        Fog Member #10220
        Osborne Users Club of Houston (OUCH)

OKITALIC downloads an italic character set to the "downline loadable
character generator."  Italics can then be used with WordStar or any
other program by sending the sequence 1Bh,32h (ESC 2) to the printer.  
Although it has been used on an Osborne 1 DD with an Okidata ML92 with
a parallel interface, it should run on any CP/M system with the ML92
or 93 printer with serial or parallel interface.       

This is the same as the Epson FX italic characters except that the     
lower case "j" has no dot.  The italics can be printed in 10, 12 or 
17 cpi (normal or double width), superscript or subscript, or underlined 
by combining control codes.

Listed below are the patches I use with WordStar 2.26.  The only tricky 
one is ^PR (double width characters).  Evidently, WordStar doesn't send 
the ^PN sequence unless a ^PA has been previously encountered in the 
text (and vice versa).  Since the ^Px sequence is needed to shift from 
double-width back to normal width, it is necessary to put in ^PA^PN to 
shift back to 10 cpi or ^PN^PA to shift back to 12 cpi.  You can avoid 
the hassle if you don't need double-width by leaving the code out for 
USER4:.  Italics are started with ^PE and ended with ^PW (for data 
processing mode) or ^PQ (for correspondece mode).

Label   Contents (Hex)  Command  Action
PALT:   01,1C,0,0,0     ^PA      Starts 12 cpi & cancels double-width
PSTD:	01,1E,0,0,0     ^PN      Starts 10 cpi & cancels double-width
ROLUP:	02,1B,4A,0,0	^PT 	 Starts superscripts or ends subscripts
ROLDOW:	02,1B,4C,0,0	^PV	 Starts subscripts or ends superscripts
USR1:	02,1B,31,0,0	^PQ	 Starts correspondence quality mode
USR2:	02,1B,30,0,0	^PW	 Starts data processing mode
USR3:	02,1B,32,0,0	^PE      Starts italics
USR4:	01,1F,0,0,0     ^PR	 Starts double-width letters
RIBBON:	02,1B,43,0,0 	^PY	 Starts continuous underline
RIBOFF:	02,1B,44,0,0	ditto    Cancels continuous underline
PSINIT:	02,18,0D,0,0,0,                   
         0,0,0,0,0,0,0,          Initializes printer with <CR> and
         0,0,0         		 "clear buffer"

If you are using the ML92 with pin-feed, as I do most of the time, the
following changes may be useful.  They reset the top margin to zero and
the bottom margin to 11 lines.  Since the tear bar is an inch above the
print head, Wordstar can start and finish with the paper perforations
at the tear bar, while leaving a one-inch top margin and a half-inch 
bottom margin.
   
INITPF:+5  0,0,0    Sets top margin to zero lines 
INITPF:+D  0B,58,0  Sets bottom margin to 11 linesŠ<EOF>