This library contains the following Osborne 1 specific 
programs:

	ROMDUMP.MAC
	ROMDUMP.COM
        SCPRT2.MAC
        SCPRT2.COM

The first two are the source and assembled versions of a program to copy 
the contents of the O1 ROM to the TPA starting at 0100h.  You may then
save a copy of the ROM to a disk file using the CP/M SAVE command.
to use just type:
  ROMDUMP
The program will immediately print something like:

  ROM copied...Ready for SAVE 16 ROM.COM

Typeing the SAVE... stuff will produce a disk copy of the ROM file 
on the currently logged disk.  You may then peruse this file with
DAZLSTAR, ZSID, etc.  This handy both for the curious, or for those 
interested in sticking their own code into the ROM, or for those who
just want to add their name to the boot prompt message.  The later 
two of course require a ROM programmer and a blank ROM.  You may also
use UNLOAD on the ROM.COM file to produce an INTEL HEX format file
which some ROM burners will accept. (Note that you may have to manually
'back up' the code 100H bytes, since UNLOAD is hardwired into a 0100H
ORG location, and the ROM really starts at address 0000H)

The second program is just a simple OSBORNE 1 screen dump utility. It
is invoked by typing "SCPRT2" at the CP/M system prompt.  I really
intended for this to be incorporated into other programs to provide them
with a screen dump capability, so I've included the source code.  If 
you change the one JP	P,.... instruction to a JR of some type (just a
couple of new instructions) the program would be completely devoid of
absolute jumps, and hence totally relocatable.  You could then plug it
into an already assembled program (like MEX) without having the source
code...my next project.  Note that this screen dump business is some
what nontrivial, as the current 'top' of the Ozzy screen changes with
each line scroll, hence you have to uncover the where the current top
is to start.  One approach is to find the cursor, but unless the little
critter is on the bottom line, that don't always cut it.  The method
presented seems to work fine (checking the system byte VERTOFF).  

Both of the included source files are in Zilog format, hence require
a Z80 assembler to fool with.....have fun.

Bob Scott
SV FOG
Sept 1985
d source files are in Zilog format, hence require
a Z80 assembler to fool with.....have fun.

Bob Scott
SV FOG
Se