;;07-02-85

                          IFG.DOC v1.4
                            07/10/85
Eric Gans
French Dep't UCLA
Los Angeles, CA 90024

Version 1.4:  These files are for use ONLY with GSUB 1.4!! Please 
get rid of earlier versions:  they won't work with GSUB14.  These 
files  are substantively the same as in v1.3,  but the  addresses 
are  different  and  new code has been added  to  allow  for  the 
message-display and input-request functions in GSUB 1.4.


     IFG,  ELSEG,  ENDIFG and GOTOG are faster and more versatile 
than the corresponding IF, ELSE... series written for SUBMIT. (To 
be  fair,  a  good  deal of IFG was taken from  IF.ASM.)  Out  of 
deference to the latter,  I have added a "G" to all the commands; 
if GSUB becomes the standard CP/M batch utility,  I will take the 
G's off in a future version.

     IFG offers the same command structure as IF,  plus a  couple 
of  enhancements.   As  with  IF,  only the first letter  of  the 
commands count (as long as there are no spaces). The options are:

IFG N[ull] = if command line is null (e.g.,  a null variable in a 
     SUB file)
IFG E[xists] filespec
IFG A[mbig] filespec = if the filespec contains wildcards
IFG M[issing] filespec = if the filespec cannot be found
IFG Z[ero] filespec = if filespec either zero-length or missing

Additions:
IFG D[rive] dr = if current drive is dr
IFG U[user] userno = if current user is userno

Whether  these conditions are true or false,  IFG will print  the 
information  on  the screen (another improvement).   The  command 
structure is predictable:  if the condition is true, what follows 
the IFG will be executed; if it is false, an ELSEG will be sought 
else commands will be executed following the ENDIFG.  (Leave this 
out  and you get an error message.)  Since GSUB operates  in  the 
memory rather than on disk, IFG et al perform far faster than the 
IF series.

ELSEG  merely skips to the next ENDIFG since,  like ELSE,  it  is 
only executed when the original condition was true.

ENDIFG is, like ENDIF, a one-byte file consisting of a "ret".

GOTOG  Format: gotog n [#c]

Unlike  GOTO,  GOTOG  can jump backward as well  as  forward  and 
includes a count option,  permitting the creation of loops.   The 
command  to  go to is numbered according to its position  in  the 
series of commands (in the SUB file or in immediate  mode).  Only 
CCP commands are counted, not internal file commands in GSUB. You 
may include the numbers as comments in the SUB file,  but this is 
not necessary.

GOTOG n performs an unconditional goto.   To create a  loop,  use 
the  count option GOTOG n #c where "c" is the desired  number  of 
executions.   The  command number "n" must be between 1 and  255; 
"c" is a single (hex) digit from 1 to F (=15). (If you don't like 
hex numbers, just use the digits 1 through 9.)

Examples:
ifg e blurk.com     ;tests existence of file
zlonk {^nr354|}     ;commands between {} don't count for GOTOG
<The directory will now be listed>   ;message to be displayed
dir
gotog 7             ;goes to 7th command in list
elseg               ;if blurk.com doesn't exist, then rename
rn zlonk.com=blurk.com
era *.bak
endifg

ifg u 10       ;if user 10, edit zap.txt
ws zap.txt
elseg
u 10           ;else change user*
gotog 2        ;& go back to edit (the "else" clause will be 
endifg         ;skipped, as always)
          *unlike  SUBMIT,  GSUB  won't get lost when you  change 
          user numbers, but IFG &c must be accessible on disk

blurk
zap
zlonk
gotog 2 #a  ;will go back to zap and execute the loop 10 times

NB that GSUB converts all lower-case to upper case (except within 
the display-message brackets <...>) when it creates its buffer in 
high memory.


I  will  continue  do my best to implement your  suggestions  for 
modifications or enhancements.