Turbo Pascal Kermit  CP/M-80

Author: Jeff Duncan
Language: Turbo Pascal
Version: 1.1
Date: 29 December 1984

Turbo Kermit Capabilities at a Glance

Local Operation   Yes
Remote Operation  No
Transfers Text Files  Yes
Transfers Binary Files  Yes
Wildcard Send   No (planned feature)
^X/^Y Interruption  No
Filename Collision Avoidance Yes
Can Time Out   No
8th Bit Prefixing  Yes
Repeat Count Prefixing  No
Alternate Block Checks  No
Terminal Emulation  No
Communications Settings  Yes (parity)
Transmit Break   No
IBM Communication  No
Transaction Logging  No
Session Logging   No
Raw Upload   No
Act as Server   No
Talk to Server   Yes
Advanced Commands for Server No
Local File Management  Yes (dir)
Command/Init Files  No
Printer Control   Yes

  This  is  a  third  release  of  Turbo Pascal Kermit for CP/M 80.  It is not
complete or fully debugged.  Comments, fixes, bug reports, etc.  are  welcome.
I am available at (617) 839-5673 evenings, or at

            3 Anderson Lane
            No. Grafton, Ma. 01536

  Much  thanks  go to Bernie Eiben for help and encouragement, and to Columbia
University for creating  Kermit.   Thanks  also  to  those  who  have  offered
comments, fixes, and enhancements.

Modification History:

29-DEC-84 Jeff Duncan - Extensively remodeled Turbo Kermit.  Major areas
                        changed were:
V1.1

1. Binary files will now be transmitted and received correctly.

2. Added more extensive comments to entire program.

3. Added section in documentation to list operating system dependent code.

4. Announce procedure added by Alan Hull temporarily eliminated to keep
   basic release generic. (but I liked the logo)

Limited/no testing has been done in the following areas:

1. 8'th bit quoting.

2. Generating parity.

3. Printer logging.

V1.0

08-DEC-84 Alan Hull - Corrected Directory function to work on all drives.
Version 0 was hardcoded to drive C only.  Enhanced the directory
display to 5 columns, better filename display.

Added Sign-on logo for DEC Robin.  Easily changed for other
systems by recoding announce procedure.

Added file delete option (any drive).

Updated Help, command prompt, and all routines affected by the
above enhancements.

V0.0

05-DEC-84 Jeff Duncan - Initial release of Turbo Pascal Kermit for CP/M-80.


         Turbo Pascal Kermit Description

  The  motivation  behind  writing a Kermit implementation in Turbo Pascal was
principally to have a generic Kermit that would run on a  variety  of  systems
without  any  modification.   Turbo  Pascal  has  turned  out  to be a popular
language because of its speed, ease of use, and features.  It  seemed  logical
therefore  to  write  a  Kermit  in  Pascal  that could be transported without
difficulty to many machines.

  This program is still in its developmental stage.  There are still some bugs
that have to be worked out, and there are features that should be added, but I
hope this is a good starting point!

  The original goal of this project was to produce a Kermit that could compete
speed-wise with an assembly language version, but be written in a higher level
language  that  would  be easier to maintain and could be used in a variety of
systems.  It would also be easily adaptable to other  operating  systens  that
can  run  Turbo Pascal such as MS-DOS and CP/M-86.  To a large extent, this is
true.  There is  more  operating  system  dependent  code  than  I  originally
intended,  but  most of it is in a few routines that could be rewritten easily
for another operating system.  The performance is good considering that it  is
written in Pascal.  Connect mode appears to be glitch-free at 9600 baud, and I
have  had  no  problems  with  file tranfer due to speed at 9600 baud as well,
using two DEC VT-180's, running both normal CP/M and  ZCPR2.   The  degree  of
buffering on various computers could affect this.

                      Command Summary

*****************************************************************************

                    IMPORTANT NOTE

  To  abort  form  send  or  receive  use -- ^D -- NOT ^C.  This is because of
testing problems using ^C.

*****************************************************************************




  I  have  no  intention in this preliminary documentation to provide detailed
descriptions of all the commands in this version of  Kermit.   They  are  well
documented  in  the  Kermit  Users  Manual and the Protocol manual provided by
Columbia.  I hope  that  the  following  will  help  show  what  features  are
available  and  any  bugs  or  unresolved  issues there are in the implemented
commands.

  A note about the command parser: This parser will not allow ?  and escape as
in  DEC-20  and  others.   However,  the  minimum  unique abbreviation will be
recognized as a valid command.  A good portion of the parser to  do  this  has
been  written,  and  may be added to Turbo Kermit at a later time.  Both upper
and lower case letters are acceptable as input.

Connect - Establish  a  virtual  terminal  connection to a host connected to a
          serial port on the  computer.   The  current  version  supports  the
          reader/punch  port  and  the  UC1: port, because it was written on a
          VT180.  Selection of port is done  by  the  SET  command,  and  port
          switching  is  done  by  manipulating  the  CP/M  standard IOBYTE at
          location 3.  I/O is done by calls to BIOS via Turbo Pascal  standard
          functions  and  procedures.   Escape  from CONNECT mode is done with
          ^\-C.  Operation, as mentioned before, appears correct at 9600  baud
          on a VT180.

Send -    Send  the  selected file to the remote Kermit.  At present wildcards
          are not supported, but hooks are there to add this feature.

Receive - Receive  file(s) from the remote Kermit.  Files will be received and
          stored in the same names that the remote  Kermit  specifies  in  its
          file  header  packet(s).   Multiple  files  may  be  received.  This
          command does not request files from the  remote  Kermit.   It  waits
          until  the  remote  Kermit  initiated  the  file  transfer.   If the
          filename being sent already exists, Turbo  Kermit  will  attempt  to
          create  a  unique  filename  for the file.  If this is successful, a
          message to this effect will be printed on the screen.

Get <filespec> -
   Request  from  a  remote  server  that certain file(s) be sent.  The
          filespec as typed is sent exactly to the remote Kermit.  Files  will
          be received and stored as in receive mode.

Bye -   When  sent  to  a remote server, log out the server, and log out the
          host.  If the logout of the server is successful, exit to CP/M.   If
          it  is unable to logout the remote host, Turbo Kermit returns to the
          prompt level.  This is to allow reconnection to  the  remote  system
          for further action without having to reload Kermit.

Finish -  Log  out  the  remote server.  If this is unsuccessful, a message is
          displayed at the terminal.

Logout -  Logout the remote server and the remote system and remain in Kermit.

Dir -   Print  a  directory listing for any drive.  Wildcards are allowed in
          the filespec following the Dir command.

Era -   Erase  any file(s) specified on any drive.  Wildcards are allowed in
          the filespec following the Era command.

Set -   Set  a  Turbo  Pascal  Kermit  parameter.   The  following are valid
          parameters:

   PRINTER - on of off.  WIll turn the printer on for logging a virtual
          terminal connection only.

   PARITY - mark, space, even, odd, or none.  this will convert the 8th
          bit  of a file transfer to the appropriate parity for file transfer.
          Parity is stripped on receive.  Any parity except none will  attempt
          8th bit quoting if binary files are selected.

   FILE - Binary or Ascii.  If ASCII is selected, all files transmitted
          will  be terminated on the first ^Z detected in the file.  Receiving
          will continue until an end of file packet is received.  When  binary
          is  selected,  the  files  will  be sent until CP/M signals the last
          sector.  As mentioned above, binary file transfer will be  attempted
          using 8th bit quoting if parity other than none is selected.

   PORT  - Currently only reader/punch and UC1: are supported using the
          CP/M standard IOBYTE.

      Program Organization

  Because  the program is not fully documented, the following is a description
of the organization of the program to help find what's where.   Because  Turbo
will  only  handle  a  limited size file, there are a number of include files.
This was also done so that the program will compile  in  memory  to  speed  up
debug.

  The files required are:

   K.PAS - program header, include's, and main procedure
   KINIT.PAS - type, const, and var declarations, and general utilities
   KDIR.PAS - directory listing procedures
   KOPEN.PAS - open a file on the micro
   KDISPLAY.PAS - display procedures for send and receive
   KHELP.PAS - help displays and set parameter procedures
   KREC.PAS - general receive procedures
   KTERM.PAS - virtual terminal mode
   KSEND.PAS - sending a file to remote
   KREC1.PAS - receiving a file from remote
   KCMD.PAS - command parser

  The following is a list of procedures and functions by file:

File - K.PAS
           none

File - KINIT.PAS

  Tab  generates a string of spaces
  Ctl  conversion to/from control character
  Char40  adds 40 hex to integer to produce character
  Unchar  subtracts 40 hex from character to produce
    integer
  Ltrim  removes leading spaces from string
  Rtrim  removes trailing spaces from string

File - KDIR.PAS

  Adjust_Fn expands string to CP/M filename format
    also inserts wildcard characters
  Init_Fcb sets up FCB for filename search
  Searchfirst calls bdos for searching for filename
  Searchnext calls bdos for searching for filename
  Dir  generates directory listing
  Delfile  delete specified file(s)
  Deletefile calls BDOS for the delete

File - KOPEN.PAS

  Open_File tries to open a file
  Open_For_Write tries to open a file for Writing

File - KDISPLAY.PAS

  Displayt base display for send mode
  Displayr base display for receive mode
  Update  update the display

File - KHELP.PAS

  Show  show local parameters
  Help  display help message
  Set_Param sets up local parameter

File - KREC.PAS

  Get_Char tries to get a character form port
    also monitors crt for abort or retry
  Receive_Packet get a complete packet from remote

File - KTERM.PAS

  Send_Char send a character to port
  Term  virtual terminal mode

FILE - KSEND.PAS

  Check_Init sets up parameters from send init dialogue
  Check_Ack checks ack packet for correctness
  Send_Packet send a packet to remote
  Build_Packet put checksum and parity on packet
  Quit  return to CP/M unconditionally
  Finish  handle bye, finish, and logout commands
  Send  send a file to remote host
  Get_File_Data build a data packet
  Sinit  send init state handler
  Sheader  send file header handler
  Sfile  send file data handler
  Seof  send end of file handler
  Sbreak  send break handler
  Send_Ack send an ack packet
  Send_Nak send a nak packet

File - KREC1.PAS

  Rheader  receive file header packet
  Get  send server get command
  Rinit  receive send init packet
  Expand_Packet disect received data packet
  Rfile  receive file data

File - KCMD.PAS

  Parse  parse the command line
  Prompt  display a prompt
  Get_Command_Line dispatch command per typed command line


       System Dependent Code

  The  original  intent  of  Turbo  Pascal  Kermit was to produce a version of
Kermit that would be written with a minimal need for  system  dependent  code.
Turbo  Pascal provides general procedures for screen handling that obviate the
need for much system (or terminal dependent) code, but there  are  some  areas
that must be written with the target system in mind.  Somethings just can't be
done without these routines, and speed is enhanced by using them.

  However,  Turbo Pascal is quite fast.  In this implementation, I have had no
need to add assembly language routines to implement the  most  critical  speed
related routines, terminal mode and send/receive packets.  I have, though, had
to  add  system  dependent code.  This version of Kermit is designed to run on
CP/M-80 only.  In all the terminal and communications  port  routines  I  have
used BIOS calls.  These have allowed a terminal mode that will operate at 9600
baud.  BIOS calls have also been used to send and receive data packets.  These
are  not  quite as fast, but appear to limited to slightly less than 4800 baud
with no buffering of data in the basic operating system.  The  other  area  of
this  program  that  uses  CP/M-80  system  calls  is  the  directory printing
routines.

  I  was  planning  to separate all the system dependent code into one module,
but decided against that because there is too much of it and the routines span
several blocks that do not logically fit together.  Instead, this  section  of
the manual for Turbo Kermit is intended to detail those areas that have system
dependent  code  for those who may be interested in modifying this version for
other operating systems.

   1. Directory Listings

      The  directory  listing  code of Turbo Kermit are almost entirely system
    dependent.  The directory information is extracted via BIOS calls, and the
    directory mask is converted to upper case and expanded to be  readable  by
    CP/M-80.   This  will  probably  be  different  for  most  other operating
    systems.

   2. IOBYTE

      All  communications  (terminal  mode  and send/receive packets) are done
    with CP/M Bios calls.  In order to interrogate the various ports, the CP/M
    IOBYTE is changed to reflect  the  desired  communications  port  desired.
    This  version  presumes  that  the  IOBYTE  is located in RAM at 0003 hex.
    Three  variables  are  used  to  set  the  IOBYTE.   They  are   'iobyte',
    'base_iobyte',  and  'port_iobyte'.   'base_iobyte'  is a copy of 'iobyte'
    when the program is entered.  'port_iobyte' is initially set to  point  at
    the  reader/punch port.  This variable can be changed using the 'SET PORT'
    command (procedure located in file 'khelp.pas'.  Additional ports  can  be
    added in this routine.

  3. Sending characters to communications port

      The include file 'kterm.pas' includes the virtual terminal mode, and the
    only  procedure  that  transmits  to  the remote ports, 'send_char'.  This
    procedure resets the IOBYTE to point at the appropriate port and sends the
    character using a BIOS call.  This routine could  be  easily  replaced  to
    send a character on another type of system.

  4. Receiving packet data

     When  receiving  packet  data  from  a  communications  port, a procedure
    located in the include file 'krec.pas' is used.   This  procedure,  called
    'get_char'  performs  the  same type of port switching required by CP/M to
    check status as virtual terminal mode.  This routine can  be  replaced  by
    something a different operating system can understand.

  5. Virtual terminal mode

     Virtual terminal mode is riddled with CP/M BIOS calls.  Because CP/M does
    not  allow  port  status  to  be  read except when the port is the logical
    console, termianl mode is a loop that changes the ports to be the console,
    and checks the status.  When the status indicates a character is available
    at the communications port, it is fetched and sent to the screen.  When  a
    character  is typed at the keyboard, it is sent to the communications port
    via the 'send_char' procedure above.   Terminal  mode  would  have  to  be
    rewritten for any other type of system.

     There  is  no terminal emulation package in this version of Kermit.  This
    would be difficult to accomplish and still maintain any reasonable speed.

  6. Opening files

     File  opening  and  closing  is  all  done  with Turbo Pascal procedures.
    However, the size of the the filenames is hard encoded into  the  routines
    so  some messing around will be required for systems that handle different
    length filenames.

     Note also that the procedure 'adjust_fn' located in 'kdir.pas' is used to
    find  places  to  insert  characters  in the filename if a naming conflict
    occurs when opening a file for  writing.   If  you  change  the  directory
    listing  routines,  leave  that  one  in  there, or implement the filename
    conflict routine differently.

  7. Deleting files

     Deleting  files  is done with CP/M BIOS routines.  This will also have to
    be rewritten for another system.