SCRPRINT.DOC
                              ------------
                     Documentation for SCRPRINT.COM
                          v1.0 - E. Meyer 1/85

            [Note: for the Osborne Executive computer only.]


     SCRPRINT allows you to get a printout of whatever is currently on your
Osborne Executive CRT screen at any time, without disturbing the screen or any
software you may currently be running.

            To install it:   A>SCRPRINT    [or SCRPRINT ON]

            To remove it:    A>SCRPRINT OFF

            To print the screen:  type control-underline (^_)

When "installed", SCRPRINT remains part of your CP/M Plus operating system -
technically, an RSX (Resident System Extension).  It does nothing until you
type ^_, at which point it will print the screen.  When it's done, it will
beep once, and you will be right back where you were before, ready for input
to whatever program (if any) you were running.
     Do not install it more than once: multiple copies of the RSX waste your
RAM space, and may interfere with one another.


                           RESTRICTIONS ON USE

     There are several restrictions on the use of SCRPRINT.  First, since it
has to access video RAM, switching bank 7 in must not disturb the RSX itself:
it must lie safely above address E000h.   If there are already RSXs installed,
and the installation of SCRPRINT would place it below E000h, you will get the
error message "++ Address Error ++", and SCRPRINT will not install.
     Second, remember that sometimes CP/M does input by line, rather than by
character (for example, from the A> prompt).  In this case your ^_ character
will not be recognized until you hit RETURN; then the screen will print.
     Third, an RSX can only intercept BDOS calls.  Consequently, SCRPRINT can
only be called from within software that gets its keyboard input through BDOS
calls.  Unfortunately, much CP/M software uses direct BIOS calls for this
purpose.  In order to get SCRPRINT to work from inside such programs, you will
have to patch them to use a BDOS call (typically BDOS 6) instead.  In practice
this is not difficult.
ch programs, you will
have to patch them to use a BDOS call (typically BDOS 6) instead.  In practice