S E T S C B 
	View and set System Control Block Values


	(C) 1986  Gordon Wilk
		  6707 Springpark Ave
		  Los Angeles CA 90056



CPM3's System Control Block has been described in Osborne and DRI documentation
as well as in FOGHORN articles.  There remain numerous undocumented locations
in the Block.

SETSCB is a tool for experimenting with  with the SCB.  It displays all the
values in the Block, including the undocumented locations, and allows any of
them to be changed in memory.

The command SETSCB <CR>
will display the SCB in a paged display that rolls back to the top after the
last value is displayed.  At any time, any byte can be changed by pressing "C",
then, at the prompts, entering the address and new byte in hex.  Remember
that values displayed as words are actually stored backwards in memory.

SETSCB alters only the memory image.  It does not alter the SCB image in the 
CPM3.SYS file on disk.  Although it is easy enough to write the SCB block from
memory back to disk, it is not appropriate to do so.  The memory image is not
the same as the disk file.  Various locations are altered during the boot
routines.  SETSCB can serve in place of SETDEF, USER, DEVICE etc. 

Some of the undocumented locations have been labeled based on their use as I
discovered them from experimenting with SETSCB.  Some of these are described
below.  All are commented in the program listing.  Locations of undiscovered
significance remain.  Users who discover the function of these locations or
correct labeled locations are requested to modify the code and comments
accordingly.  The code is table driven and all locations can be modified by
changes to D$Tble and M$LABELS in the data section.  I would be interested to
hear of any discoveries.

The comments in the listing should be used to help interpret values.
Uncommented locations are described in the DRI documentation.

The approved method of accessing the SCB is through a BDOS call.  The SCB,
however contains its own address (at offset 3A).  This can be obtained by a
BDOS call and all subsequent references made by absolute address.  This is the
way the CPM3 Loader and Console Command Processor do it.  And it is the way
SETSCB does it.

The Console Command Processor (CCP) and the Loader can get input from five
different sources: the console, a BDOS chain command, a GET file SUB file, or
a multiple command line.  The later three are saved in an RSX format in high
memory.  The locations labeled Inp Buffer, CCP Flags 1-3, RSX Page, Command
Pointer and Buffer Pointer are used to keep track of where the next command is
coming from and how it should be processed.  The CCP Flags also record certain
features entered with the SETDEF system transient.

CCP Flag1 (F8B3)
	bit 0	SUB active
	    1	Do not remove RSX's
	    6   Do not reset User #
	    7   RSX's present
    Flag2 (F8B4)
	bit 0&1 Display program name on call
	    3   search order = COM,SUB
	    4   search order = SUB,COM
	    5   reset disks
	    6   SUB input available
	    7   chained input available 
    Flag3 (F8B5)
	bit 1   Load PROFILE.SUB if bit=0		 

A transient program can change the current drive and/or user but the CCP will
reset it to the difault value on warm boot.  The default drive and user are
stored at locations F8AE and F8AF for such restorations.  only the CCP normally 
accesses these locations.  Some system transients allow temporary setting of
the page mode; the default page mode is stored so that the CCP can reset it.

Some of the unlabeled locations may be used by SUBMIT.COM or other system
transients for similar temporary changes to SCB values.

Remember that GENCOM can add an RSX header to any com file which will set ANY
byte in the SCB.  This allows you to set a custom environment for any 
program.

The Load Profile flag is interesting.  CPM3 tries to load PROFILE.SUB on each
cold boot if bit 1 of CCP flag 3 is 0.  If the disk search order includes 
drive B:, the seach for this file will be made on that dirve as well as A:.
If there is no disk in drive B:, a BDOS error message results.  Setting the 
drive search order to *, A:, B: should be combined with setting the Load 
Profile flag to 1.  This can be done with SID or DU.  The SCB is the tenth
record in CPM3.SYS.

The code as written is specific to a CPM3 system using Televideo 9xx terminal
codes (the Osborne Executive is one such).  Changing the codes for "clear 
screen" and "cursor at x,y" will enable the program to run on any CPM3 system.


RELATED PROGRAMS:
	SEESCB	(SIG/M 236.1) displays the SCB in the same format at SID
			      without labels or explanation; it is 8k. 

	SETDEFLT (FOG CPM/047) displays and sets a few SCB values on DISK.
			       It is 20K.

REFERENCES:
	Osborne Executive Technical Manual.  Volume B, Appendix A.
	DRI. CPM Plus Programmer's Guide. Appendix A.
	DRI. CPM Plus System Guide. Page 28.
chnical Ma