'FiRe - File Restoral Utility Program'

	    FIRE    v12  by George F Reding	 08/10/87

Utility program to restore disk files to like-new condition, where the
file allocations for each file are in a sequential order rather than
being scattered all over the disk (such as after a file/program has been
modified).  Usable on any CP/M 2.2 or 3.0 system which has a Z80 CPU.
Can be used regardless of TPA memory and/or if the system directory max-
imum capacity is too large.

Version 10 clobbered the DE registerd in the XBIOS2 routine which would
make the sectran for CP/M 2.2 to not work properly.

------------------------------------------------------------------------

Created from:	RESTORE v12
	by:	Steve Dirickson
		21145 Raintree Place NW
		Poulsbo, WA  98370-9726
Other credits:
		CPM22E by Mike Griswold
		SYSLIB by Richard Conn

------------------------------------------------------------------------
			    CONFIGURATION

There's very little (if any) configuration required in order to use this
program. The following bytes may be changed with DDT, SID, or SZAP:

   103	byte	Disk change wait.
		   set non-zero for no waiting.
   104	byte	File relocation linefeed character.
		   set 0Ah for scrolling of file names,
		   0 for no scrolling (updates 1 line),
		   as each file is worked on.
   105	word	For CP/M 3.0 only.
		   value of your largest sector size.
		   (Morrow hard-disk systems is 1024)

------------------------------------------------------------------------
		     NOTES FROM THE SOURCE CODE

DPB offset and table lengths for CP/M 2.2 are different from those for
CP/M 3.3.  They are now automatically set by the program, and the BIOS
access is performed differently, eliminating the need to copy BIOS vec-
tors into the program.	Much 8080 code is changed to Z80 which conserves
memory space and increases the speed of the program.  You may use the
program even if available (TPA) memory falls short of the capability to
handle your system maximum directory entry capacity (BSH, BLM, DRM, and
AL0 and AL1 values are all factors).  Either your TPA may be too low, or
your system directory capacity (DRM) is too large (eg., 2048 or more?
maximum entries capacity).  If the situation does arise, a message is
given of the MAXIMUM ACTIVE entries that you may have to be able to con-
tinue, and you may abort if you desire not to continue.  The user should
ensure that there are LESS active directory entries by using DU, after
using SAP. >>

	 WARNING <<  To CONTINUE with MORE entries ACTIVE than
	 the figure shown WILL TRASH both files and directory.
	 Because of the memory limitation and differences among
	 among systems, no warranties are expressed or implied
	 and a user of this program shall assume any and all re-
	 sponsibility for results arising from usage of the program.


adjust maximum directory number (DRM) to a smaller/fake value for cases
where the directory has a capacity to hold 2048 (or more??) entries, or
in cases where the tpa may fall short of of capability to handle all of
the directory entries.	Adjust the directory group count (AL0 and AL1)
which varies with BLM (block size BLS) so that it matches with the smal-
ler/fake DRM value.  In order to use the program in such cases of too
many directory entries and/or of too little tpa space the TOTAL of
ACTIVE directory entries will have to be verified by the user with "DU"
or some equivilent program (after using "CLEANDIR", "SAP", "SAPP", etc).
A warning message and the maximum number of active entries that the pro-
gram can handle is given, with opportunity for the user to abort. Faking
of the DRM value is similar to that which "SAPP" (for CP/M 3.0) is capa-
ble of (an assembly time option).  The way I have implemented it here is
an improvement though and "SAPP" will subsequently be updated to imple-
ment this means of "auto-faking".
;
;
	CALL	DOCOLL		; Get group count and 1st group
				;   don't save real group count
	LD	A,(NEWGRP)	; Get our fake group count
	LD	(DIRGRP),A	; Save fake number of groups instead
	JR	FAKGRP		; Save real start/search group
;
; If enough memory, set up variables (see above about faking)
;
CKDRBF: CALL	DOCOLL		; Get group count and 1st group
	LD	(DIRGRP),A	; Save number of groups in directory
;
FAKGRP: LD	(STRTGP),HL	; Starting group in case faked
	LD	(SRCHGP),HL	; Save 1st group after directory
;

------------------------------------------------------------------------
			     CP/M 3 TEST

CP/M 3.0 tests made on a Morrow MD-11 with two 20 Mb CMI hard disk
drives, formatted capacity is 22,004k each, block size of 4k, and a
maximum capacity of 2048 directory entries.  In my test, 2,488k of
files were present on the test hard drive.

In performing the test I newly formatted one hard drive then randomly
PIP'ed some files to it eg., *.MAC, *.BIN, *.TXT, *.ASM.. etc., which
didn't make things totally scrambled, but it was a start.  Then, I ran-
domly PIP'ed some more files to another user area.  But that still was
not random enough for my test.

Then I edited a few of those files in conjustion, along with erasing,
etc.  That broke things up just enough for the test to soon begin.

I used SAPP (for CP/M 3.0) as the directory MUST BE sorted with any un-
used or erased entries set to 0E5H's.  Then used DU to list the active
directory entries to my printer to see where the allocations for each
file were now at, before use of this program.

Then came the big test with the program.

The Morrow can have up to 2048 maximum directory entries, so I was given
the warning message and shown the maximum number of active entries that
I could have (1536 for my system).

I already knew that I had MUCH less than that amount active, so I con-
tinued.  In a moment, I was given the statistics of the drive which was
displayed as follows:

	Statistics

		Active dir  entries: 94
		Tot grps  allocated: 372
		Group swaps  needed: 156
		Group reads  needed: 312
		Group writes needed: 312
		Dir rewrites needed: 61

	Press 'Y' to continue, else aborts:

And I chose to continue at the prompt, after those stats.

The program was roughly halfway through listing the files as it works on
each one takes a bit of time when it just zipped through the remaining
file names and said completed.	I then used DU to inspect and everything
is fine. CRC check of the those files that were just relocated compared
to the CRC of their originals resulted in an exact match.

Final test was made on the other hard disk drive where there were 5,824k
of files present.  The statistics were:

	Statistics

		Active directory  entries: 427
		Total  groups	allocated: 1456
		Group	 swaps	   needed: 1449
		Group	 reads	   needed: 2889
		Group	 writes    needed: 2889
		Directory rewrites needed: 424

The final test took approximately 3.5 hours for the program to complete
its task.  Most definitely the program does take quite a bit of time to
do its work, but in comparison to the act of copying files to floppy or
other drive, then erasing or reformatting the source drive, and copying
the files back to the source drive, this program is a labor saving de-
vice.

Result:  TEST SUCCESSFUL FOR CP/M 3.0.

------------------------------------------------------------------------
			     FINAL NOTES

Definitely the wear and tear that this program may save on a drive will
justify its periodic usage.

Much of the original source code is still intact, although I did change
labels to a limit of 6 characters and removed the 8080 code which was in
the program for conditional assembly.

Plus some minor changes were made, replacing some 8080 code with Z80 eg.,
usage of direct load of DE, etc), addition of my own code for compati-
bility with CP/M 3.0 utilizing routines from CPM22E, and accomodation
for low TPA systems and/or any systems with too large of a directory
entry capability.

The author of RESTORE from which this program has developed, should have
a field day figuring out where all of the mods have been made.	Much
credit should be given to him, for his work.  Thanks much to Steve Dir-
ickson.

------------------------------------------------------------------------

					- George Reding