SUPERSUB

         A replacement for the CP/M SUBMIT utility


     One of the most useful programs provided with CP/M is the 
SUBMIT utility, which allows system commands to be read from a 
disk file for automatic processing.  Its command-line 
substitution facility provides a convenient means of developing 
"prototype" command files, with actual parameter substitution 
performed when the command file is invoked.
     There are, however, some shortcomings associated with 
SUBMIT that recur frequently.  Frequently enough to inspire me 
to write my own batch processor, SUPERSUB, that completely 
replaces, and is fully compatible with, the standard SUBMIT 
utility.

PROBLEMS WITH SUBMIT

     SUBMIT will produce a "garbaged" output file whenever it 
encounters an empty line in the input file.  This is a real 
handicap when attempting to pass command lines to PIP.COM, for 
example, using XSUB (the CP/M2 utility that extends the SUBMIT 
capability to transient programs), since the only way to exit 
PIP is to enter an empty command line (you can enter a control-
"C" as the first character of the line, but this is a "real-
time" function, and cannot be done within a SUBMIT file). 
SUPERSUB generates the necessary zero-length line in the output 
file.
      Another SUBMIT drawback is the constant need to enter an 
editor and create a command file, even for the simplest of 
jobs.  This added step discourages the use of SUBMIT for very 
simple "command stacking" applications. With this in mind, I 
gave SUPERSUB the ability to interactively accept command lines 
from the console.  An additional option allows the entire job 
to be specified on the SUPERSUB command line.

COMMAND FILE NESTING

     I felt that a nesting capability would be a significant 
feature to add to SUPERSUB.  For example, it would be useful to 
create a submit file called COMPILE.SUB, to facilitate the 
program compilation process, and "clean up" any leftover files.  
COMPILE.SUB might look like this:

	BASCOM =$1	  ;COMPILE PROGRAM SPECIFIED IN CMD LINE
	L80 $1,$1/N/E	  ;LINK THE PROGRAM
	PIP B:=$1.COM	  ;MOVE THE OBJECT FILE TO THE B DRIVE
	ERA $1.REL	  ;DELETE THE .REL FILE
	ERA $1.COM	  ;  AND THE OBJECT FILE

     Now let's say I want to compile several programs at once 
(a common situation in applications programming).  Under 
SUBMIT, I would have to type in a SUBMIT invocation for each 
program:

   A>SUBMIT COMPILE LEDGER    [COMPILE.SUB executes, operator waits
				 for it to complete, then types:]
   A>SUBMIT COMPILE PAYABLES  [more waiting for COMPILE.SUB, then:]
   A>SUBMIT COMPILE RECVBLES  [and the job is finally done.]

     Using SUPERSUB, I can create a file (CMPILALL.SUB) 
containing the commands

   SUBMIT COMPILE LEDGER
   SUBMIT COMPILE PAYABLES
   SUBMIT COMPILE RECVBLES

and execute the whole thing with the single command line

   A>SSUB CMPILALL

(Note that I've abbreviated SUPERSUB to SSUB on all my disks; 
SUPERSUB as a name is a bit grandiose anyway).  I can also save 
the trouble of creating CMPILALL.SUB (especially if I want to 
do this only once) and enter the single command line

   A>SSUB /COMPILE LEDGER;SSUB COMPILE PAYABLES;SSUB COMPILE RECVBLES

or, if the individual command lines to be executed are a bit 
long, I can specify the Interactive mode by entering only a 
slash ("/") on the command line (after the SUPERSUB 
invocation).  SUPERSUB will then prompt for each command line 
with an asterisk.  To continue the previous example,

   A>SSUB /
   *COMPILE LEDGER
   *SSUB COMPILE PAYABLES
   *SSUB COMPILE RECVBLES
   *                       [empty line here terminates]

ON-LINE HELP FUNCTION

     I believe all programs of any complexity should be "self-
instructive" by providing the user a means of typing out, on 
the terminal, the major modes of operation, and any necessary 
command line syntax.  Further, the command line used to invoke 
this "help summary" should be the simplest possible form not 
otherwise used by the program.  In the case of SUPERSUB, this 
is a command line with no arguments at all:

   A>SSUB

SUBMIT.COM COMPATIBILITY

     SUPERSUB is fully compatible with CP/M's SUBMIT utility, 
including command parameter substitution and control-character 
translation:

   1) Parameters within the "prototype" file, of the form $1, 
      $2, etc., are substituted from the command line on a one-
      for-one basis.  Parameters are passed through to any 
      nested files.  Two successive dollar-sign characters 
      ("$$") may be used to introduce a single "$" into the 
      output file.

   2) An up-arrow symbol ("^") may precede an alphabetic 
      character to insert the associated control-character into 
      the output file.

DETAILED INSTRUCTIONS

     In addition to the normal SUBMIT mode of operation and 
associated command line usage, SUPERSUB provides two additional 
modes of input: Interactive and Summary.


SUMMARY MODE

Summary mode allows the entire SUBMIT job to be specified in 
the CP/M command line.  This mode is enabled by using the slash 
("/")character as the first character of the command line. The 
individual submit lines must be seperated with a semicolon. For 
example,

     A>SSUB / CRCK *.* F;CRCK B:*.* F;COMPARE CRCKFILE.CRC B:
	     ^
	     |
	      ----> (this space is optional)

will create a file of CRC's of all files on A:, then create a 
similar file on B:, then compare the two.  (CRCK, by Keith 
Petersen, and COMPARE, by Ward Christensen, are available from 
the CP/M Users Group).

INTERACTIVE MODE

You may enter the interactive entry mode by typing 
"SUPERSUB /<CR>" (ie, "SUPERSUB /" with no arguments).  
Supersub will prompt for input with an asterisk, and you may 
then enter SUBMIT lines from the keyboard.  Multiple commands 
may be entered on a line by separating them with semicolons.  
An empty line terminates the input.  Example:

A>SUPERSUB /
*CRCK *.* F
*CRCK B:*.* F
*COMPARE CRCKFILE.CRC B:
*				<empty line here>
A>CRCK *.* F			<submit file begins execution>

has the same effect as the above SUMMARY mode example.

HELP FUNCTION

Typing SUPERSUB with no arguments will print the built-in help 
file.





NOTES

1) Nested SUBMIT runs are only usable up to a maximum of 128 
   nested commands at any one time.  This is a limitation of 
   the CP/M Console Command Processor.

2) If you change the drive specification for the output file, 
   you may want to do the same thing with XSUB (Digital 
   Research's function nine extender).  Within XSUB, find the 
   submit File Control Block (search for "$$$     SUB" within 
   XSUB.COM)  and change the first FCB byte (ie, the byte 
   before the first "$") to:
		0 - to use default drive
		1 - to use drive A:
		2 - to use drive B:
   etc.

3) In SUMMARY and INTERACTIVE modes, passed parameters have no 
   meaning.  When these modes are used, the parameter flag, 
   "$", will be passed through literally to the output file.

4) Zero-length output lines may be created in SUMMARY and 
   INTERACTIVE modes by using two consecutive semicolons.  This 
   is, in effect, a blank logical line.

5) Interactive mode may be aborted by typing control-C as the 
   first character of a line.  Also, all normal CP/M editing 
   characters are available in this mode.