Reducing the Swelling of the Phone Bill with DIF and SSED
November 17, 1981
Chuck Forsberg
Computer Development Inc
Beaverton OR

        Lately  (if not sooner) it has become obvious that  there 
must  be a better and cheaper way to distribute software  updates 
to  changing  programs than to transmit all of the new  files  in 
their  totality,  even though only a few lines in each have  been 
changed.

        For  some years the Unix differential file print  program 
diff(1)  (the  (1) refers to the section of the Unix  Programmers 
Manual in which it is described) has had a -e flag which provides 
a set of ed commands suitable for transforming the first file  to 
the second.

        With  these tools,  only an update file need be transmit-
ted,  provided,  of course, that both the sender and the receiver 
had copies of the same antecdent file.

        I have written a "new" diff called dif.c which manages to 
operate in the primitive CP/M environment.   The editing commands 
output in response to the -e option refrence sequential lines  in 
the  source  files,  so they (the commands) can be executed by  a 
stream editor.   (The Unix diff(1) creates difference files  with 
non-forward-sequential commands.)

        To generate a difference file, the command is

        dif -e oldfile newfile >file.dif

        The  >file.dif redirects the standard output to the file.  
A  + may be susbtituted for > if simultaneous console  output  is 
desired.

        The receiver then invokes:

        ssed oldfile <file.dif >newfile

        Which  will result in newfile being created identical  to 
the  oroginal  newfile.    Well,  not  precisely  identical,  but 
identical  up  to  and including the  EOF  (^Z)  character.   The 
dribble  after  that  may  change,  so  CRCK  may  say  they  are 
different.  To check, compare the two files with dif.

        Unix  folks with 14 character file names and modification 
times  stored by the filesystem have little trouble  keeping  the 
files  synchronized.   (If  the antecedent files  are  different, 
there's no telling what the output file will look like!).  For us 
poor  CP/M folks (verrry) patiently awaiting something like  Unix 
to appear magically on out desktops,  I propose that the revision 
or revision date of the antecedent file be placed in the new file
adjacent  to  the new revision or date,  preferably on  the  same 
line.   This  way  the  user may easily verify that  he  has  the 
correct antecedent.

        Dif  Versions  1.10 and later place hash indices  of  the 
RETAINED  lines of the antecedent file in the difference  output. 
This  allows  ssed  1.10 or later to verify  correctness  of  the 
antecedent file.   The new .dif files are compatible with the old 
ssed, but, alas, not with Unix ed or sed.

        The  array sizes in dif.c may have to be shrunk  somewhat 
to run on a 48k system.

        For testing, give

        dif -e filea fileb |ssed filea >filec
        dif fileb filec

        (fileb and filec should be identical)

        It ought to work if you said
        dif -e filea fileb |ssed filea |dif fileb
        and it does, with version 2.0.

        Version  2.0 of dif.c adds a -u flag which will unsqueeze 
filea before comparing it to fileb.

        Thus you can say
        sq filea
        dif -eu filea.qqq fileb |ssed filea |dif fileb

        Or you can say
        dif -eu filea.qqq fileb |ssed -u filea.qqq |dif fileb
        to test dif and ssed.
(Be sure dif and ssed are exactly where you say
they are, or else pipes will be broken.)

        Restriction:   Since the BDS Standard I/O library and the 
Directed  I/O  package are somewhat  confused  about  translation 
between  CP/M's cr/lf terminated lines and **nixs' \n  terminated 
lines, dif was written to strip cr's from the input in order that 
only one cr appear on the output.   As a result, lines terminated 
by cr/lf,  lf, and lf/cr all come out the same!  This would munge 
files  where  lf/cr  has a special meaning  (MBASIC  continuation 
lines) or where embedded cr's are used (RTTY art).

        Unix is a trademark of WECO, CP/M of Digital Research.