PATCHES.DOC for CRUNCH / UNCRunch v2.3

     -----------------------------------------------------------------
     Note:  The patch  bytes for v2.3 are in different locations  than
     previous releases. The corresponding functions are the same, how-
     ever (except of course the Z3 flag, which is new to this version)
     -----------------------------------------------------------------
 
     This  document describes every possible one byte patch which  can
     be  made to CRUNCH.COM and UNCR.COM.  In each case,  the  patches
     can be made to either program for corresponding identical effects
     (except  the  "Bigger  File" patch has  no  significance  on  the
     UNCRunch program).
 
     The  patches  marked "***" are the ones which can be  changed  by
     running  the  installation program, CRINSTAL.  In each  of  those
     cases, a "NO" answer corresponds to the "zero" patch value, which
     is considered the default.
 
     -----------------------------------------------------------------
 
     Byte    Significance
     ====    ============
 
     10EH    *** "Quiet Mode Flag".  Patch to any non-zero value  to
             have  the program default to "non-verbose"  mode.  This
             has the same effect as using the /Q option on the  com-
             mand  line,  ie the program will not  display  lots  of
             churning  numbers  on the screen during  operation.  If
             this  flag is zero, it can be effectively reversed  for
             any single run of the program by using the /V option on
             the command line.
 
     10FH    ***  "Prompt Before Overwrite flag.  If patched to non-
             zero,  existing  files will be  overwritten  without  a
             prompt.
 
     110H    ***  "Turbo-DOS Flag".  If patched to non-zero, program
             will not attempt multi-sector I/O.  Otherwise the  pro-
             gram will use it if the BDOS  "Get System Version" call
             returns  a value of 3.0 or higher.  See  "TURBODOS.WRN"
             for more information.
 
     111H    "Confirm  Every  File Flag".  If set to  non-zero,  the
             program  will ask "Do it?" for EVERY file (as  it  does
             when the /C option is invoked).  While this is probably
             not a particularly useful configuration, it is included
             for the sake of completeness.
 
     112H    "Warm  Boot Flag".  If set non-zero, the  program  will
             perform  a "warm boot", as opposed to a return  to  the
             CCP, each time its is run.  This is normally not neces-
             sary,  but is included for people running  systems  who
             have  reason  to believe that the CCP will  not  remain
             resident.


     113H    ***  "Bigger File Flag".  If set non-zero, the  program
             will  NOT  ask the question "Result  file  larger  than
             original. Keep it anyway?".  The assumed answer to  the
             question will be "Yes".

     114H    "Maximum  Drive allowed, plus one".  The default  value
             here  is "FF", effectively disabling the  feature.   If
             you so desire, you may enter a value here ("A" = 2, "B"
             = 3, etc), in which case the program will intercept any
             references to higher drives (giving an "Invalid  Drive"
             error).   If you leave this feature  deactivated,  your
             operating system will gladly tell you about the invalid
             drive spec when it gets it.
 
     115H    "Maximum  User  Code  Allowed, plus  one".  Similar  to
             above.  Note however that the command line parser  will
             reject  all  references to values above  15  no  matter
             what.   In  this case, you don't even get  an  "Invalid
             User  Area" message, you will get  "Invalid  Argument".
             31 user areas are NOT currently supported.
 
     10BH    ***  "Z3  Flag". Non-zero configures program for use on
             the ZCPR3 operating system.  Non-zero values  in either
             109H or 10AH  ( Z3 "environment descriptor" ) will have
             the same effect.