CP/M MODEM PROGRAM DOCUMENTATION
	    by Mark M. Zeiger and James K. Mills
         and Gary Grossoehme for WRAM Computer Corp.
			  8/28/82

This  program  uses  the  file transfer routines  written  by  Ward 
Christensen  in his CP/M file transfer program (V2.0 as of  8/6/79) 
and  is  compatable with his program in single file transfer  mode. 
Multi-file transfers are only possible between two systems  running 
the program described below.

This program has two functions:

        1.  Communication
        2.  Program transfer

COMMUNICATIONS

The program may emulate a terminal or echo data back to sender (act
as a computer).

Terminal Mode  -  'T' Option

        The  terminal mode may be called with or without a file  name. 
        If  a  file  is  specified (it should be  a  new  file),  then 
        anything  received  by the modem may be saved  in  memory  and 
        later  written on disk.  The save feature is toggled ON/OFF by 
        Control-Y.  A colon  (:)  will be printed  at the beginning of 
	each line  when  memory save is active.  The colon will not be 
	transmitted over the modem nor will it be saved in memory.

        If  a  file  is not specified,  then memory save  can  not  be 
        activated.

        If  the memory buffer is full (the buffer is from the  top  of 
        the  program  to  the  bottom  of  BDOS),   the  contents  are 
        automatically  written  to  disk  (but the  file  is  not  yet 
        closed).  Communications  may  then continue with  the  buffer 
        reinitialized.  The  computer with which you are communicating 
        must  accept  the  X-ON and X-OFF  (Control-Q  and  Control-S) 
        conventions or data will be lost.

        When  communications are over,  use Control-E to exit from the 
        Terminal  mode and enter the Menu.  The file to which you  are 
        writing  must then be closed by using the  'WRT'  command.  If 
        this  is  not done,  all data will be lost.  I decided not  to 
        close  the file automatically since there will be  times  when 
        you leave terminal mode and then decide to re-enter.  This may 
        be done while in the Menu by using the 'RET' command.  You may 
        re-enter Terminal mode and save in the same file as many times 
        as  you wish as long as you have not closed the file with  the 
        'WRT' command.

        While  in  Terminal  mode,  Control-T will  put  you  in  File 
        Transfer mode.  This will allow you to send the contents of an 
        ASCII file over the modem. This routine does no error checking 
        and  there are no protocols specified between this program and 
        the  receiving computer other than that it should be ready  to 
        receive  data  via  the  modem.   Control-X  will  cancel  the 
        transfer.


Computer mode - 'E' Option

        This  mode  echos data received by other  computer.  Only  one 
        computer  may be in this mode at one time.  There is  no  save 
        feature  in this mode.  Useful if you wish to communicate with 
        somebody running the terminal portion of the program.

File transfer - 'S' and 'R' Options

        These  features  are  the same as in the  CP/M  Modem  program 
        written by Ward Christensen except that upon completion of the 
        transfer, control returns to the Menu unless the secondary 'T' 
        option has been selected.  In the latter case, control returns 
        to Terminal mode.  Remember that if you are operating a remote 
        computer   using   a  timesharing  program   (such   as   Ward 
        Christensen's "BYE"),  the remote should be instructed to send 
        or  receive  in  the  quiet (Q) mode as  a  secondary  option. 
        Examples  of  commands for sending and  receiving  are  listed 
        below.

Multi-file transfers

        Using  the B (batch) secondary option,  more than one file and 
        ambiguous filenames may be transferred. To send files, use the 
        primary  option  "S" and the secondary option "B" (along  with 
        any  other  secondary options and baudrate).  To  receive  the 
        files  being  sent,  use the "R" primary option  and  the  "B" 
        secondary  option.  Files may not be named since filenames are 
        sent by the sending program, but a disk drive may be specified 
        (or else the files are written to the default drive).

Backup option

        There  is  a byte at the beginning of the program (106H)  that 
        will  create a backup file if a file on the disk has the  same 
        name  as the file being received in multi-file  transfer  (see 
        MODEM.SET). If this byte is set to 0FFH, a backup file will be 
        created.  If  it is zero the file on the disk will be  deleted 
        before the new file is received. If you are running CP/M 2 and 
        a file on the disk is designated R/O or SYS,  a backup will be 
        created whether the byte at 106H is set or not.

        Be  careful - if you are running CP/M 1 and the drive on which 
        you  are receiving has an R/O file with the same name  created 
        by CP/M 2,  the R/O file can not be accessed (found,  changed, 
        erased,  etc.)  by CP/M 1.  You will therefore have two  files 
        with  the same name when you are running CP/M 2.  To fix  this 
        problem, use CP/M 1 to change the name of the file that is not 
        R/O. Then use CP/M 2 to do what you want with the R/O file.

        Examples:

        The  sender enters  SBT B:*.COM to send all the  COM  files on 
	disk B.  Also  specified  was terminal mode when done.

        The  receiver enters  RB to receive all  the  files being sent 
	on the default drive. 


        The sender enters the command  SB ASM.COM  *.HEX  B:M*.* which
	will send ASM.COM from the default drive,  all the  HEX  files 
	from the default drive,  and all the  files  starting with "M" 
	from the B drive.  

        Multifile transfers may only be done from the menu. It may not 
        be specified when the MODEM program is called.  In other words    
        A>MODEM  SAB  *.COM   will result in an INVALID  OPTION  error 
        message.


Return to Menu - 'M' option

        When asked to select an option, 'M' returns to Menu.

The MENU

        If  the Modem program is entered with no option,  the Menu  is 
        called.  The  Menu gives the choice of selecting the  standard 
        options as defined by Ward Christensen (T,  E,  R, and S). The 
        Terminal  mode has been greatly expanded as  described  above. 
        The "R" and "S" commands must be called with a filename or you 
        will be required to enter the primary command (S or R) and the 
        filename  again (but NOT the secondary options).  If you  want 
        multi-file  transfers,  then  the "R" option does not  need  a 
        filename.

  RET - You may also enter terminal mode using the 'RET' command,  but 
        no  data  will  be saved since a file may not  be  named  with 
        'RET'.  Use  the 'RET' command to RE-ENTER Terminal mode after 
        it  has  first been entered with the 'T' option.  If  this  is 
        done, you will still be able to save the communications if you 
        were doing so before you exitted the terminal mode.

  WRT - The  'WRT' command must be used after leaving  Terminal  mode. 
        This  writes  the  last buffer to disk and  closes  the  file. 
        Failure  to use the 'WRT' command results in loss of all  data 
        and a file of length zero.

  DEL - The  'DEL'  command  erases the most recent file  accessed  in 
        Terminal mode.  Useful if you decide after communications that 
        you don't want to save information just gathered.

  CPM - The 'CPM' command reboots and returns to CP/M.

  XPR - The  'XPR'  command is a toggle which causes the  menu  to  be 
        printed  or not printed.  Initially the menu is on unless  the 
        program is called with the "X" option (ie.  A>MODEM X ).

  DIR - The 'DIR' command lists the directory of a CP/M disk.  A drive 
        may  be specified (ie.  DIR B:) or the default drive  will  be 
        listed.  After  the directory is listed,  the menu will not be 
        printed whether XPR mode is on or off.  If XPR mode is on  and 
        you wish to see the menu, hit return.



LISTING OF COMMANDS AND OPTIONS

    Primary options

        S - send a CP/M file (must specify file/s)
        R - receive  a CP/M file (must name file unless B sec opt used)
        T - terminal mode (specify file if memory save wanted)
        E - terminal mode with echo
        M - return to menu
        X - used only when program is called to initially
            toggle menu off

    Secondary options

        B - multi-file mode for sending and receiving files
        T - return to terminal mode after transfer (memory save off)
        R - view what is received in file transfer
        S - view what is being sent in file transfer
        V - view what is being sent or received in file transfer
        T - Terminal mode (used with remotely controlled computer)

EXAMPLES        (fn = filename,  ft = filetype)

        Send file.
                                   S fn.ft


        Receive  file on B drive,  view what is being received, return
	to terminal mode 

                               RRT B:fn.ft

        Send all COM files, no messages on console, same  way as  last 
	transfer.

                                  SBQ *.COM

        Send two files from two different drives

                           SB A:fn1.ft1  B:fn2.ft2

        Receive files being sent by above on drive A. 

                                    RB A:

        Terminal mode,  save  communication in  file,  originate  mode 
	(in terminal must type CTRL-Y to start save, in menu must type 
	"WRT" to close file)

                                   TO fn.ft



        Any problemsor bugs, please call me:

				Or latest revisor:
        Mark M. Zeiger		James K. Mills
        198-01B 67th Ave.	824 Jordan Place
        Flushing, N.Y. 11365	Rockford, IL  61108
        (212) 454-6985		(815) 398-0579


	or 
	WRAM Computer Corp.
	(503) 244-2168