If  you have a KAYPRO II and often wish that you had more room on 
your disks or if you have said why didn't I wait and get a KP  4, 
then the upgrade to a KAYPRO 8 is for you.  This upgrade is NOT a 
massive  "rebuild/redesign"  your computer type of operation  nor 
will you have to take out a home improvement loan to change  your 
trusty old II into a 8.

The  purpose  of this modification is to upgrade the single  side 
double density disk drives (Tandon 100-1) of the Kaypro II, which 
have  a  capacity of 191K to double sided quad density drives  of 
784K each.  The number of drives to be upgraded is up to you, one 
original  +  one  800K,  two 800K,  four 800K,  two  800K  +  one 
original,  two 800K + two 390K,  or just about any combination of 
four  that you can think of.  In my system I have chosen the  two 
800K disk drives.

Now how much is this going to upset the local economy;  less than 
$500, check with your dealer on how much he will allow you for an 
old II as a trade in on a 2X or a 4 (ouch!!!) but remember he has 
to make a profit to stay in business.
 
  WHAT YOU WILL NEED (up grade to two 800K drives)

     ITEM                SOURCE              COST

     Pro-Monitor 8       Micro Cornucopia    $49.95
     DSQD disk drives    Back pages BYTE     $150 each (or less)
     IC  74S04           Electronic parts    $1.00 (or less)
                         store or mail order
     40 pin IC socket (1)     "              $1.00 (or less)
     24 pin IC socket (1)     "                   "
     20 pin IC socket (1)     "                   "
     16 pin IC socket (1)     "                   "
     14 pin IC socket (1)     "                   "
     30 gauge wire

As  you can see the upgrade can be performed for less than  $355; 
however there are certain risks (not to equipment) to your mental 
health:  most  mail order houses have a minimum order of a  least 
$10.00 (I was not able to locate the 74SO4 IC in any of the local 
(El Paso) parts stores;  next the IC sockets must be of the  very 
best quality, I used them for adapters (had some from Radio Shack 
that were not satisfactory), the pins must have at least the same 
length  and  thickness  as the legs of an IC chip  (not  easy  to 
find).

The  Micro-C articles on performing this upgrade (issues 12,  15, 
18  and  21) direct you to cut traces on the CPU  board  and  run 
jumper wires to perform the modifications,  to me the finality of 
cutting  a  trace is not pleasant.  What I have done  is  use  IC 
sockets  with  selected  pins bent out and run the  jumper  wires 
between the "bent out" pins, makes it easy to "un-modify"

  PROCEDURE
   1.    MONITOR ROM
     A   Bend out pin 21 of a 24 pin socket (will be installed in 
         U47)  connect  to  pin 2 of a 20  pin  socket  (will  be 
         installed  in  U59),  do  NOT bend out pin 2 of  24  pin 
         socket.
     B   Remove U47 and U59.
     C   Install two modified sockets in  designated slots (U47 &         
         U59).
     D   Install  new  U47  (Micro-C's  Pro-8),   reinstall   U59 
         (74LS373).

  2.     BANK DECODE
     A   Bend  out pin 1 of a 16 pin socket,  connect to pin 8 of        
         same 16 pin socket (not bent out).
     B   Remove U60.
     C   Install  U60  (74LS138) in  modified  socket,  reinstall         
         assembly in U60's slot.

  3.     FLOPPY CONTROLLER
     A   Bend out pin 13 of a 40 pin socket (will be installed in         
         U72),  bend out pins 5 and 6 of a 14 pin socket (will be        
         installed in U73. 
     B   Connect  pin  13  of 40 pin socket to pin 5  of  14  pin 
         socket (both pins bent out).
     C   Connect  two  inch  length of wire to pin 6  of  14  pin 
         socket (bent out).
     D   Remove U72 and U73.
     E   Install modified sockets in designated slots.
     F   Reinstall U72, install new 74S04 in U73.
     G   Remove "ribbon cable" going to disk drives.
     H   Connect  wire  from  U73 pin 6 to pin 32  of  J6  (cable 
         connection), by making a very small eyelet this wire can 
         be  connected  from  the top of the board and  will  not 
         interfere   with   the   cable   connection   when   its 
         reinstalled, later on.
 
There  is  a  much easier way to do all  this,  buy  a  Kit  from 
Highland Microkit; P.O. Box 21; Highland, MD 20777. Dan Carl made 
up  a kit for me which contained ALL the  sockets,   wiring,  the 
74S04  (that hard to find rascal) and he also included a new  and 
faster  Z80 PIO (U72).  Dan's sockets are the gold plate machined 
pins, top quality.

You will still need the Micro-C Pro-8 ROM though.

I  installed  the do it yourself version first and  then  put  in 
Highland's  kit,  I  was just not satisfied with the  quality  of 
parts  that I could find on the local market.  Dan's kits are the 
finest  that I have ever seen,  see Frank Fallon's review in  the 
Nov-Dec  KUGRAM or KPII4M.DOC on DL4 for a review of his 4-5  MHz 
speed up kit.
 
DISK DRIVES

There are several makes of drives on the market which will do the 
job, see the back pages of BYTE and Computer Shopper. By a little 
shopping you should be able to find some drives for $150 or less. 
What  you  are  looking for is 96 TPI (tracks  per  inch)  double 
sided.  My choice was the TEAC 55F's.  TEAC mounts their  circuit 
boards  upside-down  from Tandon so keep this in mind if you  are 
planning  to keep one of the old Tandons,  you will need  it  for 
Uniform or MF disk conversions programs or what I may do later is 
put a TEAC 55B in as the third drive. If you mix TEAC's and other 
manufactures  the  ribbon  cable will require a  twist  that  may 
resemble  a  "two and a half gainer with a  forward  twist".  The 
terminator must be installed on the drive on the end of the daisy 
chain,  makes no difference if its called A, B, C, or D, just the 
last physical drive.  My A  drive is on top and the last drive on 
the cable, it has the terminator. This way the cable makes a nice 
loop without any undue stress or weird twisting.  Should you wish 
to interchange disks with someone with a factory machine you must 
be aware of the methods used in writing data to a disk.  The head 
on the disk drive is really three heads;
               _,           READ/WRITE HEAD
             /    _________
            /----|_________|<---------------TUNNEL ERASE           
WRITE AREA <|  : |_________<--DATA is not erased
            \----|_________|<---------------TUNNEL ERASE
             \_^         

The  relative motion is for the read to be moving right to  left, 
the data section of the head will write the data in a rather wide 
track  (up  to .021 in),  then the two "tunnel erase  heads  will 
erase  the outer edges of the data track leaving only a track  of 
.012  in.  These are the figures for a factory machine (48  tpi). 
Now when you switch to a quad drive the max width of the track is 
.0105 in, which does not remove all the old data which was put on 
by  a  factory machine.  This will not cause any  trouble IF  the 
disk is used only on a quad drive BUT if this disk is put back in 
a  standard machine it will see the new data,  written by the  96 
tpi drive, and some of the old data, written by the 48 tpi drive. 
This tends to confuse the computer to no end.
   TRACK WIDTHS
                 48 TPI         
         /---------/\----------\
         |<-------.021 in----->|   
             |<--.012 in-->|
         | G |             | B |
         | U |  DATA AREA  | A |
         | A |             | N | 
         | R |E5E5E5E5E5E5E| D |
         | D |5E5E5E5E5E5E5|***|
         |***|  |G| D |B|  |***|
         |***|  |U| A |A|  |***|
         |***|  |A| T |N|  |***|
                |R| A |D| \______This area of .00075 in. will NOT 
                |D|   | |        be erased when the disk is used 
                |*|E5E|*|        in a 96 tpi drive.
                  |<A>|        A= .0065 in
                |<- B ->|      B= .0105 in
                \_______/
                 96 TPI


The way to over come this problem,  if you are going to  exchange 
disks  between  machines,  is to erase the old disk with  a  bulk 
eraser  and then reformat  it in your machine.  The old drives in 
another  machine will be able to read your narrow data track with 
no problem without seeing the "left overs". The potential problem 
is when you write on a disk formatted by 48 tpi machine and  then 
expect the disk to be read in a 48 tpi machine. The other machine 
NOT  yours.   I'll  say some more about other makes of  computers 
later on.

FLOPPY DISKS for use in a KAYPRO 8

I had a large number of single sided double density disks on hand 
when  I made the modification to my machine (3+ months  ago)  and 
simply started to use what was on hand. The predominant brand was 
BASF  however I also hand many other brands on hand,  every  disk 
that  I  have used in the new 800K system has  formatted  without 
error.  A  few required two tries but only a few ( 2 or 3 out  of 
100  ).  I've been using a BASF as my modem diary,  saving a temp 
log for the terminal session and then editing out unwanted  stuff 
after I get off the line ( MEX-SET ) no failures & the DIR tracks 
were  written to and erased 5 to 6 times a week.  The system disk 
is  a ValuLife,  same results.  Based on my experiences  I'd  say 
continue  to  use what ever disk you are comfortable with on  the 
factory drives.

WHAT DID NOT GO RIGHT

Not very much for this para: Plu*Perfect's enchantment to Perfect 
Writer,  for some reason unknown to me,  will not work.  Kaypro's 
MFDISK  is  the  only  other  item that  I've  found  not  to  be 
compatible  with this mod.  MFDISK is hardware dependent and  the 
hardware  was  changed --- therefore!  I do not have  a  copy  of 
UNIFORM  but  MicroC  says  it will not run because  it  also  is 
hardware dependent.

REFERENCES

Micro Cornucopia
issue # 12 page 24 "Kaypro column"
issue # 15 page 14 "Great Eight Kaypro"
issue # 17 page 50 "response to letter from Charles Dugan"
issue # 18 page  3 "Letter by Greg DeHoogh"
                24 "Kaypro Column"

TEAC
FD 55 maintenance manual page 108
  
AND LAST

READ  READ  READ every thing that comes from MicroC and the drive 
manufacture.  This  is an easy mod to do IF and only if  you  can 
follow directions, no short cuts permitted.   I like it.


If you are thinking about installing one of the CPU speedup kits
on the market, you should consider the kit sold by HIGHLAND
MICROKIT  P.O. BOX 21 HIGHLAND, MD 20777. I installed of these
kits in late June and its worked perfect since then. The nice
thing about these kits is that NO soldering or cutting of PWB
traces is required on an older KP II. This kit is the same as the
speedup modification described in MICRO C #12 (Jun 83). The only
program that has not worked at 4 Mz is PLU*PERFECT's fast copy,
at 56 sec to copy a disk who cares! My KP II will run for about
one hr at 5 Mz but then it craps out but at 4 Mz it'll go all
t 56 sec to copy a disk who cares! My KP II will run for about
one hr at 5 Mz but then it craps out but at 4 Mz it'l