UNSPOOL.ASM                     81-11-21
          for CP/M 2.0 and up.

          AUTHOR:                 Gary P. Novosielski
                                  Rutherford, NJ

                                  (201) 935-4087

          INTRODUCTION:

                  UNSPOOL (Ver 3.0) is a program to send a standard
          CP/M file such as a .PRN or .ASM file to the system's list
          or punch device, while still allowing other system operations
          to take place.  The file is transferred during periods when
          console is waiting for input.

          SYNTAX:

                  UNSPOOL [d:]filename.ext [dev]
                          or
                  UNSPOOL dummy OFF

                  [square brackets denote optional parameters]

                  Where   d:              is an optional drive spec
                                          such as A: or B:.  If not
                                          entered, the current default
                                          drive is assumed.

                          filename.ext    is the name of the CP.M file
                                          to be printed/punched

                          dev             is the symbolic name of the
                                          output device to be used.
                                          Valid devices are LST and
                                          PUN.  Note that the colon
                                          (:) usually present in these
                                          names is NOT entered.  If not
                                          specified, the LST: device is
                                          assumed.
                          OFF             If OFF is specified
                                          instead of a device name, the
                                          operator will be offered the
                                          option of cancelling UNSPOOL
                                          if it is already running.
                          dummy           Because the word OFF is the
                                          second parameter, a filespec
                                          is still needed.  A dummy name
                                          of "." will suffice as a place
                                          holder.

          Examples:

                  UNSPOOL TEST.PRN

                          will send the file TEST.PRN from the current
          default drive to the current LST: device.

                  UNSPOOL A:TEST.PRN LST

                          is exactly equivalent to the above, assuming
          drive A is the default drive.  Note that the device name has no
          trailing colon.

                  UNSPOOL B:ZINGER.HEX PUN

                          will send the file ZINGER.HEX from the B drive
          to the current PUN: device regardless of which drive is
          currently the default.  Note that the device is "PUN"
          not "PUN:".

                  UNSPOOL . OFF
                  UNSPOOL *.* OFF
                  UNSPOOL OFF OFF

                          all cause an operator prompt: "Do you want to
          cancel UNSPOOL?"  A single "Y" or "N" (Yes or No) is accepted
          from the console as a response.  Any other character is assumed
          to mean "No".

                  UNSPOOL OFF

                          causes the file "OFF.   " to be sent to the
          list device.

          OPERATION:

                  Upon loading, the program checks to see that the
          the BIOS vector table pointed to by the word at location
          0001H is valid, i.e. is a table of JMP instructions containing
          at least 16 entries.  If an error is detected, the program
          will display an error message on the console and attempt to
          warm-boot CP/M.

                  If found, the BIOS vector table is copied into the
          program segment which will remain active during unspooling
          so that subsequent application programs running concurrently
          with UNSPOOL will still have access to the BIOS.

                  This table is modified to trap attempts to warm boot
          the system or perform direct console input.

                  The address of the old BIOS vector table, the BDOS
          entry address, and the CCP return address (from the top of the
          stack on entry) are saved in memory.

                  The "dev" parameter from the command line is checked.
          If not valid, an error message is typed and control returns
          to the CCP.

                  If the "dev" parameter is the literal OFF, the program
          executes a BDOS funcion 0 (System Reset) and terminates.

                  The file named in the command line is opened for
          input.  If not present, the command is echoed to the console
          followed by a "?" and control returns to CCP.

                  If the drive is not explicit, the current default
          drive number is recorded internally in case the default drive
          is changed while UNSPOOL is active.

                  The current user number and IOBYTE values are checked
          and stored internally so that if the user number is changed,
          UNSPOOL will still be able to read the input file.  If the
          device is changed (using STAT LST:=TTY: for example) unspool
          will continue to use the physical device in effect at the
          time the program was initiated.  Any application programs
          will, however, use the new values of the user number and the
          new physical device assignments.

                  If no errors were detected, the active program segment
          which monitors all calls to BDOS is relocated into high memory
          just below the CCP.  This reduces the available user program
          area by 3 K:  4 pages for the UNSPOOL supervisor segment,
          and 8 pages for the CCP which is commonly overwritten by user
          program buffers.  The BOOT and BDOS jumps in low memory are
          modified to protect the CCP and UNSPOOL supervisor segment.

                  Control is then returned to the console.  Normal
          CP/M operation will then be possible. Characters will be
          sent from the input file to the output device whenever the
          console is idle.

                  Whenever an application program or the CCP requests
          console input using BDOS functions 1 or 10, or a direct call
          into the jump table at C(BOOT + 1) + 6, the supervisor
          segment intercepts these requests and checks to see if the
          console is idle.  If it is, characters are transferred from
          the input file to the output device until the console becomes
          ready, i.e. a key is actually pressed.  At that time the
          BDOS function or BIOS call is executed normally, and control
          returns to the application program.

                  If a jump to BOOT is attempted, this is also
          intercepted by the UNSPOOL supervisor segment.  The message
          "Unspooling in progress" is displayed on the console, and
          no actual boot takes place.  Control is returned to the
          protected copy of the CCP instead.  Before returning, a disk
          reset is performed and the default DMA address is reset to
          0080H to simulate a true warm-boot as closely as possible.

                  If warmboot is attempted using BDOS function 0, the
          program will prompt the operator with the option to cancel.
          If the response is "Y", warmboot is performed using BDOS
          function 0 as requested.    Otherwise the request is handled
          as with normal warmboot, above.

                  When the input file is completely transferred, or
          a 1AH end-of-file character is detected, the supervisor
          becomes inactive, and passes on all previously intercepted
          requests immediately, without checking console status.  When
          the next warm-boot request is detected, the supervisor removes
          itself from memory by executing a true warm-boot, and informs
          the operator with the message "UNSPOOL completed.".

          NOTES:

                  While UNSPOOL makes every effort to restore the values
          of the DMA address, USER number, IOBYTE, and default disk drive
          before returning control to the program, a hardware reset may
          leave these values in an undetermined state if unspooling was
          actually taking place at the time.

                  When function 10, Read Console Buffer is used, UNSPOOL
          will transfer characters only until the first key is pressed.
          At that time, no characters will be transferred until the
          input line is completed by pressing a carriage return.

                  UNSPOOL requires that the List Status function in
          the BIOS was properly implemented at system installation time.
          UNSPOOL will not send characters to the LST: device unless it
          recieves a ready condition from the List Status routine.  If
          the PUN: device is used, no status check is provided for by
          CP/M, so a not-ready condition on the punch may cause the
          system to hang up if PUN was specified on the command line.
          See the CP/M Alteration Guide for a discussion of the BIOS
          List Status routine.

                  Although the console is polled frequently during the
          unspooling of the file, some of the diskette operations may
          take a second or two to complete, for example when a new extent
          is opened.  Since the console is not polled during this period,
          high speed typing may cause one or more characters to be lost.
          This effect will vary depending upon the program being run,
          the types of input reqests (character or line) it uses, and
          the relative locations on disk of the spool file and any
          files in use by the program.  As a result, heads-down typing
          is not reccommended while UNSPOOL is running.  Some experience
          with UNSPOOL will teach the user when caution is required.

          INSTALLATION:

                  The source file is written for assembly with the
          MAC assembler.  The .HEX file produced is LOADed to a .COM
          file and executed just as any normal program.  Relocation is
          done at execution time as described above.

                  If the assembly option EXPAND is set to TRUE, tab
          characters in the input file will be expanded to spaces with
          assumed tab stops at every eighth print position.  This option
          should be set to FALSE if the printer driver or the printer
          itself can properly handle the tab character.  If the option
          PHYSBS is set to TRUE, a backspace character will cause the
          tab expansion algorithm to recognize backspace characters
          and decrement the column count when a backspace is encountered
          in the input file.  This option should be set to FALSE if
          backspace characters are ignored by the printer.  All other
          control codes except carriage return are assumed to be non-
          printing, and are ignored by the algorithm.

                  If tab expansion is included, the version number
          in the signon message will be followed by "/T".

                                  Gary Novosielski




õÍOCñwg