TITLE:  SETMX

BY   :  IRV HOFF

DATE :  10 OCT 82

TOPIC:  PRESETTING EPSON MX-80 PRINTER OPTIONS


     This simple program allows EPSON MX-80 users to preset a number
of options.  The printer can then be satisfactorily used with the TYPE
command (via CTL-P) or other normal listing programs.


     These options include:  10 or 16.5 chars. per inch
                              6 or 8 vertical lines per inch
                              single strike or double strike
                              emphasized print
                              reset to normal default values


     To use, turn on the Epson printer and then call up SETMX.COM.  It
will display various options on its menu.  Several selections can be
made at the same time or a number reentered if mis-typed.  If RET is
immediately typed it defaults to a standard configuration.


            Default is:  10 characters per inch
                          6 vertical lines per inch
                            single strike print


     After the appropriate answers have been typed, hit RET to leave
the program (or CTL-C).  The printer now has the options you selected.
The TYPE command (via CTL-P) may then be used or any other LIST routine
desired.

     Obviously some options were not included.  The SETMX.ASM file can
be edited and then reassembled.  (ASM.COM works fine for this purpose.)
Even if the operator is not too familiar with using source code, there
are enough examples already included to make the job of adding some ad-
ditional feature fairly simple.


                                 Irv Hoff
                                 Los Altos Hill, CA  94022