El Paso TX   -   10/26/83

Now, how did Digital Research ever get the idea of using "the number of
days since 01/01/78" for their MP/M and CP/M plus system date format?
Surely, they must have had a reason and the prime consideration, I assume,
was space. Space is what is at a prime in disk directories, so they
decided to make the date as small as possible.

It just so happens you can get 179 years into 16 bits. That plus the fact
that microprocessors, CP/M and 8- and 16-bit stuff will probably not be
with us anymore in 20-30 years, assures that the format doesn't get
obsolete.

Unfortunately, the format brings with it the agony of conversions.
Enter myself. Now, you have someone to thank (or curse) for taking the
conversion work off your fingers. I have written two routines which I
call DATE and UNDATE. They can be assembled and linked into any program
using RMAC/LINK or M80/L80 and provide conversion functions for you.
I decided to keep it simple and not provide Microsoft FORTRAN etc.
compatibility, but rather gear it towards the assembly language
programmer. Since most existing clock routines already are written to
provide ASCII output, and since the UNDATE function will probably
quite often be used to convert keyboard input data, no provision was
made to convert a binary or packed BCD date.

This is a description of the two routines, their actions and parameters:

DATE
====

The DATE routine is to be called at it's entry point, @DCVRT, with
the date to be converted in HL in Digital Research format. The DATE
routine expects a global symbol, @DCFLD, to be the pointer to the first
byte of an ASCII date field. On exit, that date field will be filled
with the date corresponding to the input value in ASCII. A typical
field, which is usually declared in the main module would look like this:

@DCFLD:	DB	'  /  /  $'

The field can be totally empty, or hold a previous date. No error checking
is done and only bytes 0,1,3,4,6, and 7 are written. If delimiters are
needed, they should be in place like above. If the field is terminated
by a dollar sign, it can be printed under CP/M with:
LXI D,@DCFLD ! MVI C,9 ! CALL 5


UNDATE
======

The UNDATE routine is to be called at it's entry point, @UDCVT. The
contents of the registers are irrelevant. A date field structure
exactly as described for the DATE routine above should be present
and declared with global symbol @DCFLD as it's first byte. UNDATE
will convert the ASCII date, which must be stored in MM/DD/YY format,
to Digital Research format and return the resulting 16-bit value in HL.
NOTE: The date is checked for the following format errors:

	Year 77 or earlier
	Month over 20
	Day over 40
	Non-numeric ASCII character

and the routine will abort with the CARRY flag set and all registers
holding undefined values. If none of the above format errors are
detected, CARRY will be RESET and HL will hold the result. Despite
the rudimentary error checking, the CALLING PROGRAM is responsible
for a valid date field!


NOTES:
======

	Both routines can probably be improved a bit, especially the DATE
	routine is a bit slow.

	YOU, the writer of the main module using these routines, are
	responsible for properly initializing the date field.

	I chose to use simple names, such as DATE and UNDATE to identify
	the source modules. In order to avoid possible symbol conflicts,
	I decided to be a lot more cryptic with the name selection for
	the entry points and the parameter.
	Again, the entry point for DATE is @DCVRT, and the entry point
	for UNDATE is @UDCVT, while the ASCII date field is @DCFLD.

	You might, if you intend to do a lot of programming, put these
	routines into some form of library, possible append them to
	the SYSLIB library (If Rick Conn doesn't mind...)

Have fun converting dates!


P.S.	These routines work. I write a small program which started at day
	1 and counted up, displaying the date first in DRI format, then in
	ASCII, and then converted the ASCII back to DRI format, and in all
	cases it translated correctly up to 12/31/99. Hardest part was
	convincing the DATE routine that there is no MM/00/YY...
riter