HOW TO USE KERMIT FOR TRANSFERRING FILES
                     BETWEEN MICROCOMPUTERS

                     Norman Weatherby, Ph.D.
             Center for Population and Family Health
                       Columbia University

                          July 24, 1984


     KERMIT (like the frog, a registered trademark of Henson
Associates, Inc., used by permission) is ideal for transferring
ASCII and binary files between computers of all sizes.  It is a
protocol for transferring sequential files between computers of
all sizes over ordinary asynchronous telecommunication lines
using packets, checksums, and retransmission to promote data
integrity.  KERMIT is non-proprietary, thoroughly documented,
well tested, and in wide use.  The protocol and the original
implementations were developed at Columbia University and have
been shared with many other institutions, some of which have made
significant contributions of their own.  KERMIT programs have
been written for a wide variety of microcomputers, minicomputers,
and mainframes.

     Which ones?  At the end of this document is an extensive
listing that was downloaded (using KERMIT) from a DEC mainframe
at Columbia University.  In addition, you will find the address
to write for futher documentation, and some information for those
who would like to participate in the growth and acceptance of
KERMIT as one of the major file-transfer protocols.

     I wrote this guide so that people who have very little
computer experience could use KERMIT to transfer files between
CP/M micros or between CP/M and IBM PC-type systems.  It simply
tells you how to work with KERMIT, without going into its
features.

     This guide was submitted to the KERMIT distributors, and
they like it, but they have NOT stamped their approval on it.  It
is not a substitute for the real documentation.  And, as the real
documentation states:

     No warranty of the software nor of the accuracy of the
     documentation surrounding it is expressed or implied,
     and neither the authors nor Columbia University
     acknowledge any liability resulting from program or
     documentation errors.

KERMIT is copyrighted, and it is not "public domain".  Simply, it
is a free program that is not to be sold as a product.  As the
distributors state, you are free to redistribute KERMIT on your
own terms, and are encouraged to do so, with the following
stipulations: KERMIT should not be sold for profit; credit should
be given where it is due; and new material should be sent back to
Columbia University at the address given in the summary so that
they can maintain a definitive and comprehensive set of KERMIT
implementations for further distribution.

     Where do you get KERMIT?  As stated below, Columbia
University distributes versions of the program only on nine track
magnetic tape.  You can get the program from friends, bulletin
board systems, and various areas on services such as CompuServe.
Look around for the latest version for your micro, and be aware
that the program is constantly improving.


                           NOW, KERMIT

     Without going into the details of KERMIT, this guide shows
you how to use the program to transfer files between micro-
computers that have KERMIT. The sections include

     1. Connecting the computers, either directly or through
        modems
     2. Setting the baud rates
     3. Loading KERMIT into memory
     4. Setting KERMIT's options
     5. Communicating between computers
     6. Sending and receiving files
     7. Checking what was sent
     8. Figuring out why (If) KERMIT does not work
     9. Summary


CONNECTING THE COMPUTERS

     If you are going to transfer the file over the telephone
system through modems, hook up a

                        full duplex modem

to each computer's serial communications port (com1: on IBM PC
type machines, or on CP/M machines, rdr:/pun: or auxin:/auxout:).
You may need to get a cable that switches pins 2 and 3 to a modem
if the port is a printer port (lst: or printer).  If you are
working with acoustically coupled modems, set one modem to answer
mode and the other modem to originate mode.

     If you do not have two modems, and the computers are in the
same room, you can

     a. Directly connect the serial modem ports of the two
        machines.  The cable that is needed is one in which pins
        2 and 3 are switched when connecting two modem ports.

                               OR

     b: Directly connect the serial modem port of one computer to
        the serial (not parallel) printer port of the other
        computer.  This may cause a problem, since you have to
        make sure that KERMIT talks to the printer port of the
        other machine.  However, it is the only way to get, for
        example, the Osborne Executive to KERMIT a file to an IBM
        PC-type machine.

One benefit of using a direct connection between the computers is
that you can use high baud rates, such as 4800 baud, to transfer
the files.  Since you are not using modems or telephones, ignore
the parts of this guide that concern use of the modems and
dialing of the telephone.


SETTING THE BAUD RATE

     The baud rate controlls the speed of the file transfer.
The baud rate can be set from within KERMIT some CP/M machines,
such as the Osborne 1 and the Intertec Superbrain, and on MSDOS
(PCDOS) computers.  One really nice feature of KERMIT is that you
do not have to cope with that poorly-documented mode command on
the IBM PC-type micros.

     If you do not know whether KERMIT handles the baud rate,
skip forward in these instructions and load KERMIT into memory.
At the KERMIT prompt, give the command

                            set baud<cr>

where  <cr>  means to "hit" the return key.  KERMIT will tell you
if the baud rate setting command has not been implemented.

     If you cannot set the baud rate from within KERMIT, such as
on H89 systems, then you can get back to your operating system by
typing, at the prompt,

                            exit<cr>

Then use the computer's software to set its baud rate, usually to
300 or 1200 baud when modems are used.  The baud rate of a CP/M
machine is set through the SETUP or CONFIGUR utilities supplied
with the system.


LOADING KERMIT INTO MEMORY

     Loading KERMIT into the memory of an Apple II or Atari
computer is more difficult than loading it into CP/M or MSDOS
(PCDOS) systems.  Thus, readers should refer to other
documentation and help files for assistance with these systems.

     IF YOU HAVE A HARD DISK: Micros with hard disks, such as the
IBM PC-XT, often refer to all or part of the hard disk as disk
C  .  If you have a hard disk, copy your KERMIT program and
associated utility, help, and documentation files from the KERMIT
floppy to the hard disk (if someone else has not copied them over
already).  Then work off of the hard disk.  That is, if you do
not see the prompt for the hard disk on your screen, type the
command

                             c:<cr>

Then, to load KERMIT into memory, type the name of your kermit
program, which is usually KERMIT.  For example, at your operating
system's prompt, type

                           kermit<cr>

Then skip to the section below about setting KERMIT's options.

     IF YOU HAVE TWO FLOPPY DRIVES: Put the KERMIT diskette in
drive A of each computer.  Note that on a CP/M machine such as a
Kaypro, H89, or Osborne 1, it is wise to have the operating
system on the KERMIT disk (through the use of the SYSGEN utility)
and to type the command

               cntl C (without a carriage return)

where  cntl  is the control key and  C  can be upper or lower
case, to make the computer realize that a new disk has been put
in drive A.  This "warm boot" command is not necessary on micros
that use CP/M 3.0, MSDOS, or PCDOS operating systems.

     Put a formatted disk in drive B of the system which is to
receive the file.  On the sending system, put the disk with the
file that you want to transfer in drive B.  Go to drive B, and
then get into KERMIT on each machine by typing  a: and the name
of the program, which is usually KERMIT.  For example, type

                          a:kermit<cr>

Newer versions of KERMIT allow you to change the "logged disk
drive," but it is wise to follow the above advice so that you are
sure of the disk that you are sending from or receiving to.


SETTING KERMIT'S OPTIONS

     To see the options that are available in your version of
KERMIT, type at the prompt the command

                           status<cr>

Note that the toggle command   set ibm  , which can be set  on
or  off , is NOT FOR IBM PC MICROS--it is a command for Columbia
University's IBM mainframes.

     SETTING THE PARITY: A computer "byte" is composed of  eight
bits--where each bit is a zero or one.  All (english) printable
letters, numbers, punctuation marks, and spaces between words can
be represented by seven of the eight bits.  The eighth bit is
reserved for checking to make sure that the other seven bits are
correct.  However, some microcomputer software packages (such as
WordStar) use the eighth bit for special characters that allow
features such as right justification.  In any event, if both
computers allow the following command, issue it to allow the
transmission of all eight bits:

                       set parity none<cr>

     SETTING THE FILE-MODE: Microcomputers store files in two
ways:

     ASCII files--codes such as letters, numbers, punctuation
     marks, and spaces, or as

     binary files--codes that are recognizable to a computer but
     not to you, such as the way programs are stored.

If you are transferring an ASCII file, issue the command

                       set file ascii<cr>

If your are transferring a binary file, use

                       set file binary<cr>


     SETTING THE BAUD RATE: If you can set the baud rate from
within KERMIT, make the baud rates of both computers equal by
typing at the prompt the command

                        set baud xxxx<cr>

where  xxxx  is the baud rate you want.  For example, you may
type

                        set baud 1200<cr>

If these commands do not work, try

                          set baud ? <cr>

and select the correct baud rate from a menu that is given on the
screen.  If you get messages that  set baud  command is not
implemented,  you will have to get out of KERMIT and set it from
your operating system, as discussed above.


COMMUNICATING BETWEEN COMPUTERS

     Then type at the prompt the command

                           connect<cr>

on each computer.  This will put you into the connect mode, which
allows one computer operator to send messages to the other
operator through the modems or the direct connection.  Note that
KERMIT replies with an "escape" message that tells you how to get
back to the command state of the program.  WRITE DOWN THIS
MESSAGE, AS YOU WILL NEED IT LATER.

     In fact, it is a good idea to test the command now.  The way
you get back to the KERMIT prompt varies by the type of system.
In general, you will have to issue the command but add a  C
(upper or lower case) to it to get back.   For example, on many
CP/M machines that have the backslash character \ , the "escape"
command is control \  , but you type

                ctrl\c  (without typing a return)

where  ctrl  is the control key.  After some experimentation, you
will see the KERMIT prompt, and then you can type the command
connect<cr> again.

     For those who are using modems: From the originate modem,
dial the answering modem.  If you have an auto-dial modem, you
can issue the dial command to it.  For example, with a touch tone
telephones and a Hayes SmartModem, the only command that is
necessary is for the originate modem:

                           ATDTxxxxxxx

where xxxxxxx is the telephone number to dial.

     When the connection is made, each  you each will be able to
send and receive messages that serve to test the connection.

     If you want to see what you are typing, get back to the
     KERMIT prompt by typing the "escape" command that you
     wrote down and tested above.  Then issue the command

                         set loc on<cr>

     to have a local echo, but you must remember to

                         set loc off<cr>

     before attempting to transfer a file.

If the connection is not made, so that it is not possible to
send AND receive messages, then you should check

     the baud rates of the computers,
     the modems, and the wiring to the modems,
     or the wiring between the directly-connected
     computers,

and make sure that the computer is sending or receiving data
to the correct port on the computer.  It is also helpful, as a
last resort, to check whether or not the telephone died because
you forgot to pay the bill (don't laugh...it once happened to
us!)


SENDING AND RECEIVING FILES

     When each computer operator is satisfied that a connection
has been made, then both operators return to the KERMIT prompt,
as explained above.

     The operator that wants to receive a file types

                           receive<cr>

The file name will be sent from the other machine.

     The operator that wants to send a file types the command

                  send [drive:]filename.ext<cr>

For example, to send the file on disk B that is named
myfile.txt , the operator would type

                      send b:myfile.txt<cr>

It is usually not necessary to type in the drive specification,
since you should be using disk B as the "logged disk drive", but
it is always safe to do so.  If the receiving operator hits the
return before the sending operator hits the return, it may be
necessary for the receiving operator to hit another return before
the file will be sent.

     KERMIT will wait for a few seconds, and then the operators
will see on their screens that packets of information are being
sent and received.  KERMIT first sends the file name, and it is a
good sign to the receiving operator when the file name appears on
his or her screen.  The number of packets will increment on both
machines until the transfer is complete, and then each computer
will return to the KERMIT prompt.  At that time, the receiving
operator can check the file or another file can be sent.


CHECKING WHAT WAS SENT

     Once a connection has been established with KERMIT, it is
not broken if one or both of the operators return to the
operating system of their computers to check something such as
the length or name of a file.  Thus, when a transfer is complete,
the receiving operator can get out of KERMIT by typing

                            exit<cr>

at the KERMIT prompt.  The file that was received can be
examined, usually by issuing the command

                  type [drive:]filename.ext<cr>

The file will scroll by on the screen, and you will see that it
has been transferred without error!

     The receiving operator can then return to KERMIT by
reloading KERMIT into memory.  As stated above, go to your B disk
and type A:KERMIT or whatever the file name of your program is.
If you need to, reset the baud rate, and you will then be able to
transfer another file or get into connect mode and send messages.


FIGURING OUT WHY (IF) KERMIT DOES NOT WORK

     KERMIT has never, in my two years of experience with the
program, made a mistake in sending and receiving files between
CP/M computers or between CP/M computers and mainframes.  It
accurately transfers files even when the telephone line is
unusable for voice transmissions because of static and noise.

     Operators do, however, tend to make mistakes.  One such
problem is impatience.  Please let KERMIT wait for a few seconds
before you touch a carriage return on the receiving computer to
"make it work."  If KERMIT seems to be dead after about thirty
seconds of waiting, then something is wrong.  If you were able to
send messages back and forth in connect mode, or if KERMIT fails
after the first four or five packets, then probably the problem
is that one of the operators set the local echo switch on but
forgot to set it off.  It is also possible that the file that you
wanted to send does not exist, because the sending operator
missppelled its name in the send command.

     Occasionally, KERMIT will fail for reasons beyond its
control.  The transfer will fail if one of the computers involved
goes down.  For example, mainframe computers or their communi-
cation ports often go down (that's why we are now using micros
for most of our work, right?).  A feature such as call waiting or
intercom messages on a telephone line will stop the transmission
if they happen during a transfer.  I view these failures as
advantages in that it shows that KERMIT is smart enough to quit
when there is a major problem.

     We have also encountered a problem with the way BASICA and
dBASE II on IBM PC-type computers mark the end of a file and save
it.  The solution is to load the file into a text editor or word
processor and then resave it before sending it.  For example,
load a file into WordStar and then save it.  An unreliable
alternative is to copy the file using the /A parameter.  The
problem is not fully understood; it centers around the PCDOS and
MSDOS software's use of buffered output when writing disk files.

     Apple II versions of KERMIT work well with DOS 3.3, but
Apple IIs do not work so well.  They are slow, there are
differences between the II, the II+ and the IIe, and there is no
standard way that people set up their Apple's for communications.
If you plan to use Apple KERMIT, please check with other Apple
KERMIT users before ordering your communications card and modem.
Currently, the best cards may be the Apple Communications card,
the Hayes Micromodem II, or the Super Serial Card.  Actually, the
best way may be to install a Z80 card in the Apple II and run the
Apple CP/M version of KERMIT.


SUMMARY

     KERMIT is a very powerful program, with extensive error
checking, and thus it is ideal for transferring files between
computers.  The full documentation will show you many commands
and options for the program.  You may want to order the
documentation, but the simple procedures in this guide may be
adequate for your needs.

Extensive documentation is available for this program from

          KERMIT Distribution
          Columbia University Center for Computing Activities
          7th Floor, Watson Laboratory
          612 West 115th Street
          New York, NY  10025

There are three publications: the User's Guide, the Protocol
Manual, and the Source Listing for your system.  Each costs
$5.00, and you should make out your check to Columbia University
Center for Computing Activities.  Make sure and tell them what
microcomputer and operating system you are using.  Those who are
interested in mainframe implementations (which currently cost
$100 for the complete distribution) should write for ordering
information.  Note that the KERMIT distributors can provide the
programs only on 9-track magnetic tape in a varity of formats.
They do not provide the program on floppies.

     When necessary, there are specific help files that are
distributed with KERMIT to help with its use.  For example, there
is a help file with the Kaypro II version because of the non-
standard way a Kaypro handles tab stops on its screen.

     There are also articles and announcements about KERMIT.  For
example, see BUSS #88 and June-July, 1984 issues of BYTE.

     Please do not call the Kermit Distribution Center for
assistance with KERMIT for your micro.  After all, it is a free
program, and national support, sales, service, debugging,
revisions, everything else is being handled by only two or three
part-time people.  You can write, however, for the publications.

     Finally, KERMIT is changing and improving constantly --
versions are added for new systems, old versions are improved,
and documentation is rewritten.  You are encouraged to make your
own contributions to "KERMIT culture" and to make them available
not only to your friends, but also to send them back to Columbia
at the address given above, on 9-track magnetic tape or IBM PC
eight sector floppy disk.  For example, we need KERMIT for
TurboDos version 1.2, and we need to know how to implement the
"break" key on many CP/M machines (like the H89) through
software.

     The most current version of KERMIT for CP/M machines is
3.9a, which fixes a bug in version 3.9 that may garble the
transmission of apmersands.  A brand-new MSDOS version is soon to
be released.  Watch for new releases and updates.  Meanwhile,
below is a recent but even now out-of-date listing of available
versions.


      CURRENT KERMIT VERSIONS as of 4:42pm  Wednesday, 6 June 1984

Listed in reverse chronological order of installation at Columbia.  "Code" is
the prefix under which the files are stored in the KERMIT distribution area.

CURRENT KERMIT VERSIONS as of 9:46pm  Wednesday, 18 July 1984

Listed in reverse chronological order of installation at Columbia.  "Code" is
the prefix under which the files are stored in the KERMIT distribution area.
New entries are added at the top.

Code  Machine/OS        Language     Ver #   dd/mm/yy  Author or Contact

TSO   IBM 370/MVS/TSO   IBM Asm       1.0    18/07/84  SYSRONR@UCHIVM1.BITNET
APP   Apple II/DOS      CROSS         2.1    18/07/84  G.BUSH@COLUMBIA-20
20    DEC-20/TOPS-20    MACRO-20    4.1(236) 18/07/84  CC.FDC@COLUMBIA-20
K11   PDP11/RSX11M,M+   MACRO-11      2.18   17/07/84  ATSBDN@UOFT01.BITNET
K11   PDP11/RSTS        MACRO-11      2.18   17/07/84  ATSBDN@UOFT01.BITNET
K11   PDP11/RT-11       MACRO-11      2.18   17/07/84  ATSBDN@UOFT01.BITNET
APO   Apollo/Aegis      FORTRAN       1.0    13/07/84  John Lee, RCA Labs
HPM   HP1000/RTE        FORTRAN       1.0    13/07/84  John Lee, RCA Labs
SIR   Sirius-1          MASM          1.20   12/06/84  Barry Devlin, Dublin
ST    HP3000/SoftwareTools/Ratfor     1n     18/02/84  kpd%HP-LABS@CSNET-Relay
ST    Univac/SoftwareTools/Ratfor     1n     11/06/84  kpd%HP-LABS@CSNET-Relay
CPM   Apple II/CPM-80   ASM           3.9A    6/06/84  CC.FDC@COLUMBIA-20
CPM   DECmate II/CPM80  ASM           3.9A    6/06/84  CC.FDC@COLUMBIA-20
CPM   Generic CPM80 2.2 ASM           3.9A    6/06/84  CC.FDC@COLUMBIA-20
CPM   Generic CPM80 3.0 ASM           3.9A    6/06/84  CERRITOS@USC-ECL
CPM   H/Z-19/CPM-80     ASM           3.9A    6/06/84  CC.FDC@COLUMBIA-20
CPM   H/Z-100/CPM-80    ASM           3.9A    6/06/84  CC.FDC@COLUMBIA-20
CPM   Kaypro II/CPM-80  ASM           3.9A    6/06/84  CC.FDC@COLUMBIA-20
CPM   Osborne 1/CPM-80  ASM           3.9A    6/06/84  CC.FDC@COLUMBIA-20
CPM   Superbrain/CPM80  ASM           3.9A    6/06/84  CC.FDC@COLUMBIA-20
CPM   TRS80-II/CPM80    ASM           3.9A    6/06/84  CERRITOS@USC-ECL
CPM   Vector Graphx/CPM ASM           3.9A    6/06/84  CC.FDC@COLUMBIA-20
CPM   VT180/CPM-80      ASM           3.9A    6/06/84  CC.FDC@COLUMBIA-20
CPM   TelconZorba/CPM80 ASM           3.9A    6/06/84  G.BUSH@COLUMBIA-20
PRO   DEC Pro-350       Bliss         1.0     1/06/84  G.BUSH@COLUMBIA-20
VMS   VAX/VMS           Bliss         3.0.051 1/06/84  G.BUSH@COLUMBIA-20
K10   DEC-10/TOPS-10    MACRO/Bliss   3(124)  1/06/84  G.BUSH@COLUMBIA-20
TRS   TRS-80 I and III  M80           3.5    30/05/84  stan@RICE
170   Cyber 170/NOS     Fortran77,asm 2.0    25/05/84  knutson@UT-NGP
UCI   IBM PC/p-System   UCSD Pascal   0.1    23/05/84  KMM@CORNELLA.BITNET
RBLC  Rainbow/MS-DOS    CI/86         2.14   23/05/84  LCAMPBELL@DEC-MARLBORO
800   ABC-800/ABCDOS    BASIC-II      2.2     8/05/84  Per_Lindberg_QZ@QZCOM
86/APC NEC APC/CPM-86   ASM86         2.7     7/05/84  CONTEXT@WASHINGTON
86/RB Rainbow/CPM-86    ASM86         2.7     4/05/84  CC.FDC@COLUMBIA-20
MAC80 8080 Cross Asmblr MACRO-10  10E(120)   30/04/84  CERRITOS@USC-ECL  
CPM   Morrow Decision I ASM           3.9    26/04/84  CC.FDC@COLUMBIA-20
CPM   Nokia MikroMikko  ASM           3.9    26/04/84  CC.FDC@COLUMBIA-20
CPM   Ohio Sci/CPM-80   ASM           3.9    26/04/84  CC.FDC@COLUMBIA-20
MP    PDP-11/MUMPS-11   MUMPS(1982)          11/04/84  KMM@CORNELLA.BITNET
UCT   Terak/p-System    UCSD Pascal          11/04/84  KMM@CORNELLA.BITNET
KPROTO"KERMIT Protocol Manual"        5th Ed  2/04/84  CC.FDC@COLUMBIA-20
KUSER "KERMIT User Guide" English     5th Ed  5/03/84  CC.FDC@COLUMBIA-20
MU    Honeywell/MULTICS PL/I                 28/02/84  P.Amaranth, Oakland U 
TA2   Tandy 2000/MS DOS MASM          1.20   16/02/84  smp@UTEXAS-11
PRI   Prime/PRIMOS      PL/P                 10/02/84  L.Spira, The SOURCE
AOS   Data General/AOS  Ratfor                2/02/84  John Lee, G.E.      
HP1   HP-150/MS-DOS     MASM          1.3     2/02/84  Frank Heartney, H-P
CMS   IBM 370/VM/CMS    IBM Asm               1/02/84  CC.DAPHNE@COLUMBIA-20
MDS   Intel DevSys/ISIS PL/M                 27/01/84  Chris@COLUMBIA-20
RT    PDP11/RT11        OMSI Pascal          24/01/84  Bruce Pinn, U Toronto
HP9   HP-98xx/p-System  HP Pascal            20/01/84  Gallaher@RUTGERS
VF    VAX/VMS           Pascal/Fortran       18/01/84  Bruce Pinn, U Toronto
ATA   Atari/DOS         Action!               9/01/84  G.TANG@SU-SCORE
MTS   IBM 370/MTS       Asm, Pascal           6/01/84  "Gavin Eadie"b@UMich-MTS
UN    Univac 1100/Exec  Exec Assembler       22/12/83  STEVENS@MACCWISC.MAILNET
PC    IBM PC etc/PC-DOS MASM          1.20   30/11/83  CC.Daphne@COLUMBIA-20
PC    H/Z-100           MASM          1.20   30/11/83  CC.Daphne@COLUMBIA-20
VIC   Victor 9000/CPM86 ASM86         1.1    25/11/83  Barry Devlin, Dublin
SEE   Seequa/MS DOS     MASM          1.18   17/11/83  Glenn Everhart, RCA
VIC   Victor 9000/MSDOS MASM          1.18   10/11/83  Bryan Peterson, ORNL
UX    (various)         Unix                 17/10/83  CC.FDC@COLUMBIA-20
VIC   Victor 9000/MSDOS MASM          1.1     3/06/83  Barry Devlin, Dublin
VX    VAX/VMS           VAX-11 C             24/04/83  Todd Little, DEC