TYPE DU-V78.D*

::::::::::
DU-V78.DQC
::::::::::
DUU.DOC
by Ward Christensen (revised 09/27/81)
With additional notes by Ron Fowler

HOW TO USE DU ver 7.5 DISK UTILITY
        (Extended and called DUU on CP/MUG v.55)

DUU, Disk Utility-Universal, is an enhanced version of
previous DU programs, on CP/MUG volumes 40 and 46.

The primary change is the additions by Ron Fowler, to make DU
work with virtually any 1.4 or 2.2 system, single or double
density.  

A further change by Ward C. updates the "F" command.  Under
1.4, the "F" command would find a file, then position to it. 
This was possible because open/search returned a number in
(A) which was the "directory entry number".  However, since
CP/M 2.2 doesn't return the actual "directory entry number" on
an open or search, as 1.4 did (because 2.2 can have more
directory entries).  Thus, DUU now does the directory search
itself, positioning to the file.   See the "F" description
below.


        INDEX

1.0     INSTALLATION:
2.0     USE:
 2.1    COMMANDS, BY FUNCTION
  2.2   ALPHABETIC COMMAND SUMMARY
3.0     NOTES
4.0     INTERPRETATING DIRECTORY DATA 
  4.1   SINGLE DENSITY
  4.2   DOUBLE DENSITY


1.0     INSTALLATION:
===
        The 7.0 and later versions of DU are designed to 
be installed with a minimum of trouble.  In fact, in al-
most all cases, no changes to the source file should be
necessary to get DU up and running. This is because DU
uses the disk paramter block of CP/M to determine the
characteristics of the disk environment.  (see the dis-
claimer for certain non-standard versions of CP/M 1.4).
        The only parameter that should need to be changed
will be the clock speed flag at 103H.  Leave this byte
zero if you have a 2 mhz clock.  Patch it non-zero for
4 mhz.  This is only needed for the "Z" (sleep) command.
An alternative is just to use larger numbers when running
4mHZ or 5MHz.


2.0     USE:
===
An initial command string may optionally be placed as an
operand of the original DU command, i.e.:

     A>DU G0;D;G2;=OK<D><A><1A>;D

For example, if you want to only MAP the disk, then exit:

        A>DU M;X

Once DU is running, it expects single-letter commands much 
like SID or DDT.  For ease of use, multiple commands may be 
placed on one line, separated by ";".  In addition, a given 
command or string of commands may be repeated, either indef-
initely (until ^C is pressed), or a given number of times.

To avoid an accidental ^C from dropping out of DU, only an 
explicit "X" command will exit DU.


2.1     COMMANDS, BY FUNCTION
===

Help:
        ?       request help

Positioning:

        Gnn     by allocation group
        Snn     by sector
        Tnn     by track
        +nn     going ahead nn sectors
        -nn     going back nn sectors

I/O:
        R       Reads sector
        W       Writes sector
        <       Puts current sector "away" into a buffer
        >       Recalls previously saved sector

Displaying:
        G       Shows current group, track, sector
        M       Maps the disk - where are the files
        Mxx     Map starting at group xx
        D       Dump the sector (hex + ascii)
        A       Dump sector in ASCII
        H       Dump sector in hex
        Vnn     Views (like CP/M TYPE) nn sectors
        #       Shows disk parameters

Changing:
        CHnn,val Change data in hex
        CAnn,val Change data in ascii ( with <xx> escape to hex)
        Unn     Change user to nn

Searching:
        Fname   Find a file in the directory
        F       Find next occurrence (extent) of same name
        =aaaa   Scan for aaaa (in ASCII) from current
                sector on

Misc:
        Znn     Sleep (nn tenths of a second) such as to allow
                viewing data before it scrolls off
        Lx      Log in disk x
        P       Turn on/off printer output toggle
        Q       Before any command does it "quietly"
        X       Exit to CP/M
        /nn     Repeat previous command nn times
                (indefinitely if nn omitted)


2.2     ALPHABETIC COMMAND SUMMARY
===

        #       Prints the disk parameters

        +       advance 1 sector (if below track 2,
                this advances to next numerical, if
                2 or >, advances based on CP/M's normal
                sector scrambling algorithm, i.e. so +
                will get the next logical sector of the file

        -       backs up 1 logical sector

                Note + and - may take an amount:
                for example, +15 steps in 15 sectors.

        /       Repeats entire command.  Defaults
        /nn     to "forever".  nn may be 2 to 65535

        <       Saves current sector in a save buffer

        =string Ascii search, starting at current
                sector. <xx> hex may be imbedded,
                or used alone:  To find "IN 0FEH":
                =<db><fe>
                Ignores bit 7 unless <xx> is used.

                Since ";" is a command delimiter, you
                have to use <3b> to search for a ";".
                
                Also, since "<" is a hex-escape char,
                use << to meane a single "<".

        >       Gets saved buffer.  < and > may be used
                to move a sector to another place.


        ?       Gives command summary

        A       Dump sector, ASCII only

        CHaddr,val,val,val... change hex in sector
        CAaddr,char string... change ASCII in sector
                NOTE that <xx> may be hex imbedded
                in the Ascii:  ca0,OK<d><a><1a>

                ----> Use W to write changes to disk.
                Note that the C command echoes
                the overlaid data for verification.

        CHaddr-addr,byte
 or     CAaddr-addr,byte        repeats a change

        D       Dump sector, hex + ASCII

        Fname   print directory for file "name",
                then positions to it's directory 
                sector. 

        F       Find next occurrence of name in dir.

        Gnn     Position to group nn and read.

        G       Shows current position

        H       Dump sector, hex only

        L       Re-logs in the current disk. You may pull
                out a disk, put in a new, and "L" just
                to log it in. (See "LOGGING IN DISK" in NOTES 
                below)

        Lx      Logs in disk 'x', such as: LB

        M       Dumps a map of the group allocations
                for files.
        Mn      Shows which file is allocated to
                group "n".

        N       Resets CP/M via the BDOS.  This may
                make it possible under some implementations
                of CP/M to change the disk format (e.g., density,
                sides, etc)

        P       Toggle printer switch on/off

        Q       Quiet: Preceeding any command, suppresses console 
                output

        R       Reads the sector currently positioned to
                into memory.  Note R (Read) is implicit in
                the G, +, and - commands, but N-O-T in the
                S and T commands (I did it because I was
                tired of disk reading after T command before
                I had a chance to issue the S command)


        Snn     Position to sector nn, and read

        Tnn     Seek to track nn (no read)

        Ux      Logs user 'x' for next F command.  Gives
                '?' error if not CP/M version 2.x.
                (Note "F" no longer needs this - finds
                 ALL files - erased, any user, etc)

        V       Views the current sector.
                (assumes ASCII data)
        Vnn     Views nn sectors

        W       Write back the current sector (N-O-T-E may
                not be used after an F command, as CP/M was
                used to find the file in the directory

        X       Exit back to CP/M (Must press return).  Ctl-c
                was too easy to hit over modem lines, so I
                decided on 2-byte (X, CR) to exit.


        Z       Sleep - causes the program to pause, such
                as to look at a dump.  Z is 1 sec.  Znn
                is nn tenths of a second on a 2 MHz 8080.



3.0     ====== NOTES ======
===
* MULTIPLE COMMANDS: May be separated by ";"

Example: the following commands will erase the
        b disk directory to all E5's:

        lb              log in b drive
        g0              position to dir.
        ch0-7f,e5       fill with e5
        <               save the sector
        >;w;+;/16       restore, write, next,
                        repeat 16

----This could be shortened to:

        lb;g0;ch0-7f,e5;<
        >;w;+;/16

* DUMP COMMANDS: All dump commands (D, A, H) may be optionally 
followed by a starting and ending address:
        D0,7F   is the same as just D
        D3,5
        A20,3F

* LOGGING IN DISK: In the original DU, I logged in the disk the 
way DU now does.  Then, I found that when you had a blown 
directory, you DIDN'T want to log the new disk in.  Thus I 
changed DU to just change which disk was selected.  Then along 
came double density, with its attendant "select density" 
functions, and Ron apparently put this back in.  So, it now 
sometimes works for double density, but makes DU very 
"intolerant" of disks with un-readable directories.  A 
solution is to log in a disk which is OK, and is of the same 
density as the blown disk, then put in the blown disk WITHOUT 
logging it in.
        However, you are now opening yourself up to possible 
problems because of the buffering of physical sectors in the 
BIOS.  The best technique, (but not guaranteed), would be to 
seek to the unused inner tracks of the first disk, do the 
read, THEN change disks.  That way if it writes anything, you 
won't have destroyed anything.  ...assuming the disk is not 
completely full.  Another technique, assuming the second disk 
does not contain a CP/M system, would be to seek to track 1, 
then do the read there, then change disks to the blown one.


4.0     INTERPRETATING DIRECTORY DATA 
===
4.1     SINGLE DENSITY
===
The following explains the format of a CP/M directory entry
as shown by DU, using either the "F" (find file) command,
or just doing "D" (dump) of the directory sectors, which
are located in groups 0 and 1 on a single density disk.
                ----------------
Sample result of "FSID.COM" command:

40  00534944 20202020  20434F4D 0000003A  *.SID     COM...:*
50  33343536 3738393A  00000000 00000000  *3456789:........*

First line -

40  00534944 20202020  20434F4D 0000003A  *.SID     COM...:*
||  |||                      |  ||    ||    |         |
||  ||^----hex file name-----^  ||    ||    ^file name^
||  ||                          ||    ||     in ASCII
||  ||                   extent-^^    ||
||  ||                                ||
||  ||           file size in sectors-^^
||  ||
||  ^^-00 = file active  Other values (e.g 03) = User #
||     E5 = file erased
^^-displacement of line in directory sector

Second line -

50  33343536 3738393A  00000000 00000000  *3456789:........*
    |                                  |   |
    |                                  |   ^- allocation groups
    ^-----allocation group numbers-----^        just happened
                                                to be printable


4.2     DOUBLE DENSITY
===

The following is a sample of FSID.COM running on double
density system:

:FSID.COM
00  00534944 20202020  20434F4D 0000003A  *.SID     COM...:*
10  38003900 3A003B00  00000000 00000000  *8.9.:.;.........*
G=0000:00, T=2, S=1, PS=0

The primary difference is that the groups now occupy
2 bytes, i.e. "38 00" "39 00" ...  This follows the INTEL
and CP/M convention of putting 16 bit values high-byte-first.
Thus it means group 0038, 0039, etc.

Note that in double density, each group stood for 2K, not 1K,
so there were half as many groups for the same file.

Be VERY careful when patching a directory under double density.
I once made the mistake of putting, for example:

        ch10,38,39,3a,3b...

When I went to read this file, it tried to access group 3938,
with resultant angry exclamations from the disk stepper as it
attempted to go south to Peoria for the data.

                                        09/30/81 Ward C.

[UTILITY] 00:37>PACE:  MVI     A,' '
        JMP     TYPE