Enclosed are 4 file locator programs:

  LSS
  RFF
  LIKE
  FL

LSS is similar to the commonly seen LS, the bare-bones file name lister with 
output suitable for piping to other programs.  This version has some 
interesting file time/date selection criteria which makes it useful for 
program development/project management.

A similar thing can be said for RFF.  It's Find File with some useful file 
time/date selection criteria

LIKE is similar LSS with one major difference: it finds files with a string  
anywhere in a file name.  For example:

   LIKE TEMP

will find files:
   TEMP????.???
   ?TEMP???.???
   ??TEMP??.???
   ???TEMP?.???
   ????TEMP.???

This feature is useful for those of us who can't quite remember WHAT name we 
gave to a file:  Was it PROGDOC.TXT ... or was it DOCMYPRO.DOC ... or perhaps 
V23DOC.W51?  If you remember a PART of the file name, you could go quite 
bonkers doing all of the  wild cards with the DIR command without LIKE.

FL stands for "Find Like".  It combines RFF and LIKE, allowing a LIKE search 
on an entire disk.

They are all spawned from the same basic 'C' code and share some common 
features and controls.

File inclusion controls:
   Normally, these programs are used to search for files - not directories, so 
   directories are not normally included.  With RFF and FL one MAY want to 
   find directories, so they have an 'INCLUDE DIRECTORIES' control.  There is 
   also an 'EXTENDED LISTING' control, which will include ALL files.  When 
   extended listing is specified, ALL information about the files is 
   displayed: attributes, size, creation date and creation time.  The extended 
   listing also provides a tally of file size as well as space remaining.

   /I - include directories (RFF and FL)
   /X - extended listing

   In addition, LIKE and FL automatically assume that the search extension is: 
   .???.  You MAY, however, provide an EXTENSION to LIKE and FL.  If the 
   extension is provided, these programs look for an exact match to the 
   extension (the wildcarding is only in the file name portion).  '?'s ARE 
   permissible in the extension, though.

   In the event that you're not sure WHERE in the file name the match string 
   may be (name OR extension) an 'INCLUDE EXTENSION' control is provided in 
   LIKE and FL.  When enabled, the string search is performed over the 11 byte 
   file name/extension (where it normally is performed only on the file 
   name).

   /E - included extension

   Thus, the command:

      LIKE TMP /E

   will locate:

   TMP?????.???
   ?TMP????.???
   ??TMP???.???
   ???TMP??.???
   ????TMP?.???
   ?????TMP.???
   ??????TM.P??
   ???????T.MP?
   ????????.TMP

File selection controls:
   Once it is determined which files are included, one may choose which will 
   be selected.  Selection is based on file attributes and date/time.

   /A - select files with ARCHIVE   bit set
   /H - select files with HIDDEN    bit set
   /R - select files with READ-ONLY bit set
   /S - select files with SYSTEM    bit set
   /D - select files with DIRECTORY bit set
   /V - select files with VOLUME    bit set

   If none of these controls are selected, ALL files are displayed.  If more 
   than one is selected, the logical OR of the controls is used.

Time/date controls:

   Once inclusion and selection are complete, these programs provide for 
   further file selection based on creation date.  These features are useful 
   for project/program development, backup performance, etc.  With these 
   controls, the user may specify group of files by TIME (any date), DATE (all 
   hours), TIME and DATE, and a special non-standard or 'windowed' selection 
   (files created between specified hours between specified dates).  When 
   dates and times are specified, the standard format of mm-dd-yy and hh:mm:ss 
   should be used.  Shortcuts can be made: mm or mm-dd can be specified, as 
   can hh or hh:mm.  mm-dd-yy defaults to 01-01-80 and hh:mm:ss defaults to 
   00:00:00.  Thus 06-27 implies 06-27-80.

   To aid program file management, a shortcut for today's date and the current 
   time are provided:  when 'T' is specified instead of mm-dd-yy, today's date 
   is used, and when 'N' is used in place of hh:mm:ss, the current time is 
   used.
   
   Selection is done by bracketing between a lower date/time (default of 
   00:00:00 on 1-1-80) and an upper date/time (defaulting to some time, 
   23:59:59 on some date in the next century - I forget which at the moment).

   /LD<date>|T - specifies lower date
   /UD<date>|T - specifies upper date
   /LT<time>|N - specifies lower time
   /UT<time>|N - specifies upper time
   /N - specifies a non-standard (windowed) selection (see below)

   Normally files are selected between the lower date:time and upper 
   date:time.  This is acceptable for most applications.  However, it may be 
   necessary to locate files created on specified hours on specified days (for 
   example, all files greated between 9 AM and 11:30 AM on 6-23-94 thru             
   7-1-94).  The /N switch allows this type of selection.

HELP!

   As always, a bit of on-line help is available using the:

   /? control!


                                     SUMMARY
                CONTROL
   PROGRAM   |   /I  /E  /X  /A  /D  /H  /V  /R  /S  /LD /UD /LT /UT  
   ----------+------------------------------------------------------
   LSS       |            X   X   X   X   X   X   X   X   X   X   X
   LIKE      |        X   X   X   X   X   X   X   X   X   X   X   X
   RFF       |    X       X   X   X   X   X   X   X   X   X   X   X
   FL        |    X   X   X   X   X   X   X   X   X   X   X   X   X