;************************************************************************
;*									*
;*			RAM MEMORY ASSIGNMENT				*
;*									*
;************************************************************************

;			OSCOR-1
;			9 OCTOBER 1980
;			R. DAVID POGGE

			ORG 8000H

;	** 16 BIT GENERAL PURPOSE REGISTERS **

A1:	NOP
	NOP
A2:	NOP
	NOP
A3:	NOP
	NOP
A4:	NOP
	NOP




;	** REGISTER STACK **

PCREG:	NOP	; USER'S PROGRAM COUNTER
	NOP
SPREG:	NOP	; USER'S STACK POINTER
	NOP
RET1:	NOP	; USER'S FIRST RETURN ADDRESS
	NOP
RET2:	NOP	; USER'S SECOND RETURN ADDRESS
	NOP
RET3:	NOP	; USER'S THIRD RETURN ADDRESS
	NOP
RET4:	NOP	; USER'S FOURTH RETURN ADDRESS
	NOP
HLPAIR:	NOP	; USER'S L REGISTER
	NOP	; USER'S H REGISTER
DEPAIR:	NOP	; USER'S E REGISTER
	NOP	; USER'S D REGISTER
BCPAIR:	NOP	; USER'S C REGISTER
	NOP	; USER'S B REGISTER
PSWREG:	NOP	; USER'S FLAGS
	NOP	; USER'S ACCUMULATOR




;	** OUTPUT PORT IMAGES **

OP0IMG:	NOP	; BIT 0 - TTY
		; BIT 1 - PLOTTER PEN LIFT
		; BITS 2-7 (UNUSED)
OP1IMG:	NOP	; PLOTTER DRIVE X
OP2IMG:	NOP	; PLOTTER DRIVE Y
OP3IMG:	NOP	; BITS 0-7 (UNUSED)




;	** INPUT PORT IMAGES **

IP0IMG:	NOP	; BIT 0 - TTY
		; BIT 1 - PUSHBUTTON BAR
		; BITS 2-7 (UNUSED)
IP1IMG:	NOP	; BITS 0-7 (UNUSED)
IP2IMG:	NOP	; BITS 0-7 (UNUSED)
IP3IMG:	NOP	; BITS 0-7 (UNUSED)




;	** MATH PACKAGE VARIABLES **

R:	NOP	; POLAR DISTANCE "R"
	NOP
THETA:	NOP	; POLAR ANGLE "THETA"
	NOP
QUAD:	NOP	; VECTOR QUADRANT
		; 00 = 1ST QUADRANT
		; 40 = 2ND QUADRANT
		; C0 = 3RD QUADRANT
		; 80 = 4TH QUADRANT
RECTX:	NOP	; RECTANGULAR COORDINATE "X"
	NOP
RECTY:	NOP	; RECTANGULAR COORDINATE "Y"
	NOP
SIGN:	NOP	; NUMBER OF NEGATIVE SIGNS (ODD NUMBER = NEGATIVE)
TEMP1:	NOP	; TEMPORARY STORAGE 1
	NOP
TEMP2:	NOP	; TEMPORARY STORAGE 2
	NOP




;	** I/O LIBRARY VARIABLES **

BUFF:	NOP	; TTY I/O BUFFER
	DS 80



;	** PLOTTER PACKAGE VARIABLES **

NORMX:	NOP	; NORMALIZED X COORDINATE (0 TO 255)
XMAX:	NOP	; MAXIMUM X COORDINATE (-32,767 TO +32,767)
	NOP
XMIN:	NOP	; MINIMUM X COORDINATE (-32,767 TO +32,767)
	NOP
NORMY:	NOP	; NORMALIZED Y COORDINATE (0 TO 255)
YMAX:	NOP	; MAXIMUM Y COMPONENT (-32,767 TO +32,767)
	NOP
YMIN:	NOP	; MINIMUM Y COMPONENT (-32,767 TO +32,767)
	NOP




;	** STACK **

BSTACK:	NOP	; BOTTOM OF THE STACK
	ORG 80FFH
TSTACK:	NOP	; TOP OF THE STACK

	END
SUBBAK*BTABLESLST0Þ)