Turbo Pascal Communications Library

   1.0 Introduction

         Turbo   Pascal   provides   a   fairly   uniform  programming
       environment for a variety of microcomputers  running  CP/M  and
       MS-DOS.   It is fast, and the differences between versions can,
       in general, be worked around.  Certain  areas  are  a  problem,
       however - communications, and system dependent function.

         This  set  of  routines  is  intended to address the first of
       these  problems, difficulty in  communicating with  the outside
       world.  Each   operating  system  is  different in  the way  it
       handles communications, and different hardware  implementations
       create problems when trying to use communications ports.  There
       is a need for a standard set of routines that provide the basic
       communications  needs  for  most programs.  If the routines are
       rewritten  for  various  micros,   generalized   communications
       programs can be written.  Any programming tricks can be used to
       perform  the  actual  functions, but a uniform calling sequence
       can be used.

        1.1 Sample Programs

             A   sample   communications   library   is  available  as
           'CLIB180.INC'.  This library includes an  example  of  each
           function and procedure listed below.  Some of the functions
           are  very  simple, as the VT180 has PSETUP available to set
           parity and/or baudrates.  CLIB180 also supports the RAINBOW
           (100A,100B) running CP/M version 2 or higher.

             A  sample  of  the  use  of the communications library is
           given  in  the   program   'COMDEMO.PAS'.    This   program
           implements a 'connect' mode and allows simple file transfer
           by  capturing data from the communications port and storing
           it in a file, or sending a file to a remote system.

             COMDEMO.PAS  was written as a 'test-case' for CLIB180.INC
           - it's also useful as the "first piece"  to  "customize"  a
           "text-capture"   utility  for  a  new  micro-system,  which
           doesn't have yet a way to "talk protocol".   TURBO-Pascal's
           inherent  compilation-speed  and  (relatively  high  -  see
           above) portability will help in  getting  the  "first"  and
           "crucial"  step accomplished : Enable TEXT-capture "to" and
           "from" another system.  The typical "next step" seen is  to
           establish  an  (preferably)  Error-Correcting protocol like
           KERMIT.

  2.0 General Library Description

       2.1 Variables, Constants, and Typed Variables

            All  library  functions,  procedures, and global variables
          begin with 'c_'.  This should minimize collisions with other
          program variables.  Any variables that begin with 'c__'  are
          for  the  use  of  the  library  itself, and should NEVER be
          modified by the main program.

            All  variables  required  by  the  library  only should be
          included here.  This would include such variables as  IOBYTE
          definitions for CP/M, etc.

            The   following   are  predefined  types,  constants,  and
          variables in the library:

          Types

            c__string10 = string[10];
            c__string5 = string[5];
            c__port_names = an  array  of string10's that will list the
                            possible ports for the computer.
            c__baud_names = an  array  of string10's that will list the
                            possible baud rates for the computer.
            c__parity_names = an  array  of string10's that will list the
                            possible parity settings for the computer.

          Constants

            c_lib_version = computer type, revision of library, and date.
            c_port_str = all possible  strings that  the available  ports
                         are  equivalent  to.   The  first  two  MUST  be
                         'NOT SET'  and  'DEFAULT'.  After  all ports are
                         defined, the last  element in the  array MUST be
                         null ('').
            c_baud_str = all possible strings that the available baud rates
                         are equivalent to.  The first two MUST be
                         'NOT SET' and 'DEFAULT'.  After all baud rates are
                         defined, the last element in the array MUST be
                         null ('').
            c_parity_str = all possible strings that the available  parity
                           settings are equivalent to.  The first two MUST
                           be  'NOT SET' and  'DEFAULT'.  After  all ports
                           are defined, the last element in the array MUST
                           be null ('').

          Variables

            c_kbd_char : The returned keyboard character.
            c_comm_char : The returned comm port character.
            c_current_port : The number of the current port. the string
                             equivalent of the port number is :
                             c_port_str(c_current_value).
            c_current_baud : The number  of the current baud rate.  The
                             string equivalent of the baud rate is :
                             c_baud_str(c_current_baud).
            c_current_parity : The number of the current parity setting.
                               The string equivalent if the parity is :
                               c_parity_str(c_current_parity).

       2.2 Functions

           2.2.1 C_INIT

                Initialize  a  communications port.  Initialization is
              system dependent,  but  should  include  such  items  as
              setting  hardware specific values, obtaining the initial
              value of the IOBYTE in CP/M systems, etc.  It should  be
              run  at  the  beginning  of  each  program that uses the
              communications library.

                The way the port, baud rate, and parity variables are
              set up, executing c_init(1,1,1) will set up a default
              communications port.  This is a good way to begin any
              program so the at least some communication port is
              initialized.  For some systems, having no port set up
              will cause system hangups.

              c_init(port, baud, parity : integer) : boolean;

              Inputs : port   -  Number  of  the  port.  This  can  be
                                 obtained  by  scanning  the  list  of
                                 ports  contained    in   the    array
                                 c_port_str.
                       parity -  desired   parity   setting  on  port.
                                 The number  of the  available  parity
                                 values  for the  particular computer.
                                 These can be obtained by scanning the
                                 list of parity  settings available in
                                 the array c_parity_str.

                       speed -   desired  port  speed.  The number of
                                 the available baud rate settings can
                                 be obtained by scanning  the list of
                                 available  baud rate settings in the
                                 array c_baud_str.

              Output : Function  returns TRUE if the desired setup  is
                       valid, and FALSE if the setup is invalid.

              Variables affected : c_current_port, c_current_baud, and
                                   c_current_parity are set to their new
                                   values if the operation was successfull.

              Other effects: depends on implementation.

           2.2.2 C_SET_PORT

              Select the desired communications port.

              c_set_port(port : integer) : boolean;

              Input : port - Number of the port.  System dependent.  A
                             list of the available ports  can be found
                             in the array c_port_str.
              Output : Function returns TRUE if new port was selected,
              and FALSE if the new port was an invalid port.

              Variables affected : sets c_current_port, c_current_baud,
                                   and c_current_parity to those for the
                                   new port.  Other variables are system
                                   dependent.

              Other  effects  :  current port should not be changed if
              function returns FALSE.

           2.2.3 C_SET_PARITY

              Set the parity on the current port, if possible.

              c_set_parity(parity : integer) : boolean;

              Input : port - Number of the port.  System dependent.  A
                             list of the available ports  can be found
                             in the array c_port_str.

                       parity -  desired   parity   setting  on  port.
                                 The number  of the  available  parity
                                 values  for the  particular computer.
                                 These can be obtained by scanning the
                                 list of parity  settings available in
                                 the array c_parity_str.

              Output: Function  returns TRUE if the parity is reset to
                      the new value, and FALSE if the parity could not
                      be set.

              Variables affected: c_current_parity is changed to the new
                                  parity if the operation was successfull.
                                  Other variables are system dependent.

              Other effects: should leave same parity if result is FALSE.


           2.2.4 C_SET_BAUD

              Set the baud rate on the specified port, if possible.

              c_set_baud(speed : integer) : boolean;

              Inputs : speed -   desired  port  speed.  The number of
                                 the available baud rate settings can
                                 be obtained by scanning  the list of
                                 available  baud rate settings in the
                                 array c_baud_str.

              Output: Function returns TRUE if the baud rate can be
                      set and FALSE if the baud rate cannot be set.

              Variables Affected: c_current_baud is set to the number
                                  of the new baud rate if the operation
                                  successfull.  Other variables are
                                  system dependent.

              Other  effects  : Should leave the baud rate the same if
                                error.

           2.2.5 C_GET_KBD_CHAR

              Check the keyboard for an available character.

              c_get_kbd_char : boolean;

              Input : none.

              Output : Function   returns   TRUE  if  a  character  is
                       available  and  false  if   no   character   is
                       available.

              Variables affected : c_kbd_char   is   changed   to  new
                                   character if function returns true.

              Other effects : function  must always leave the computer
                              in  the same state as it was found, i.e.
                              for  CP/M the IOBYTE must be returned so
                              that  CON: is set to main console.

           2.2.6 C_GET_COMM_CHAR

              Check  the currently selected communications port for an
              available character.

              c_get_comm_char : boolean;

              Input : none.

              Output : Function   returns   TRUE  if  a  character  is
                       available  and  false  if   no   character   is
                       available.

              Variables affected : c_comm_char   is   changed  to  new
                                   character if function returns true.

              Other effects : Function  must always leave the computer
                              in  the same state as it was found, i.e.
                              for  CP/M the IOBYTE must be returned so
                              that  CON: is set to main console.

       2.3 Procedures

           2.3.1 C_PUT_SCR_CHAR

              Send a character to the console screen.

              c_put_scr_char(character : char);

              Input : character to be output.

              Output : none.

              Variables affected : none.

              Other effects : Function  must always leave the computer
                              in  the same state as it was found, i.e.
                              for  CP/M the IOBYTE must be returned so
                              that  CON: is set to main console.

          2.3.2 C_PUT_COMM_CHAR

             Send a character to the selected communications port.

             c_put_comm_char(character : char);
 
             Input : character to be output.

             Output : none.

             Variables affected : none.

             Other effects : Function  must  always leave the computer
                             in  the same state as it was found,  i.e.
                             for   CP/M the IOBYTE must be returned so
                             that  CON: is set to main console.

    3.0 VT180 Communications Library

         This  is  an implementation of a standard set of routines for
           communications, for the DEC  VT180  (Robin).   The  VT180's
           main features are as follows:

         Microprocessor:         Z80A
         Memory:                 64k bytes
         Operating system:       CP/M-80
         Communications ports:   4 serial

           CRT:  hard-wired terminal port to VT100 terminal

           LPT:  printer port

           UC1:  user defined console port

           PTR:  high speed reader port
           PTP:  high speed punch port

       The  VT180  uses  the Digital Research standard IOBYTE for port
       switching.

       3.1 The IOBYTE


              A few words about the IOBYTE are in order.  The ports on
           a  CP/M-80  computer are described by PHYSICAL names (CRT:,
           LPT:, etc.).  When the IOBYTE is used, they are  mapped  to
           LOGICAL  ports,  and  the IOBYTE allows reassignment of the
           physical ports to different logical ports.  For example, on
           the VT180, the pysical ports UC1: and CRT: can be  assigned
           to  be  the  logical  port  CON:.  When booted normally all
           console I/O goes to CRT:,  the  internal  VT100  port.   If
           desired,  the  UC1:  port can be assigned to be CON: and an
           external device can act as the system console.  I use  this
           method  with  a  modem so I can dial up my computer and use
           the remote terminal as the console.

             The IOBYTE is the device that allows this reassignment of
           physical  ports.   The IOBYTE is a byte in memory, normally
           located  at  address  0003.   This   may   vary   in   some
           implementation  of  CP/M.   There  are  four  fields to the
           IOBYTE:

             LIST       PUNCH      READER       CONSOLE

           bits 6,7   bits 4,5    bits 2,3      bits 0,1

           The values below are the possible IOBYTE assignments:

             Console field (bits 0,1)

               00 console is assigned to the console printer device (TTY:)
               01 console is assigned to the CRT device (CRT:)
               10 batch mode, RDR: is console input device, LST: device is 
                  console output.
               11 console is assigned to the user defined console (UC1:)

             READER field (bits 2,3)

               00 reader is teletype device (TTY:)
               01 reader is the high speed reader device (PTR:)
               10 reader is user defined reader #1 (UR1:)
               11 reader is user defined reader #2 (UR2:)
    
             PUNCH field (bits 4,5)

               00 punch is teletype device (TTY:)
               01 punch is high speed punch device (PTP:) 
               10 punch is user defined punch #1 (UP1:)
               11 punch is user defined punch #2 (UP2:)

             LIST field (bits 6,7)

               00 list device is teletype (TTY:)
               01 list device is CRT device (CRT:)
               10 list device is lineprinter device (LPT:)
               11 list device is user defined list device (UL1:)


              Two  of  the  serial  ports on the VT180 can be used for
           serial communication, the READER/PUNCH port,  and  the  UC1
           (user defined console) port.  From the chart above, setting
           the  two  least  significant  bits of the IOBYTE to 01 will
           allow normal console I/O to the  VT100  terminal.   Setting
           the  same two bits to 11 will allow the UC1: port to be the
           system console.

              Working   with   the   READER/PUNCH  port  is  a  little
           different.  This is because the status of the  reader  port
           cannot be obtained directly with reader system calls.  If a
           call to get character from reader is done, the routine will
           hang  there  until a character is available.  This will not
           allow the alternating status checking  required.   However,
           there  is  a  way.  The reader port can be made the console
           port (IOBYTE value xxxxxx10).  Now the status of the reader
           can be obtained without waiting.  The  characters  received
           from  the keyboard are sent to the punch port with a system
           call to punch output.

           2.5.3 Eight Bit Data

                The  Digital  Research  manual for CP/M specifies that
              the hight order bit of a  character  obtained  with  the
              CONIN bios call will be zero.  This is not the case with
              the  VT180.   All  8  bits are significant.  This allows
              binary data to be transmitted and received by the VT180.
              Other systems may vary.

           2.5.4 Function Descriptions

              2.5.4.1 Function C_INIT

                   The c_init function sets up the  intial values for
                 the communications  library.  This function  MUST be
                 executed at the beginning  of any program  that will
                 use  the comm  library.  It initializes  the  iobyte
                 settings, and sets up the default values for all the
                 possible ports.
                   On  entry, it sets all  the ports to their default
                 values.  Since the parity and baud rate on the VT180
                 cannot  be  easily  set,  DEFAULT  is  all  that  is
                 allowed  for these  settings.  The default  port  is
                 the comm port, which  is the normal VT180 comm port.
                   If  an  illegal  port,  baud  rate,  or  parity is
                 requested, the function returns FALSE.

              2.5.4.2 Function C_SET_PORT

                   Two ports are allowed for the VT180.  Valid values
                 for port are 1, 2, and 3,  yielding default  (COMM),
                 COMM, and UC1, respectively.

              2.5.4.3 Function C_SET_BAUD

                   In  this  version of the library, baud rates cannot
                 be  set, and  the function  will return FALSE  if any
                 value other than 1 (default) is requested.

               2.5.4.4 Function C_SET_PARITY

                   In  this  version  of the library, parity cannot be
                   set, and  the  function  will  return FALSE  if any
                   value other than 1 (default) is requested.

               2.5.4.5 Function C_GET_KBD_CHAR

                    This  function uses bios(1) to obtain  keyboard
                    status  and  bios(2)  to  obtain a character.

               2.5.4.6 Function C_GET_COMM_CHAR

                    This  function uses bios(1) to obtain port status
                    and bios(2) to obtain a character.

           2.5.5 Procedures

               2.5.5.1 Procedure C_PUT_SCR_CHAR

                   This procedure uses bios(3) to send a character
                   the screen.

               2.5.5.2 Procedure C_PUT_COMM_CHAR

                   This  function  checks whether the selected port is
                 the reader or the UC1 port and uses bios(5) to  write
                 to the punch port or bios(3) to write to UC1.