NAME
    hd

SYNOPSIS
    hd <options>

DESCRIPTION
    Hd  is  a program for testing hard disks - M10, M20, M26
    with a Morrow  Designs  controller.  All  seeks,  header
    writes, and sector writes are immediately checked. Every
    head  is  read  after  every seek, thus testing the head
    select logic as  well  as  mechanical  repeatability.  A
    recalibrate  operations  is performed after each failing
    seek. The default battery of operations is format, seek,
    header, data, in that order.  The default set of drives is
    only drive A. At the beginning  of  the  seek  and  data
    tests,  the  disk  is first formatted if it is obviously
    not yet formatted.
    The following options are understood:
        A-Z:
                Specify a list of drives to be  tested.  For
                the purpose of 'hd', drives are denoted by a
                single  letter  A  - Z. 'A' means drive 0 on
                the controller at  I/O  location  50  (hex).
                Drives  A-D  are  on the first board, E-H on
                the  second  etc.  Each  specification  must
                contain  a  colon (':'). The case of letters
                is ignored. As many drive specifications  as
                desired  may  appear.  Each  drive specified
                will be tested. The following  are  examples
                of valid drive specifications: 'A:', 'A-D:',
                'AB:'.

        header
                Do  a  header test. The original header data
                is  preserved  (except  possibly  when   the
                program terminates abnormally.)

        format
                Format the disk. The disk is first formatted
                and then all the headers are checked.

        seek
                Do  a seek test. The disk is first formatted
                if need be.

        data
                Test reading and writing  sectors.  The  bad
                sector map is reinitialized at the beginning
                of  each  sector  test.  The  disk  is first
                formatted if need be.

        xN
                Set the repeat count to N. 'N' is a base ten
                number. Normally the  battery  of  tests  is
                performed   only  once  for  each  specified
                drive.









        unix
                Assume a UNIX like sector arrangement.  This
                means that the sectors are numbered starting
                at  zero. Also the bad sector map blocks are
                the last two on the volume. Normally the bad
                sector map is assumed to be on the last  two
                sectors of the first track.

        save
                Save  the data when formatting. Normally all
                the data  is  destroyed  during  formatting.
                Note: this makes the formatting much faster.

        settle N
                Specify  a  non-standard head settling time.
                The  head  settling  delay  is  set   to   N
                milliseconds.  The  defaults are M10 - 33ms;
                M20 - 0; M26 - 20ms.

        skew N
                Set the skew factor to N. The skew factor is
                the number of physical  sectors  to  advance
                between each sequential logical sector.

        start N
                Set  the  starting  cylinder. All operations
                will be restricted to cylinders N and above.

        stop N
                Set the stopping  cylinder.  All  operations
                will be restricted to cylinders N and below.
                Example:
                "hd start 5 stop 5" would test only track 5.
                Note:  cylinders  are  numbered  starting at
                zero.

        quiet
                Be quiet. Nothing is printed. The bad sector
                map is still recorded on the disk.

        verbose
                Causes complete input and output data to  be
                printed  for  each  hard  error on header or
                sector I/O.

        error N
                Set the maximum error count to  N.  If  more
                than this number of a single type accrue the
                drive  is "failed" and the rest of the tests
                are aborted. The program will then  move  on
                to  the  next  drive  (if more than one were
                specified).

        shake
                Use "shake system" protocol.

EXAMPLES
            hd a-d: x3 unix shake








    Would test the first four drives, three times with  unix
    sector arrangement using 'shake system' I/O protocol.